## Slide 1: ANL APS-Upgrade Short Pulse X-ray (SPX) LLRF System
ANL*: Tim Berenc, Hengjie Ma, Ned Arnold, Frank Lenkszus
LBNL**: Larry Doolittle, Gang Huang, John Byrd
LLRF 2011 Workshop
Oct. 20, 2011
*Work at Argonne supported by U.S. Department of Energy, Office of Science, Office of Basic Energy Sciences, under Contract No. DE-AC02-06CH11357.
** Work supported by U.S. Department of Energy, Office of Science, Office of Basic Energy Sciences, under Contract No. DE-AC02-06CH11354.

## Slide 2
Advanced Photon Source (APS) @ Argonne National Laboratory
Planned
SPX Location

## Slide 3: APS-U SPX System – Zholents’ Transverse RF Chirp Concept1
Goal: provide ~2 psec (presently 50-100 psec) X-ray pulses at 6.5 MHz rep. rate for time-resolved studies
Ideally, second cavity exactly cancels effect of first cavity
1 A. Zholents et al., NIM A 425, 385 (1999)
Correlation between vertical distribution of x-rays and time-distribution of electrons that generated them. Pulse can be sliced or compressed with an asymmetric cut crystal.
RF at ~2815 MHz
(8th harmonic of Storage Ring RF)

## Slide 4: Performance Requirements
Common
Mode
Differential
Mode
Residual kick
Residual tilt

## Slide 5
SPX System - Conceptual Design Strategy
Orbit Feedback System provides long-term stability … < 100 Hz
LLRF System on its own > 10 Hz [10 Hz – 100 Hz overlap with Orbit Feedback]
Beam Arrival Time feedback to main Storage Ring RF to address common mode phase
LBNL-based phase stable references2 to synchronize RF (x-ray pulse) and user lasers
Single Klystron per cavity
LLRF drift compensation via CW calibration tone
2 J. Byrd et al., Optics Letters Vol. 34, No. 20 (2009)

## Slide 6
R&D System Proof of Principle (1 Sector, 2 cavities)
Cavities counter-phased (180deg) to demonstrate tolerance requirements
Cavities run in-phase to create a chirped beam around entire ring to have a look at short pulse x-rays

## Slide 7
RF Strategy #1 – Regulate to Designated Phase Reference
  Don’t let the LO assume the role of the phase reference
  Phase is a Differential Measurement
  Mixers preserve phase information, x’s and ÷’s preserve timing
  In theory, common mode LO and clock noise cancels

## Slide 8
LLRF4 Board – Input Differential Phase Noise
CLK
IF

## Slide 9
RF Strategy #2 - CW Drift Compensation3
0.09
~ 35 dB
~ 0.023 rms
~ 0.118 rms
5
3 “Signal Processing for High Precision Phase Measurements”, G. Huang, L. Doolittle, J. Staples, R. Wilcox, J. Byrd , Proceedings of BIW10

## Slide 10
CW Drift Compensation – Intermodulation Distortion
Double Sideband Cal-Tone
Single Sideband Cal-Tone

## Slide 11
Freq. Generation Chassis
LLRF Receiver #1
Cavity Emulators
#1 and #2
Residual
Phase Noise Test Set
(measure noise between cavity emulators)
LLRF Receiver #2
LLRF Benchtop Demonstration:
Differential Phase Noise between 2 LLRF controlled cavity emulators
Price paid to suppress low freq. noise
(i.e., beam loading & microphonics)
LLRF System contribution
~ 20 fsec rms [0.1 Hz – 1MHz]

## Slide 12
Freq. Generation Chassis
LLRF Receiver #1
Cavity Emulators
#1 and #2
Residual
Phase Noise Test Set
(replaced with E5052B for AM)
LLRF Receiver #2
LLRF Benchtop Demonstration:
Amplitude Noise

## Slide 13
Some Lessons Learned about Deflecting Cavities

## Slide 14
Deflecting Cavity Beam Loading
function of both: Offset and Tilt

## Slide 15
CW small signal model will help track system noise & error budgets
Deflecting Cavity Dynamic Model
LLRF 2011 Workshop
Caution:
Pedersen/Boussard transfer functions are normalized for amp/phase. Beam loading factor, Y, can be negative for deflecting cavities. Amp/Phase control can be lost when beam offset drives the cavities to full field (there is no drive carrier). This isn’t true for I/Q control.
Proper normalization for I/Q transfer functions is to rotate into the cavity voltage frame, but not to normalize with respect to the various carrier terms.

## Slide 16
Example of Differential Phase Noise induced by Common Beam Jitter
Sector A
Sector B
Residual Kick
Uncontrolled Beam Arrival Time Error
Deflecting Cavity – Motivation for Electrical Alignment
LLRF 2011 Workshop
QL = 2e6
200mA
when
Cavity-to-cavity vertical alignment errors cause differential beam-loading which leads to differential phase noise.

## Slide 17
Feed Forward OFF
Feed Forward ON
AM & PM suppression
360Hz Feed-Forward correction of Klystron High-Voltage Power Supply (HVPS) induced noise
via dispersion, beam phase noise shows up as horizontal beam motion
Horizontal BPM Data
= Motivation to Reduce Storage Ring Beam Jitter
Deflecting Cavity – Motivation for Electrical Alignment

## Slide 18: Summary
Digital LLRF systems are capable of femto-second level synchronization [0.1 Hz – 1MHz] with proper attention to common source distribution
Modern optical fiber link systems promise long-term femto-second level synchronization between RF systems, diagnostics, and user lasers
Deflecting cavities present new intellectually stimulating & challenging system design