## Slide 1: A TPC for the Linear Collider
ECFA Detector Panel Review – 4 Nov 2013
Introduction
Jan Timmermans (NIKHEF)

## Slide 2: LCTPC Collaboration (1)
27 signatories; 5 pending; 13 groups ‘observer’ status

## Slide 3: LCTPC Collaboration (2)
TPC as central tracker already in TESLA LC (2001)
October 2001: TPC R&D proposal to DESY PRC
  ~bi-yearly reviews by PRC; last one Oct 2010
2007/08: formal start global LCTPC collaboration
  Memorandum of Agreement (MOA); defining Work Packages
  Yearly Addendum, updating (general) information
  Work Package (#5) overseeing the R&D after the ILD DBD
Organisation:
  Collaboration Board, one member/institute; chair Leif Jonssen
  3 Regional Coordinators (Americas, Asia, Europe): one is chosen as Spokesperson, currently Jochen Kaminski
  Speakersbureau, Editorial Board
Cooperation with other TPC & MPGD groups: T2K, RD51, …

## Slide 4: LCTPC Collaboration (3)
Workpackage(5):
  Advanced endcap: mechanics/alignment
  Advanced endcap: electronics development
  Advanced endcap: cooling
  Advanced endcap: power pulsing
  Gating device
  Fieldcage
  ILD TPC integration/machine-detector interface
  LCTPC software/correction methods

## Slide 5: LCTPC and Linear Collider
TPC as central tracker in ILD concept detector for ILC
High occupancy in inner part of a TPC at CLIC @ 3 TeV; would need very small pads (1 x 1 mm2) or pixelised readout.
ILC possibly (hopefully likely) to be built in Japan. Preferred site has recently been selected.
First stage of ILC @ 250 GeV (Higgs “factory”)
2nd stage extension to 500 GeV (top, Higgs self coupling and other precision/new physics studies)
Possible final upgrade to 1 TeV
Both ILC and CLIC incorporated in new global Linear Collider Collaboration

## Slide 6: Extra challenges at CLIC
Beam structure: 50 bunch trains per second; length of train is ~180 ns (ILC: 5 Hz, 1 ms train length)
Separation between bunches in train: 0.5 ns. Time stamping becomes issue (but still seems possible). At ILC time between bunches ~300 ns
At high energy occupancy too high in inner part of TPC, due to:
  High cross-section of hadronic 2-photon process
  High pair background due to beam strahlung
  Would need pixelised readout
High occupancy also implies high primary ion density

## Slide 7: In relation to ILD detector
Based particle flow concept; topological reconstruction of events:
  Efficient separation of charged and neutral particles
  High granularity/high spatial resolution subdetectors
  High redundancy and efficiency
  Strong magnetic field 3.5 T
Efficient reconstruction of
secondary vertices
Very good momentum
resolution charged particles
Very good jet energy resolution

## Slide 8: TPC performance/design parms
Continuous tracking is key to reconstruction of non-pointing tracks
(signature in several new physics scenarios

## Slide 10: Example: Higgs recoil measurement
e+e- ➝ HZ ➝ Xμ+μ-
Recoil mass opposite the μ-pair;
Requires excellent momentum resolution

## Slide 11: Another example in SUSY
Minimum and maximum energies provide accurate determination of the masses of primary slepton and secondary neutralino

## Slide 12: TPC in ILD
Current design: 240 modules per endplate,
size approx. 17 x 21 cm2

## Slide 13: TPC with MPGD
MicroMegas
GEM
Two gas amplifications:
Analog TPC
with standard pad readout
(need signal broadening)
Digital TPC
with CMOS pixel readout

## Slide 14: Drift gas choice
T2K gas: Ar/CF4/iC4H10 in ratio 95/3/2 %
Fast gas, with large value ωτ
→ Drift is along B-fieldline

## Slide 15
4 Tesla
Transv. Diff.
Long. Diff.
Drift vel.
3 Tesla
1 Tesla
0 Tesla

## Slide 16: LCTPC testbeam infrastructure
DESY II testbeam area T24/1
PCMAG ~1T solenoid (KEK)
Fieldcage (DESY/EUDET)
Endplate(s) (Cornell, NSF)
3D lifting stage (DESY, EUDET, AIDA)
Upgrade PCMAG (KEK, DESY, AIDA)
HV, gas, slow control (DESY, EUDET)
Beam/cosmic trigger (NIKHEF, Saclay)
Laser calibration (Victoria, DESY)
DAQ (Lund, Brussels, Saclay, Medipix Coll.)
CO2 cooling system (KEK, NIKHEF)
Laser beams (under development) (BNL)
Software (MANY groups)

## Slide 17: Test beam area
Usually e- beam 1-5 GeV
PCMAG ~1T solenoid. Initially manual filling of liq.He from dewar. From 6/2012 closed system with 2 cryo coolers and 2 He gas compressors
3D lifting stage

## Slide 18: TPC in PCMAG
Lightweight fieldcage, cathode, endplate anode structure:
  7 modules ~17x22 cm2
Diameter 72 cm, maximum drift distance ~57 cm
Dummy modules + endplate guard structure
(External) Si layers in between TPC and inner wall of PCMAG under consideration; 4 cm space radially

## Slide 19: 2PCO2 cooling system in preparation
Purchased by KEK
Tuning tests at NIKHEF almost
finished
Module test foreseen at NIKHEF
in December
Transport to DESY early 2014

## Slide 21: Next talks
Technologies – Jochen Kaminski
Ion feed back – Philippe Gros
Electronics – Paul Colas
Mechanics – Jochen Kaminski
Software/simulations – Astrid Muennich
Outlook – Takeshi Matsuda

## Slide 22: Backup slides