## Slide 1
Presented by: Christopher Gerth
WP-18 Special Diagnostics Installation Status
Notes: How to edit the title slide
Fill in the text written in brown

## Slide 2: Scope of WP-18 Devices
  Distribution of fs-stable optical synchronization signals over entire facility (~ 3.5 km)
  Monitoring of long. properties: beam energy, bunch profile/length and bunch arrival time.
20pC | 4.53ps | 1.46ps | 185fs | 5.23fs
100pC | 4.80ps | 1.55ps | 197fs | 11.6fs
250pC | 5.27ps | 1.70ps | 223fs | 25.4fs
500pC | 6.00ps | 1.96ps | 259fs | 43.0fs
1000pC | 6.77ps | 2.23ps | 303fs | 84.0fs
Energy | 130MeV | 600MeV | 2.5GeV | 17.5GeV
Igor Zagorodnov, 2011
Energy change (x 100) after accelerating sections: I0, L1, L2, L3
Bunch length change (x 1000) after bunch compressors: BC0, BC1, BC2
Bunch arrival time may change after dispersive sections: BC0, BC1, BC2
  => Longitudinale Diagnostik nach Beschleunigung und Bunch Kompression

## Slide 3
Rückblick: Longitudinale Diagnostik bei FLASH / XFEL
Entwicklung der longitudinalen Diagnostik für FLASH fand bei FLA statt (P. Schmüser, B. Schmidt)
Installation, Betrieb und Wartung beim XFEL => Bedarf an technischer Infrastruktur => Eingliederung der long. Diagnostik in den M-Bereich
Anfang 2010: WP-18 wurde in MSK integriert: M. Felber, Ch. Gerth, H. Schlarb (GL MSK) von MPY
MSK schlecht aufgestellt im Bereich Mechanik: Verstärkung durch Mechaniker Martin Schäfer und M-Verbundwerkstatt (es gibt aber keinen Mechanik-Ingenieur bei MSK)
MSK verfügte nur über ein Digital/Analog Labor: => Labor für Optikaufbauten eingerichtet (Büro-Container 28f) => Labor für Vormontage in XTIN UG1 R017 vorgesehen
Entwicklung für das optische Synchronisationssystem finden im Laser-Labor von FLA statt => eigenes Laserlabor wird benötigt
Weiteres technisches und wissenschaftliches Personal wurde eingestellt => ca. 8 FTE
FELs: Erzeugung ultra-kurzer X-Ray Pulse FEL einige 10 fs Bunchlänge ↔ Speicherring einige 10 ps Entwicklung von Messtechniken mit fs-Zeitauflösung

## Slide 4: Overview on WP-18 Devices
Laser-based
Synchronization
Reference
Distribution XTIN UG5 R25
(MLO, FSD, Faser-Links)
REFM
LLRF
Synchronization
L2L
Laser
Synchronization
BAM
Bunch Arrival
Monitor
SRM
Synchrotron
Radiation
Monitors
EBPM
Energy BPM
Bunch arrival
Beam energy
Beam Energy
Energy profile
Beam energy
(Bunch arrival)
Beam energy
Bunch arrival
EOD
EO
Diagnostics
BCM
Bunch
Compression
Monitor
TDS(1)
Transverse
Deflecting
Structure
Bunch profile
Compression
Bunch profile
Slice emittance
Phase space
Bunch length/profile
1)
High-Power RF system and TDS are part of contract between European XFEL GmbH and Inst. for Nuclear Research (INR).
High-Power RF system and TDS are made by INR, Moscow.
Vacuum parts for BAM and EBPM manufactured by WP-17
Yellow: involves lasers (=> laser lab space required => XTIN UG1 in Arbeit …)
CRD
THz
Spectrometer
Bunch profile
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 5: Overview on WP-18 Devices (2)
5
 | INJ | BC0 | BC1 | BC2 | TL | UND | Sum
BAM | 1 | - | 2 | 2 | 2 | - | 7
EOD | 1 | 1 | 1 | - | - | - | 3
BCM | - | 1 | 1 | 2 | - | - | 4
CRD | - | - | - | - | 1 | - | 1
SRM | - | - | 1 | 1 | - | - | 2
TDS | 1 | - | 1 | 1 | - | - | 3
EBPM | - | 1 | 1 | 1 | - | - | 3
Sum | 3 | 3 | 7 | 7 | 3 | - | 23
TL: Supports for CRD and BAM need to be designed
7 Completely different types of devices (≈ Einzelanfertigung)
All WP18 devices in XTL and INJ
Most in B1 and B2 section
BC1 Girder Belegung
G2 : EOD, BCM, BAM
G3 : EOD, BCM, BAM
G4 : TDS
BC2 Girder Belegung
G2 : BCM, BAM
G3 : BCM, BAM
G4 : EOD
G5 : TDS
Notes: 5
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 6: Generic Layout
6
Zuerst Installation der Vakuumbauteile => WP-19 / MVS
  Bedarf teilweise der Hilfe von Experten im Reinraum
  Beamline Hardware: EOD, BCM, CRD, SRM => Installation am Girder in XTL
  SRM: Nach Einbau der Bunchkompressor Schikanen
Rack equipment
  Es gibt kein Installationsteam: Organisation der Installation durch Experten mit Unterstützung vom WP-18 Team
  Rasante Entwicklung bei Optiken, THz Detektoren 1D Detektoren, Kameras, MTCA, … => richtigen Zeitpunkt treffen um Designs ein zu frieren: nit zu früh / nicht zu spät
Vacuum
setup
Beamline Hardware: Detektion und Signalwandlung
19’’ Module:
Conversion for signal detection
MTCA:
Signal detection, computation, …
LLRF
19’’ Modules:
Operation of Hardware
Rack
e-beam
Notes: 6
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 7
WP-18 MTCA Crates
About 22 crates in 12 different configuration (12 in XTL)
About 200 MTCA boards of 20 different types
Pre-commissioning of crates before installation at final location (on demand and availability)

## Slide 8: WP-18 Rack/Crate/Device test and installation
8
Rack installations:
  Every rack configuration different (22 stations, shared, room reserved => TC rack inventory)
  No pre-commissioning: Installation of MTCA and 19’’ modules at final location
  Installation and cabling by experts plus others (depends on rack, depends on others)
MTCA Crate installation
  Almost every crate configuration different (about 22 crates)
  Integration tests: should be close to MTCA device storage and testers (tbd.)
  Crate storage unclear (where to store 22 crates)
MTCA Devices
  Device labeling and documentation in KDS (Matthias Felber, Maciek Kudla)
  Device testing: as for LLRF boards, some boards during pre-commissioning
Too many side constraints for each rack => no standard installation procedure
Needs to be organized within WP-18 Team …
Notes: 8
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 9
Overall Schedule:
  Injector Commissioning: BAM, EOD, TDS, 4 Links (complete systems)
  Handover of all vacuum parts to WP-19 by end of 2014
  Installation of all additional equipment (20 systems and 20 Links) until 06/16
Additional Equipment Installation schedule
  No rigid schedule as for instance like LLRF (A01 – A26)
  Needs to be planned by device responsible persons and coordinated in WP-18 team
Coordination will depend on
  Availability of WP-18 hardware
  Availability of sub-system experts for device testing
  Availability of support for installation
  Availability of support for firmware / server installation
  Overall schedule (vacuum installation, infrastructure and rack installation, …)
  => Needs to be worked out
All hardware developments to be finished by end 2014
All hardware available beginning of 2015
Establish installation rules and routines …
Installation schedule

## Slide 10: Overview on WP-18 Team
Laser-based
Synchronization
Reference
Distribution
(MLO, FSD, LSU)
REFM
LLRF
Synchronization
L2L
Laser
Synchronization
BAM
Bunch Arrival
Monitor
SRM
Synchrotron
Radiation
Monitors
EBPM
Energy BPM
M. Czwalinna
C Gerth
U. Mavric
Beam energy
Bunch arrival
EOD
EO
Diagnostics
BCM
Bunch
Compression
Monitor
TDS(1)
Transverse
Deflecting
Structure
B. Steffen
P. Peier
INR (MIN)
LLRF (MSK):
M . Hoffmann
Water: MKK
Vacuum: WP-19
Coord: WPL
Admin: WPL
Bunch length/profile
Red: Post-Docs auf Zeitverträgen! … Betrieb und Wartung?
MTCA Board Entwicklung: R. Wedel und polnische Kollaborationen
Software: 3 Doktoranden + 1 PostDoc (poln. Koll.) + 1/2 HVF
MTCA Test und Installation: U. Mavric, M. Felber
1 Mechaniker (2 Jahre) in M-Verbund, 1 Elektriker (1,5 Jahre)
Zeit zwischen Design und Installation muss kurz sein, da FTEs limitiert! Schwerpunkte setzen.
Generell: WP-02 LLRF Entwicklungen übernehmen wo möglich, um Entwicklungsaufwand zu minimieren
CRD
THz
Spectrometer
P. Peier
J. Müller (FLA)
T. Lamb
PhD thesis
C. Sydlo, F. Zummack
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 11
Planning: M.K. Czwalinna, C. Gerth, C. Schmidt
WP-18 Diagnostics and Beam-Based Feedback
Combined Signals with EBPM are sent to upstream LLRF station
BAM, EOD and BCM are combined in 1 MTCA crate
Planung abgeschlossen
Spezielle polarisationserhaltene LWL fuer BAM
Roehrchen fuer LWL in XTL sind verlegt

## Slide 12
Thank you for
your attention