## Slide 1: Fermilab Test Beam Facility
Aria Soha
June 30, 2014
DESY Test Beam Workshop

## Slide 2: Location
Meson Detector Building – West
Fermi National Accelerator Laboratory
Notes: Fermilab is located in Northern Illinois, USA, outside Chicago.

## Slide 3: Layout and Rooms
Beam Areas
Work Areas
Control Rooms
Notes: 2 Beamlines
MTest for short-term (weeks) experiments
MCenter for make-up and long-term (months) experiments

## Slide 4: MTest Beam Areas
6 MT6 Experiment Areas
1A
1B
2A
2B
2C
2D
3 Climate Controlled areas
Section 2 Newly Insulated!
Notes: New! MT6.2 has been insulated to control temperature within 5 degrees.
Additional Climate controlled areas allow to maintain temperatures within 2 degrees

## Slide 5: MTest Beam Areas
6 MT6 Experiment Areas
1A
1B
2A
2B
2C
2D
2 areas with Crane access
(30 Tons)

## Slide 6: High Rate Tracking Area
Located in MTest beamline upstream of pinhole collimator (MT3 Alcove)
2.5 GHz/cm2 Rates for protons
Patch panels for signal, HV, and network link the enclosure alcove area with the MS3 service Building
Acnet controlled table
Pions also available
Notes: Detectors in this area must have Interaction Lengths of less than 3%

## Slide 7: MCenter Beamline
Beamline Now Operational!
  Similar beam to MTest
  Long dwell time experiments
  Overflow/make-up experiments
Supports Liquid Argon (Under development)
Tertiary beamline Option
  Protons & Pions
  200 MeV – 1 GeV range
Large Dipole Magnets
  ~ 1 Tesla
  1 meter bore
Notes: 2 Areas under development

## Slide 8: Facility Equipment
Patch Panels (Newly Upgraded!)
  in enclosures and control rooms
  Signal (lemo & BNC), SHV, Network (CAT5), Power, and other assorted cables are available to users in various lengths and quantities.
  Including network controlled power strips
Lasers for Alignment (Newly Upgraded!)
Helium Tubes
Phone System (Newly Upgraded!)
Web-based Cameras (Now in MT6.1A & 1B!) (All of MT6.2)
Notes: New Gigabit Ethernet throughout facility, including upgraded wireless
Web-based Cameras have 26x Optical zoom

## Slide 9: Motion Tables
ACNET Controlled to minimize accesses
1mm precision in X/Y
Rotation option now available!
Smaller stages with centimeters of travel available for small loads
Notes: http://www-ppd.fnal.gov/FTBF/facility/tables.html

## Slide 10: Gas
Gas Distribution system throughout facility
MT6.2 and MC7 have flammable capability
Some gasses provided
Notes: http://www-ppd.fnal.gov/FTBF/facility/gas.html

## Slide 11: Instrumentation
can be moved anywhere.
MS4
MT6.2
MT6.1
M05 &
MTest Control Room
Alcove Control Room
Absorber
Downstream Cerenkov
Inner/Outer
Electronics Room
Climate Controlled Area
SWIC (AD)
MWPC (Fenker Chamber)
Si strip
Telescope
(CAPTAN)
Lb-Glass
Calorimeter
Scintillator Counters
Time Of Flight
Lead-Glass
Calorimeter
Upstrm Ckov
Remotely Controlled Table
Notes: Scintillator Counters 2 & 3 now retractable
New Si Strip Telescope
Upgraded MWPC tracking – see poster 143
TOF System to be upgraded in the future
http://www-ppd.fnal.gov/FTBF/instrumentation/index.html

## Slide 12: Beam Delivery
Beam Available 24 hrs /day
6 sec event (4.2 sec spill) every 60 seconds
Control room manned during beam hours
Booster captures protons into 84 bunches (1 batch) and accelerates them to 8GeV
Bunches are 19nsec long: 1 RF Bucket (53 MHz)
Booster batch = 1.6 microsecond in length
Up to 6 batches go into Main Injector
Main Injector = 11.2 microsecond
Beam is ramped from 8 to 120 Gev and held at the flattop value
Fraction of the beam resonantly extracted each rotation over 4.2 sec to Switchyard
In Switchyard electrostatic Septa split beam twice. First split beam to NM line (Sea Quest) and M line, the second splits the beam between MTest and MCenter.
Neutrino Line
MTest
MCenter
Linac
Booster
8GeV Line
Main Injector
P1 Line
P2 Line
P3 Line
SY120
If beam were smoothly extracted, 100 kHz or less would imply 1 particle per MI rotation would occur.
Beam extraction is not smooth resulting in up to 35% double occupancy per MI rotation (11μSec)
Notes: All of these clock signals are available to users in NIM and TTL

## Slide 13: Particles & Energies
120 Gev Proton Mode
  Maximum intensity: 5E5 p/spill
High Energy Pion Mode
  + 60
  + 50
  + 40
Muon Mode:
  Every LE or HE Pion Mode with additional absorbers in MT6-1.
Low Energy Pion Mode
  +/- 32
  +/- 30
  +/- 25
  +/- 20
  +/- 16
  +/- 15
  +/- 12
  +/- 10
  +/- 8
  +/- 6
  +/- 5
  +/- 4
  +/- 3.5
  +/- 3
  +/- 2.5
  +/- 2
  +/- 1.5
  +/- 1
Mostly Electrons/
Positrons
P
π
e
μ
Some kaons
k
New ‘Energy Script’ will be able to select particles at any discrete energy.

## Slide 14: FTBF Summary
Fermilab Test Beam Facility is an High Energy Beam facility for world-wide Detector R&D
Extensive facility infrastructure & instrumentation
Flexible beam delivery
  Protons, pions, muons, electrons, kaons
  200 MeV – 120 GeV
  1 – 300 kHz intensities
Beam time available!
  http://www-ppd.fnal.gov/FTBF
  Become a User

## Slide 15: Additional Slides

## Slide 16: Tertiary Beam Details
Rates: ~200 particles / 4 sec spill (~50 Hz)
60% pions, 40% protons,
very few electrons, kaons, and deuterons
Momentum Resolution: dp = 3%
  multiple scattering limited for this momentum range
design momentum is 200MeV minimum

## Slide 17: Slow Extraction to MTest - General Beam Delivery
Beam is produced from AD’s Proton source which includes three machines. The Source, Linac and the Booster Ring. Depending on the request intensity Booster over laps beam from Linac. Each revolution in Booster is called a Turn.
Booster then delivers 8 GeV proton beam to Main Injector in bunches at a maximum of ~84 bunches at a time. This term is called a Batch.
Previous runs were partial batching*
Main Injector
Source Linac & Booster

## Slide 18: Slow Extraction to MTest - General Beam Delivery
Even though physically Main Injector can hold 7 Batches, the maximum number is 6. This is because of the abort gap needed for operations.
Main Injector
Source Linac & Booster

## Slide 19: Slow Extraction to MTest - General Beam Delivery
Beam is ramped from 8 to 120 Gev and held at the flattop value and resonantly extracted 4 seconds.
Main Injector
Source Linac & Booster

## Slide 20: Slow Extraction to MTest - General Beam Delivery
Field Free Region
2 Electrostatic Septa
Field Region
Not to scale*

## Slide 21: Slow Extraction to MTest - General Beam Delivery
Beam is extracted from the MI52 area transported
through the P1 P2 and P3 (Main Ring remnant)
Beamlines to Switchyard. In Switchyard electrostatic
Septa split beam twice. First split beam to Neutrino Muon and Meson, the second splits the Meson beam between MTest and MCenter.
P3
P1
P2
Main Injector
MCenter
Neutrino Muon
SeaQuest
MTest
Source Linac & Booster

## Slide 22: Slow Extraction to MTest – Running Modes
Key Requirements
  120 Gev Proton Mode
    M01 target in place for attenuation
    MT3 Pinhole Collimator for attenuation
    Quadrupole magnets off for larger spot size
  Low Energy Pion Mode
    MT4 target in place for production
    MT3 Pinhole Collimator out for transmission
    Quadrupole magnets specific settings
  High Energy Pion Mode
    M01 target in place for production
    MT3 Pinhole Collimator out for transmission
    Quadrupole magnets specific settings

## Slide 23: The Fermilab Test Beam Facility
World Class Facility
The only U.S. HEP Test Beam
Detector R&D focus
In 2012:
  11 experiments
  229 collaborators
  64 institutions
  14 countries
Chart: Most Recent 5 Years
| FY 2008 | FY 2009 | FY 2010 | FY 2011 | FY 2012
Experiments | 7 | 6 | 11 | 13 | 11
Collaborators* | 13.1 | 13 | 15.7 | 22.3 | 22.9
Institutions* | 9.4 | 8.6 | 9.6 | 12 | 12.8
Countries | 14 | 15 | 12 | 14 | 14
*Number of Collaborators has been scaled to fit on plot
*Number of Institutuions has been scaled to fit on plot.
FY12 only consisted of 7 months of Beam

## Slide 24: Particle Composition of Beam
Beam Energy (GeV) | Rate at Entrance to Facility (per spill) | Rate at Exit of Facility (per spill) | % Pions, Muons | % Electrons
16 | 132,000 | 95,000 | 87% | 13%
8 | 89,000 | 65,000 | 55% | 45%
4 | 56,000 | 31,000 | 31% | 67%
2 | 68,000 | 28,000 | <30% | >70%
1 | 69,000 | 21,000 | <30% | >70%
If beam were smoothly extracted, 100 kHz or less would imply 1 particle per MI rotation would occur.
Beam extraction is not smooth resulting in up to 35% double occupancy per MI rotation
120 Gev Protons
2 - 66 GeV Pions
0.5 – 32 GeV Electrons
Broadband Muons

## Slide 25: Tertiary Beam Details
Rates: ~200 particles / 4 sec spill (~50 Hz)
60% pions, 40% protons,
very few electrons, kaons, and deuterons
Momentum Resolution: dp = 3%
  multiple scattering limited for this momentum range
design momentum is 200MeV minimum

## Slide 26: Weekly Usage
FY2012 only consisted of 7 months of beam
Facility use includes Beam studies, and educational support such as EDIT 2012.
Chart: Weeks
| FY05 | FY06 | FY07 | FY08 | FY09 | FY10 | FY11 | FY12
Exp Use 4 Data (%) | 0.25581 | 0.27143 | 0.15909 | 0.1875 | 0.16667 | 0.44681 | 0.45408 | 0.6
Expt Data Taking | 22 | 19 | 14 | 18 | 13 | 34.5 | 40.5 | 27
Double Occupancy | 0 | 7.5 | 4 | 9
Facility Use (%) | 0.65116 | 0.55714 | 0.43182 | 0.45833 | 0.4359 | 0.85106 | 0.90816 | 0.96667

## Slide 27: Meson Area Beamlines