## Slide 1
TEWS TECHNOLOGIES GmbH
TAMC532
32 x
12 Bit ADC @ 75Msps

## Slide 2: Company Background
TEWS TECHNOLOGIES is a
leading solutions provider of
embedded I/O and CPU products
based on open architecture standards
(i.e. IndustryPack, PMC, XMC, CompactPCI, standard PCI, PCIe, VME, AMC, and FMC).
Our modular hardware designs are coupled with extensive software drivers and support for major real-time and server operating systems (i.e. VxWorks, Windows, Linux, Integrity, QNX)

## Slide 3: Product Photo
TAMC532
TAMC532-TM
(Developed within Helmholtz Validation Fund)

## Slide 4: TAMC532 Block Diagram

## Slide 5: FPGA
Kintex 7
  8 Multi-Gigabit Transceiver
    6.6Gb/s (optional up to 12.5Gb/s)
  PCIe Gen 2 Interface
    Endpoint or Root Port
  70k (optional up to 410k Logic Cells)
Redundant Configuration Flash
  2 x 128MBit SPI-Flash
  Field Update via MMC
  User Access

## Slide 6: FPGA Fabric Interconnects
AMC Port 0
  (e.g. Gigabit Ethernet)
AMC Port [7:4]
  (e.g. x4 PCI-Express Gen 2)
AMC Port 12
SFP+ Cage in AMC Bezel
µRTM or 2nd SFP+ Cage (software controlled)

## Slide 7: DDR3 Memory
Two independent banks
  allow double buffering or doubling the data rate
32 Bit data bus width / bank (optional 64 Bit)
800Mb/s – 1600Mb/s line rate
256MByte – 2GByte / bank

## Slide 8: 4 x Octal ADC
Resolution:
  12 or 14 Bit (assembly option)
max. Sample Rate
  75 Msps @ 12 Bit
  50 Msps @ 14 bit
Analog Inputs:
  DC-coupled with on-board ADC-driver
  Input voltage Range according to Class A2.1
    ±1V differential @ 0V common-mode voltage
Zone 3 pin assignment
  According to Zone 3 Recommendation Class A2.1

## Slide 9: ADC Clocking --- Block Diagram

## Slide 10: ADC Clocking --- Facts
Clock Inputs:
  TCLKA + B
  µRTM CLK0
  On-Board generated Clock
Input frequency range:
  10kHz – 100MHz
Clock Up- and Downscaling
ADC Clock Phase Shift
  522 steps of ½ PLL freq. (app. 200ps / step)
ADC Clock Delay
  up to 475ps (25ps steps)
Zero-Delay operation
Bypass-Mode
Clock Outputs:
  TCLKB
  AMC_TCLK
  AMC_CLK0

## Slide 11: Trigger
8 Trigger from AMC-Backplane
  AMC Port [20:17] via MLVDS-Transceivers
    each Trigger can be Input or Output
    additional NAND connection of Tx[19] and Rx[20] to Zone 3 OUT0 and OUT1
Up to 6 Trigger from RTM
  Zone 3 D[8:3] have direct connection to FPGA
  2.5V IO-Voltage

## Slide 12: TAMC532-TM Block Diagram

## Slide 13: Inputs
32 x Analog Input
  RJ45 Input Connectors
    cheap cables
    easy cable field tailoring
  Differential
  up to ±1V differential input voltage
  up to ±3V common mode voltage
1 x Clock + 1 x Trigger Input
  MMCX Connectors
  single-ended

## Slide 14: Filter Block (32x)
  Gain selection
    1, 2, 5 or 10
  Adjustable Pole-Zero Cancellation
  Gaussian Shaping Amplifier with selectable shaping time
    10µs, 1µs, 100ns
  Adjustable Baseline-Shift
  Zone 3 pin assignment according to Class A2.1

## Slide 15: Clock / Trigger + Control
  single ended clock input
    single-ended to differential conversion
    connected to Zone 3 RTM_CLK0±
  single ended trigger input
    single-ended to differential conversion
    connected to Zone 3 D[8]±
  digital Control from the AMC
    Gain, pole-zero cancellation, Shaper time and baseline shift are all controlled via one I2C interface
    IO-Voltage selectable as 1.5V, 1.8V, 2.5V or 3.3V

## Slide 16: Management
  Zone 3 pin assignment according to Class A2.1
  µRTM Management according to Class A2.1
  Optional management implementation via microcontroller
    allows adaption to nearly any MMC
    IPMI-controlled D[8:3] IO-Voltage possible

## Slide 17: TEWS TECHNOLOGIES GmbH
Am Bahnhof 7
25469 Halstenbek / Germany
Phone: +49-4101-4058-0
Fax: +49-4101-4058-19
E-mail: info@tews.com
http: www.tews.com