## Slide 1: DLCL Energy – Current Status
LSDMA All Hands Meeting October 2014

## Slide 2: Hybrid Energy Grid Management (HEGRID)
Main goal:
  Making multi-commodity energy management possible
  Heat
  Gas
  Electricity
  Other fuels (e.g. Power-to-gas)
Prototype implementation: µCHP with additional electrical heating
Source: www.senertec.de

## Slide 3: HEGRID: Challenges
Data from different sources:
  Appliances
  Smart meters
  µCHPs
  Economic data
Different stakeholders:
  Consumers
  Gas/electricity retailers
  Distribution grid operators
  Balance responsible party
Combination of
Data life cycle analysis
European energy market role model

## Slide 4: HEGRID: Results
Primary data 1. µCHP equipment data 2. Metering data (electricity) 3. Metering data (gas) 4. User preferences Derived data 5. Control signals/incentives
  1. µCHP  EMS 2. Meter  EMS 3. Meter  EMS 4. Local UI  EMS 5. BRP  EMS
(Local) EMS database
Aggregation Analysis Optimization
R: Aggr. metering data DSO: Aggr. metering data R: Energy flexibility profiles (electricity only)
Deletion of data which is no longer necessary
Acquisition
Transmission (from / to)
Storage
Analysis
Distribution (to)
Deletion
Derived data from Cs 1. Aggregated metering data
1. C‘s meter  Metering data management system
(Local) Metering database
Data validation Billing Forecasting
R: Aggr. metering data R: Grid usage invoice
Deletion of data which is no longer necessary
Derived data from DSO/Cs 1. Aggregated metering data 2. Flexibility profiles (electricity only) 3. Grid usage invoices Primary data 4. Contract data
  1. DSO  ERP 2. C  ERP 3. DSO  ERP 4. Back Office  ERP
ERP system
Data validation Billing Forecasting
  BRP: Aggr. metering data BRP: Flexibility profiles BRP: Contract info Customer: Invoice
Deletion of data which is no longer necessary
Derived data from R 1. Aggregated metering data (electricity) 2. Flexibility profiles (electricity)
1. R  Control System 2. R  Control System
Control system
  Forecasting Calculation of control signals/incentives
C: Control signals/Incentives (electricity)
Deletion of data which is no longer necessary
Balance Responsible Party (BRP)
electricity only
Retailer (R)
electricity/gas
Distribution System Operator (DSO)
electricity/gas
Customer (C)
electricity/gas
Rigoll, Gitte, Schmeck:
“Data Life Cycles in Future Residential Multi-Commodity Energy Management Systems”,
IEEE PES Great Lakes Symposium 2014 (accepted)

## Slide 5: Data Custodian Service
Energy data is personal data
Standard anonymization and pseudonymization not sufficient
Basic ideas:
  Allow for different views on data (spatial/temporal resolution, noise)
  Reveal only the lowest quality possible
  User decides which party gets to see which data in which quality

## Slide 6: Data Custodian Service
Concept published, basic prototype
Rigoll, Schmeck:
“Outline for an Energy Data Management System in Accordance with Data Protection and Privacy”,
VDE Kongress 2014 (accepted)
Rigoll, Hirsch, Kochanneck, Mauser, Schmeck:
“A Privacy-Aware Architecture for Energy Management Systems in Smart Grids”,
IEEE ATC 2014 (submitted)
Data Custodian Service
DB 1
Data Custodian
DB m
Database Connector
Request
Handler
Output Module 1
Output Module n
Access Log
…
…
out
in
out
in
req.
Input
Handler
in
in
Input Module 1
Input Module l
…

## Slide 7: Battery-Electric Storage System (BESS)
First prototype providing the whole data life cycle in one tool (ingest, search, retrieve).
  Extended workflow during ingest including
    Automatic metadata extraction
    Indexing metadata
  Search via elasticsearch implemented
  Download client based on search results
  Performance tests
  Documentation
 Please contact Volker Hartmann for more info

## Slide 8: Publications
Rigoll, Gitte, Schmeck: “Data Life Cycles in Future Residential Multi-Commodity Energy Management Systems”, IEEE PES Great Lakes Symposium 2014 (accepted)
Rigoll, Schmeck: “Outline for an Energy Data Management System in Accordance with Data Protection and Privacy”, VDE Kongress 2014 (accepted)
Rigoll, Hirsch, Kochanneck, Mauser, Schmeck: “A Privacy-Aware Architecture for Energy Management Systems in Smart Grids”, IEEE ATC 2014 (submitted)

## Slide 9: Summary
Current status
  HEGRID
  Data Custodian Service
  BESS
  Publications
Future plans
Thank you for your kind attention!