## Slide 1: WP02 PRR: Master Oscillator and RF Reference Distribution
REFMs

## Slide 2: REFMs
REFerence Modules provide reference signals to:
LLRF (1.3 GHz)
  DCM
  LOGM/uLOG
  REFM-OPT
Special Diagnostic systems (1.3 GHz)
  EOD
  eBPM
  TDS
BPM system (216 MHz)
10 MHz signal for diagnostics

## Slide 3: REFMs
18 different REFMs for distribution system (total 85)
All REFMs are based on limited number of blocks (assembly variants):
  Interferometer control board (INCON)
  Interferometer tap point
  Link power amplifier
  Stabilized power amplifier
  Power splitter
  Frequency divider
  TMCB
  FRED
  PLL 3.9GHz

## Slide 4: RF Interferometer Components
Interferometer controller (INCON)
Tap Point
Link power amplifier
Cables

## Slide 5: INterferometer CONtrol board (INCON)
Analog part of interferometer phase-locked loop – beginning of the interferometer
Amplitude stabilization
Temperature stabilization
In production

## Slide 6: Interferometer Tap Point
Limited access to manual tunning in the tunnel (attenuator and phase shifter adjustments)
Electronic, automatic tuning under development
Temperature stabilization
In design stage

## Slide 7: TMCB and FRED
TMCB – Temperature Monitoring and Control Board
Used as a controller for:
  interferometer phase-locked loop
  amplitude stabilization
  temperature stabilization
Communicate with the interferometer tap point controller
FRED – Fuse RElay boarD
Provides all necessary power supplies, fused
Current consumption monitoring

## Slide 8: Stabilized Amplifier
Phase and amplitude drifts compensation between amplifier input and output
First version developed for phase drift compensation (see figures)
Second version under development

## Slide 9: Remaining Components
PLL 3.9 GHz tested in FLASH
Remaining components available:
  Power amplifier (COTS)
  Power splitter (custom Teflon free version of commercial component)
  Frequency divider (DESY design)

## Slide 10: REFM Example (L1)
Limited number of components (assembly variants)

## Slide 11: REFM Example (L3)

## Slide 12: Mechanical Base for REFM Module

## Slide 13
Thank you for your attention

## Slide 14: Component cost
Interferometer control board (INCON)
Interferometer tap point
Link power amplifier - 1100€
Stabilized power amplifier
Power splitter
Frequency divider
TMCB – 600€
FRED
PLL 3.9GHz