## Slide 1: AMS H35 preparation and progress
J. Dopke, T. Huffman, J. J. John

## Slide 2: AMS H35 prep. status
4 chips bonded out (by Daniel) now @RAL (?)
  Al-on-Kapton glued to Carbon Fibre
  Some problems with these first boards
Further 20+ Al carrier boards at RAL
  Most problems fixed
  More chips to be bonded to these
20 carrier boards gold-plated Cu on FR4 sent to RAL
  Useful for non-rad. tests – Possibly also useful in Rad tests.

## Slide 3: AMS H35 Prep Status
Motherboard design and layout nearly complete
  Designed as test board
    Traces all on top and bottom, 4 layer board
    Designed to be tested either via 0.1” header test points or via Lemo connectors
    For digital I/Os, connector designed to mate to Atlys boards, Matt Warren – firmware for operating within SCTDAQ ported (or mostly ported)
    Connect to Atlys with standard high speed SCSI cable.
    Carrier board wire bonded to it, plenty of bondable area on pads.
    Board is easy to kludge in case of anything unanticipated
  Will send away for quotes Monday
  Will expect a 5 day turn-around
  How many boards should we order (10?, 15?)
Kastutis, Jens, Todd, and Jaya John all interested in tests. Initial tests at RAL.
  Tests at Oxford when more carrier boards released
  “Proposed Tests” document attached to Indico site.
  First Radiations will likely be at B’ham proton beam.