## Slide 1: Digital Camera Trigger for the Cherenkov Teleskope Array
March 2015
K.-H. Sulanke
DESY

## Slide 2: CTA, Cherenkov Telescope Array
H.E.S.S. in Namibia
MAGIC auf La Palma
VERITAS in Arizona, USA
about 100 telescopes, on the northern & the southern hemisphere
3 sizes: LSTs, MSTs and SSTs, similar already exist :

## Slide 3
MST Prototype by DESY

## Slide 4: Atmospheric Cherenkov Light
~15 km
cherenkov-light
g-rays
e+e- shower
intensity ➞ energy
orientation ➞ direction
shape ➞ particle
stereo ➞ source

## Slide 5: Sources of Cosmic Rays
Super Nova
Micro Quasare
Dark Matter

## Slide 6: The MST (Medium Size Telescope) Camera
PMT based, 265 cluster a´ 7 PMTs
PMT-d : 38 mm (1.5 Zoll, z.B. Hamamatsu PMT R11920-100)
Pixel-grid : 50 mm by Winston cones
1855 Pixel
Size of the pixel-array : ~ 2 qm
Weight : up to 2000 kg
extrem light sensitive
„shutter“ time in the ns region
self triggered

## Slide 7: Trigger Requirements
3/2/2015
K.-H. Sulanke, DESY
7
Design for the MST (Medium Size Telescope) Camera, „NectarCam“, France
  could also be used for LST (Large Size Telescopes), „DragonCam“, Japan
Because of the NSB (Night Sky Background), the trigger design is quite challenging
Single pixel rate can be greater than 100 Mhz
Basic requirements are
  Sensitive for weak PMT signals
  Fast
  Low latency
  Low power
  Cheap
Alternative to the „Analog Trigger“ designed by Spanish colleagues
  Based on analog sums of up to 21 pixel
  Theoretically better for weak and noisy signals (LST)
Notes: 7

## Slide 8: 37 Pixel Trigger Region
3/2/2015
K.-H. Sulanke, DESY
8
10
12
13
14
15
20
22
23
24
25
30
35
32
33
34
40
44
45
42
43
50
53
54
55
52
60
62
63
64
65
70
71
72
73
74
75
76
c
d
e
f
g
a
c
d
e
f
c
d
e
f
a
a
c
d
e
f
a
c
d
e
f
a
a
c
c
d
d
e
e
f
f
a
b
7-pixel cluster
Notes: 8
I would like to present you two examples of fast link interfaces, designed in our lab.
For both cards block schemes, test results and conclusions will be presented.

## Slide 9: 37 Pixel Trigger Regions
3/2/2015
K.-H. Sulanke, DESY
9
clusters (not pixel !) of a MST shown
Each heagon represents 7 pixel
the trigger region overlaps by four pixels always
7 cluster
trigger region
Notes: 9

## Slide 10: The Trigger Schema
3/2/2015
K.-H. Sulanke, DESY
10
PMT = Photomultiplier Tube
FEB = Frontend Board
DTB = Digital Trigger Backplane
CDTB = Clock & Trigger Distribution Board
L2CB = L2 Controller Board
L0
FEB
DTB
FPGA
PMT
L1
CTDB
L2
#01
…
#15
L0
FEB
FPGA
L1
Sector_trig
#01
…
#18
FPGA
FPGA
Camera_trig
GPS_clock
PMT
ethernet
L2CB
7
7
7
7
L0_neighbor
L0_neighbor
24V
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
backplane connections
Notes: 10

## Slide 11: Digital Trigger L0 Mezzanine Board
3/2/2015
K.-H. Sulanke, DESY
11
Preamp
LVDS Comparator
Diff. Analog in
LVDS out
7 channels
Schematic simulated
LMH6629, very low noise, low offset preamplifier
Trigger threshold
DAC
Opamp
Comp
Digital L0 Mezzanine
LVDS
Notes: 11

## Slide 12: Digital Trigger L0 Mezzanine Board
3/2/2015
K.-H. Sulanke, DESY
12
6 layer PCB with length-tuned signal lines
Preamplifier
Trigger-
Treshold-DAC
Comparator
Notes: 12

## Slide 13: L0, minimum analog input Level
3/2/2015
K.-H. Sulanke, DESY
13
Analog_in, 1mV pk
Comp_out, thr=12mV
Comp_in, gain = 27
Notes: 13

## Slide 14: L1, Digital Trigger Backplane Rev. 2
3/2/2015
K.-H. Sulanke, DESY
14
power
ethernet
Frontend board connector
L0 in /out and ...
connectors to neighbor clusters
RJ-45
RJ-45
Xilinx
FPGA
vreg
flash
24V
ethernet
power
CLK
PPS
L0_trigger
camera_trigger
IP_addr
HV_ena
SPI / JTAG
calib_cyc
reserved
flash
osc
clock (opt.+power)
PPS
L1_trigger_out
L2_trigger_in
Notes: 14

## Slide 15: Digital Trigger Backplane, cont.
3/2/2015
K.-H. Sulanke, DESY
15
Power_in
Clock_in
PPS_in
L1_out
L2_in
Local Oscillator
Xilinx Spartan-6
FPGA
FE-board
Gigabit port
Atmel PROM
(Xilinx config.)
FE-board
24V-fuse
Local synchronous
DC-DC power supply
Xilinx JTAG port
64 bit
ID ROM
Temp. sensor
FE-Board connector
neighbor cluster connections
Notes: 15

## Slide 16: Digital Trigger Backplane, 8 Layer PCB
3/2/2015
K.-H. Sulanke, DESY
16
PCB design by
Carola Rueger DESY
Notes: 16

## Slide 17: The L1-FPGA‘s Functionality
3/2/2015
DESY
17
delay
delay
delay
delay
delay
delay
delay
37 pixel
trigger
fabric
fanout
progr.
delays
PLL
Xilinx Spartan 6 FPGA
L1_trigger
L0_pix_[0][6..0]
L0_pix_[1][4..0]
L0_pix_[6][4..0]
clock
from center cluster
from surrounding clusters
to surrounding clusters
L0*_pix_[0][4..0]
calibrate
STM
to L2_trigger crate
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA

## Slide 18: The L1-FPGA‘s Functionality, cont.
oserdes 8:1
3/2/2015
DESY
18
PLL
Xilinx Spartan 6 FPGA
7 6 5 4 3 2 1 0
prog.
input
delay
950 MHz
118.75 MHz
950 MHz
7 6 5 4 3 2 1 0
118.75 MHz
clock
L0_pix0
trigger_logic_0
pix0_t0
pix1_t0
pix2_t0
…
trig_t0
7 6 5 4 3 2 1 0
prog.
input
delay
950 MHz
7 6 5 4 3 2 1 0
118.75 MHz
L0_pix36
pix36_t0
pix0_t7
pix1_t7
pix2_t7
…
trig_t7
pix36_t7
L0_pix1
0 1 2 3 4 5 6 7
950 MHz
118.75 MHz
0 1 2 3 4 5 6 7
L1_trig
iserdes 1:8
trigger_logic_7
STM
calibrate

## Slide 19: 3NN Trigger Firmware
3/2/2015
K.-H. Sulanke, DESY
19
3NN ( 3 Next Neighbor) of 37 pixel
  about 500 possible combinations
Fully synchronous design
  local oscillator (25 Mhz) or external clock (100 MHz)
Trigger latency 120 ns
Trigger time resolution 1.05 ns (950 Mhz L0-sampling rate)
Trigger jitter +/- 1.05 ns
Firmware automatically detects missing neighbor clusters (bit masking)
Notes: 19

## Slide 20: L1, Connecting the Trigger Backplanes
3/2/2015
K.-H. Sulanke, DESY
20
PCB design by
Carola Rueger DESY
50 way 0.635 mm pitch cable
Notes: 20

## Slide 21: Digital Trigger Test Setup
3/2/2015
K.-H. Sulanke, DESY
21
120 mm x 260 mm, 6 Layer PCB, various analog and digital test points
Xilinx
Analog Inputs
RS232 / 485 interface
L0-Mezzanine
L0 Testboard
L1 Trigger
Backplane
Notes: 21

## Slide 22: Digital Trigger Test Setup at DESY
3/2/2015
K.-H. Sulanke, DESY
22
Notes: 22

## Slide 23: 3NN Trigger Test Results
3/2/2015
K.-H. Sulanke, DESY
23
100% trigger and 0% trigger situation
trigger
5mV pk
2.5 ns FWHM
3ns shift
No trigger
Analog input signals, zoomed time scale
Notes: 23

## Slide 24: L2
3/2/2015
K.-H. Sulanke, DESY
24
L2 still in the design phase
  will be a crate, ~ 50 x 20 x 20 cm, ~ 11 kg
    18 x CTDB (Clock & Trigger DistributionBoard)
    1 x L2CB (L2 Controller Board)
      Ethernet interface
      Optical / electrical camera trigger output
PMT = Photomultiplier Tube
FEB = Frontend Board
CTDB = Digital Trigger Backplane
CSB = Cluster Service Board
L2CB = L2 Controller Board
L0
FEB
DTB
FPGA
PMT
L1
CTDB
L2
#01
…
#16
L0
FEB
FPGA
L1
Sector_trig
#01
…
#18
FPGA
FPGA
Camera_trig
GPS_clock
PMT
ethernet
L2CB
7
7
7
7
L0_neighbor
L0_neighbor
24V
Notes: 24

## Slide 25: The Clock & Trigger Distribution Board (CTDB)
3/2/2015
K.-H. Sulanke, DESY
25
Clock
PPS
L1_T
Trigger
finger
edge
backplane
connector
vreg
CLK
PPS
L1
Trigger
24V
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
RJ45
15 x
Cat6
Cable
QOSC
CLK
PPS
Trigger
Sel_local
PLD
Fanout
+
Repeater
Local mode, clk+pps+trigger by Altera PLD EPM3064, for test purposes
Schematic design done
Card size 160 x 233
Notes: 25

## Slide 26: The L2-Crate
3/2/2015
K.-H. Sulanke, DESY
26
Schroff 24563-442
6 U, 84 HP (21 slots)
Card size : 233 x 160 mm
Preferred slot usage, see below
D2 = 160 mm
D1 = 175 mm
D = 235 mm
L2CB
9x CTDB
9x CTDB
Notes: 26

## Slide 27: Summary
3/2/2015
K.-H. Sulanke, DESY
27
Main advantage of the digital trigger is its flexibility concerning the trigger algorithm and the simplicity of the overall scheme
The L0 stage performs very good (signals of 1mV are still detectable)
First results with the L1 stage, e.g. the 3NN trigger, are encouraging
  More sophisticated alghorithms will follow
  E.g. a time gradient trigger
The L2 stage will be designed and tested in 2015
  Intermediate solution (by Axel Kretzschmann) do exist
First camera integration tests in 2014 successful
Not yet clear who makes it finally, the analog or the digital trigger ?
Notes: 27

## Slide 28: Outlook
3/2/2015
K.-H. Sulanke, DESY
28
19 cluster „Demonstrator“ test planned in Q4 2015
  NectarCam (MST, France)
    Nectar chip based (analog pipeline chip)
Notes: 28

## Slide 29: Back Up Slides
3/2/2015
K.-H. Sulanke, DESY
29
Notes: 29

## Slide 30: L2 Trigger Sectors, MST, Example
3/2/2015
K.-H. Sulanke, DESY
30
271 cluster shown (1897 pixel)
Each sector comprises 14..16 clusters and is connected to a certain CTDB board (L2 crate)
Notes: 30

## Slide 31: Test Setup w. Pattern Generator
3/2/2015
K.-H. Sulanke, DESY
31
DTB used as pattern generator board
e.g. for 3NN pattern
time resolution is 1.05 ns
pattern generator board
trigger
board
expected
and
real trigger
Notes: 31

## Slide 32: Digital Trigger Test Board
3/2/2015
K.-H. Sulanke, DESY
32
Testing the L0 boards AND the FE-board interface of the Dig. Trigger Backplane
Xilinx with RS232 / RS485 interface, to set the discriminator thresholds etc.
DAC
Opamp
Comp
FPGA
Dig.Trigger-Bpl.
FPGA
FE-board
interface
L0-Testboard
7
6x5 L0
by surr.
clusters
Digital L0 Mezzanine
L0
LVDS
PMT
or
Pulse-Gen.
Single ended
to diff.
Opamp
RS 232
RS 485
Notes: 32

## Slide 33: Digital Trigger Backplane, List of Key Hardware Features
Nominal power consumption: 1.5 W
Weight : 95 g + 10 g cabling to neighbor clusters -> 28 kg for MST
Automatic neighbor cluster recognition (border zone)
Synchronous DC-DC converter (24 V to 3.0 V …)
Local clock and external clock input (any diff. > 0.1V pk-pk)
FPGA load by JTAG cable or PROM or remote (by FE board)
6 x bidirectional L0 signal connection with neighbor cluster
Temperature sensor (allows automatic delay correction, if needed)
adjustable 8 bit cluster position ID (for unique, position-independant, firmware)
Gigabit ethernet pass through connection to FE-board
RJ 45 connector as combined power and clock input (single cat5e cable)

## Slide 34: Combined Power and Clock Input
3/2/2015
K.-H. Sulanke, DESY
34
24V, clock, and PPS over a single wire pair
requires a single cat5e cable per cluster only (+ gigabit ethernet cable)
Current spikes of 0.8 A did not influence the (recovered) clock quality
Cat5e - Wire Pair | Standard mode | Combined mode
1 | Clock_in | Clock_in / PPS_in / 24V
2 | PPS_in | GND
3 | Trig_L1_out | Trig_L1_out
4 | Trig_L2_in | Trig_L2_in
FE-board
Gigabit port
Combined
Power and
Clock input
Ext_Clock_PPS
Clock_recovered
PPS_recovered
Clock+pps
24V
Alternative
Power conn.
Notes: 34

## Slide 35: M12 Cat6 , Combined Power / Clock Input
3/2/2015
K.-H. Sulanke, DESY
35
Instead of RJ45, more robust
by Harting, Molex, ...
To be replaced by M12
Notes: 35

## Slide 36: 7-PMT-Cluster “DragonCam”

## Slide 37: Analog Pipeline Chip
500 MHz ... 5 GHz sampling rate