## Slide 1: FLASH2 Extension of the FLASH Facility
Elektronenstrahldiagnose in FLASH2
N. Baboi, MDI für den Diagnose-Team
Beschleuniger-Betriebsseminar 2015
Grömitz, 24. März 2015

## Slide 2: Inhalt
FLASH2
FLASH2 Standard-Diagnostik Überblick
  Allgemeine Eigenschaften
  Elektronik
  Inbetriebnahme (allgemein)
Diagnostik-Monitore in FLASH2
Zusammenfassung
  Ladungs-Monitore / toroide Toroid Protection System (TPS)
  Schirme
  Beam Position Monitors (BPM): Cavity, Button und Stripline BPMs
  Beam Loss Monitors (BLM) Beam Halo Monitors Ionizations-Kammern Cherenkov-Verlustmonitore

## Slide 3: FLASH2
Extraction to FLASH2
FLASH2 variable gap undulators
315 m
5 MeV
150 MeV
1250 MeV
Bunch Compressors
450 MeV
Accelerating Structures
RF Stations
Lasers
RF Gun
Soft X-ray Undulators
sFLASH
FEL Experiments
Photon Diagnostics
Beam Dump
THz
FLASH1
FLASH2
FLASH2 Experimental Hall
≥ 30 ms gap

## Slide 4: Typische Parametern
 | FLASH(1) | FLASH2 | E-XFEL
Max. energy [GeV] | 1.25 | = | 17.5
Pulse repetition rate [Hz] | 10* | 1-10* | 10
Max. bunch frequency [MHz] | 1 | = | 4.5
Max. pulse duration [mm] | 800 | = | 600
Charge [nC] | <0.1 – 1 | = | 0.02 - 1
Photon wavelength [nm] | 4.2 – 45 | 4 – 60 | 0.05 - 6
* FLASH2 operates sometimes at 1 Hz to reduce activation

## Slide 5: Inhalt
FLASH2
FLASH2 Standard-Diagnostik Überblick
  Allgemeine Eigenschaften
  Elektronik
  Inbetriebnahme (allgemein)
Diagnostik-Monitore in FLASH2
Zusammenfassung
  Ladungs-Monitore / toroide Toroid Protection System (TPS)
  Schirme
  Beam Position Monitors (BPM): Cavity, Button und Stripline BPMs
  Beam Loss Monitors (BLM) Beam Halo Monitors Ionizations-Kammern Cherenkov-Verlustmonitore

## Slide 6: FLASH2 Standard-Diagnostik: Überblick
Most monitors were designed for the European XFEL
  Make use of synergies given by the similar time line
  Some have been designed specially for FLASH(2) or have a temporary solution
Deliver bunch by bunch measurements, with few exceptions
Generally based on MTCA-technology
  Modular architecture, high availability, redundant power, well defined management.
  9 MTCA crates for diagnostics installed at FLASH2
Challenges (not only for diagnostics)
  MTCA previously not fully developed x2timer, power supplies
  Low charge
  Different charge for FLASH1 and FLASH2 within the same pulse
  Different rep-rate of bunch trains FLASH1 and FLASH2 (10 vs 1 Hz)

## Slide 7: Diagnostik Panel

## Slide 8: Orbit Panels

## Slide 9: Neue Standard Diagnostik in FLASH
 | Pipe Ø (mm) | FLASH(1) | FLASH2% | XFEL&
Toroids | 40.5 & 100 |  | 5 | 36
Screens | 40.5 & 96 |  | 7 | 64
Screen on dump-window |  |  | 1 | 3
Cavity BPMs (10 mm) | 10 | 3 (for tests) | 17 | 101
Button BPMs | 10 - 96 | 4 | 12 | >300#
Stripline BPMs | 34 & 44 |  | 4 | -
BLMs | - |  | ~56 | >300
BHMs | 100 | 1 | 1 | 4
% Also other diagnostics, not XFEL-type: e.g. Ionization chambers, Cherenkov monitors * With FLASH-electronics and with test-LCBPM-electronics # Electronics: by PSI at XFEL, by DESY at FLASH2 (LCBPM) & Also other diagnostics, not installed in FLASH2: e.g. Wire Scanners, Dosimetry monitors

## Slide 10: FLASH2 Tunnel und technische Abseite
Electronics installed in technical corridor, parallel to tunnel
  At the XFEL: all diagnostics electronics installed in the tunnel
FLASH2 Tunnel
Extraction
FLASH1 Tunnel
ACC7
SASE undulators

## Slide 11: Diagnostik-Inbetriebnahme
“Cold” Commissioning
  Check monitors (mostly vacuum parts):
    e.g.: screens: motors, light; BPMs: short, symmetry
  Check cables
  Technical checks of electronics
    Check individual components (mostly MTCA-based) and how the parts work together
    Check availability and quality of signals needed: timing, IT
  Test servers
  Panels (!)
  Pre-calibration: either theoretical values or from lab measurements
Commissioning with beam
  Adjustment of trigger, clock
  Adjustment of electronics settings
  Calibration with beam

## Slide 12: Erster Elektronen-Strahl in FLASH2
Beam separation seen on BPM and screen before septum
Bunch Compressors
Accelerating Structures
RF Stations
Lasers
RF Gun
Soft X-ray Undulators
sFLASH
FEL Experiments
Photon Diagnostics
Beam Dump
THz
FLASH1
FLASH2

## Slide 13: Erster Elektronen-Strahl in FLASH2 Extraktion
FLASH2
FLASH1
BLM (raw)
BPM (Scope)
Screen
Toroid (raw)

## Slide 14: Inhalt
FLASH2
FLASH2 Standard-Diagnostik Überblick
  Allgemeine Eigenschaften
  Elektronik
  Inbetriebnahme (allgemein)
Diagnostik-Monitore in FLASH2
Zusammenfassung
  Ladungs-Monitore / toroide Toroid Protection System (TPS)
  Schirme
  Beam Position Monitors (BPM): Cavity, Button und Stripline BPMs
  Beam Loss Monitors (BLM) Beam Halo Monitors Ionizations-Kammern Cherenkov-Verlustmonitore

## Slide 15: Diagnostik-Monitore in FLASH2
Beam Arrival Monitors
Bunch Compression Monitor etc.
XFEL-type
Charge monitors / toroids Toroid Protection System (TPS)
Screens
Beam Position Monitors: Cavity BPMs (CBPM) Button and Stripline BPMs (Low Charge BPMs)
Beam Loss Monitors (BLM) Beam Halo Monitors Ionization Chambers Cherenkov Monitors

## Slide 16: Ladungs-Monitore / Toroide
System for the XFEL under test
  Network of monitors to interlock on transmission and bunch pattern failure
  Noise < 1 pC
Temporary solution for FLASH2
  Put signal from front-end electronics on MTCA-ADC
  Differential signal sent over CAT cables
W
W
W
W
+
+
+
Front-end
Adapter RTM
RTM SIS8900
AMC SIS8300
M. Werner, IBIC2014, WEPF02

## Slide 17: Ladungs-Monitore / Toroide
►
Resolution measured with intermediate solution: < 1 pC rms
Resolution of charge monitors along FLASH(1) (~ 0.4 nC)
o FLASH-type (VME)
o FLASH2-type (MTCA)
O FLASH2 with new amplifier
► Dark current monitor
FLASH1 / 0.4nC
FLASH2 / 0.3nC
toroide
Cavity BPMs

## Slide 18: Toroide: Strahl-Verteilung zu FLASH1 und FLASH2

## Slide 19: Toroid Protection System (TPS)
5 MeV
150 MeV
1250 MeV
Bunch Compressors
450 MeV
Accelerating Structures
RF Stations
Lasers
RF Gun
Soft X-ray Undulators
sFLASH
FEL Experiments
Photon Diagnostics
Beam Dump
THz
FLASH1
FLASH2
TPS 0
TPS 1
TPS 2
At XFEL:
M. Werner, WEPF02
A. Hamdi, DIPAC 2007, p. 349
Temporary solution using 3 TPS modules designed for FLASH

## Slide 20: Schirme
BEAM
Optics Axis
Scintillator based (LYSO:Ce), spatial suppression of COTR
Optics:
  Look under 45 deg
  Uses “Scheimpflug´s” principle to extend depth of field
10 µm resolution required
  single bunch, streaked
Demonstrated at FLASH1
200µm thick LYSO Screen (ON-Axis)
2 half 200µm thick LYSO Screens (OFF-Axis)
Dot Grid Target(spot Ø .50mm)
C. Wiebers, IBIC2013, WEPF03

## Slide 21: Schirme
Fully commissioned
FLASH2
FLASH1
1FL2SEED4
1FL2SEED6
1FL2SEED7
1FL2SEED5

## Slide 22: Cavity BPMs
Cavities
  Dipole + reference resonator
  3.3 GHz, low Q (about 70)
  17 installed between undulators – 10 mm pipe
  No individual tuning
Readout (PSI)
  MBU (Modular BPM Unit) with 2 RFFE for 2 cavity BPMs
  Up to 4 MBUs connected to 1 DAMC2 interface board
  Timing: decoding timing protocol via fiber in MBU
Resolution requirement
  2 mm rms for 0.1-1 nC and within ± 0.5 mm (1 mm at XFEL, but longer cables at FLASH2)
M. Stadler, IBIC 2014, WEPD12

## Slide 23: Cavity BPMs: Gemessene Auflösung
BPMs in FLASH2
  Difference between expected and measured position with Gaussian fit
Test BPMs in FLASH1
  0.5 mm rms for 0.24 nC bunch charge and 0.5 mm bunch offset
Resolution of various FLASH1-BPMs (designed for 1 nC)
~0.35 nC
preliminary
D. Lipka, IBIC 2014, TUPF07

## Slide 24: Cavity BPMs: Ladungs-Messung
Charge resolution for 100 pC bunch charge < 0.2 pC rms
D. Lipka, IBIC 2014, TUPF07
FLASH2 / 0.3nC
toroide
Cavity BPMs

## Slide 25: Button und Stripline BPMs: Überblick
Low Charge BPMs (LCBPM) electronics
  Name chosen in contrast to system designed for FLASH for charges of 1nC and higher
  Designed for FLASH2 (and to be installed in all FLASH)
Button or
Strip-line BPM
Delay ~100ns
Broadband
RF Combiner
RF cable 3/8“
Length < 80m
Signal of horizontal plane, delay line: ~100ns
Typical Signals from BUTTON/strip-line BPM
B. Lorbeer, IBIC 2014, TUPF08
S. Vilcins, IBIC2014, TUPF11

## Slide 26: Button und Stripline BPMs: LCBPM
Rear Transition Module (RTM)
180mmx162mm
Compatible with the MTCA.4
for physics standard
RF Front-End
MicroTCA crate
X-Channel
Y-Channel
100ns
Crate used for the tests includes:
management carrier hub (MCH)
hard disk (HD), processor (CPU)
Digitizer SIS8300
timing module x2timer
RTM Analog Output Signals
G=38dB
Att.>60dB
Peak Detector
5 BPMs/crate
Front Side
Back Side

## Slide 27: Button und Stripline BPMs: Betrieb
RMS at q=36 pC, 200 pulses (incl. beam jitter)
Server Panel for Firmware Adjustment
BPM Expert Panel
Strip-Line BPM
Button BPM
sy = 22 mm
sy = 39 mm
bunch charge | 0.1-1 | nC
bunch spacing | ≥222 | ns
maximum macro-pulse repetition rate | 25 | Hz
beam pipe diameter | 40.5 | mm
single bunch resolution | 50 | μm
Averaged RMS resolution over 1000 bunches of identical train | 10 | μm
Range for max. resolution | +/- 3 | mm
Operation range with reasonable signal | +/-10 | mm
Requirements (from XFEL requirements)

## Slide 28: Beam Loss Monitors (BLMs)
Detector
  Scintillator or fused silica (rod or fiber)
  PMT: HV voltage (~500 V) generated by Cockcroft-Walton multiplier on board mounted at PMT
Electronics MTCA-based with low latency interface with MPS
Alarms algorithms
  Single bunch
  Multi-bunch
  Integration
  OR of comparator and FPGA alarms
Readout
Electronics
Power control
PMT
&
HV
Scintillator
Beam Loss Monitor
e,γ,n0
Alarm
(to MPS)
A. Kaukher, BIW 2012, p. 35

## Slide 29: Beam Loss Monitors: Status
Calibrated single and multi-bunch alarm
Integration alarms to be calibrated

## Slide 30: Verlustmonitore am Dump: BLMs und Ionizations-Kammern
Similar to FLASH1: BLMs based on quarz-fiber + Ionization Chambers (air filled cables) along last 2m of beam line
beam
N. Baboi, BIW 2010, p. 420
BHM

## Slide 31: Verlustmonitore am Dump: Beam Halo Monitor
Similar to FLASH1
8 sensors: 4 Diamond + 4 Sapphire mounted behind the dump vacuum chambers
  At XFEL mounted outside chamber
FLASH1
A. Ignatenko, IPAC 2012, p. 816

## Slide 32: Cherenkov Verlustmonitore entlang der Undulatoren
  Fibers installed along the undulator chamber (left and right)
  Similar to FLASH1
  Will be commissioned next
FLASH1
J. Schwarz

## Slide 33: Andere Elektronen-Strahl-Monitore in FLASH2
Screen on dump-window
Beam Compression Monitors
Beam Arrival Monitors
Coherent Transition Radiation monitors
C. Behrens, IPAC’10, p. 912
A. Angelowski, IBIC 2014, MOPD25
S. Wesch, BIW 2012, THAP01
J. Good, IBIC’13, p. 814

## Slide 34: Zusammenfassung
XFEL and FLASH-type of diagnostics
  Many leassons learned for the European XFEL
Some fully commissioned:
  Screens
Some in advanced commissioning state; still to do (e.g.):
  Integration alarm of BLMs
  Implement automatic gain control for LCBPMs
  BPM calibration
Some have temporary solution
  Toroid electronics and Toroid Protection System
Some to be commissioned
  Cherenkov loss monitors
  Screen at dump-window

## Slide 35: Danksagung
Many people contributed to the work and this talk
  R. Neumann, N. Wentowski, Z. Pisarov, M. Werner, J. Lund-Nielsen, B. Lorbeer, A. Kaukher, T. Wamsat, A. Ignatenko, F. Schmidt-Föhre, K. Honkavaara, H. Tiessen, B. Michalek, R. Zahn, B. Keil, D. Nölle, O. Hensler, G. Marinkovic, K. Knaack, J. Schwarz, J. Liebing, H. Sokolinski, G. Kube, C. Wiebers, M. Felber, R. Zahn, S. Vilcins, J. Kruse, D. Renner, M. Felber, S. Schreiber, M. Holz, M. Pelzer, A. Ziegler, M. Hoeptner, H. Sokolinski, M. Stadler, I. Krouptchenkov
  and many others
Other Labs involved
  PSI: Cavity BPM electronics
Most photos by Dirk Nölle

## Slide 36: 1st Lasing at FLASH2
20:37
20:56
FLASH1
FLASH2
FLASH1 lasing in parallel with 250 pulses
FLASH2: 1 pulse
0 50 100 150 200 250
Maximum
Actual
Average
FLASH1: 250 pulses
Bunch number
Energy (μJ)
S. Ackermann, MOPF22
K. Honkavaara, FEL2014, WEB05
S. Schreiber, FEL2014

## Slide 37: Many Lessons Learned for the European XFEL
The commissioning of FLASH2 paves the way for an easy(ier) commissioning of the XFEL diagnostics
D. Nölle, IBIC 2014, WEPF15
M. Hüning, IPAC2013, WEZB101