## Slide 1: Sample Environment Integration
Joachim Schulz
WP-79
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)

## Slide 2: WP-79 Sample Environment for Six Instruments
Biology
Biology labs with XBI UC
Liquids & Gases
Fixed Targets
Fast sample scanner
Magnets & Cryogenics
Compact pulsed magnet
Liquid jets
COMO UC
HIBEF UC
Cryogenics
Temperature control
Load-lock sample exchange
Aerodynamic lens in-kind contribution
Biological sample preparation
Mass spectrometry

## Slide 3: WP-79 mission
Provide state of the art sample environment
  Biological samples for SPB/SFX and others
  Fast sample scanner for SCS, MID, SPB, HED
  Aerosol injector (via in-kind contribution)
  Compact pulsed magnets for MID, SCS, HED
Assist users bringing samples into the instruments
  Provide user laboratories
  Integrate sample environments into the instruments
    Special user equipment
    Pool of equipment in Sample Environment Group

## Slide 4: Plans for day-one sample delivery
Prototypes will be designed in close collaboration with instruments
  SCS: Fast sample scanner
  SCS: Constant field magnet
  MID and SCS: Compact pulsed magnets
  SPB/SFX: Biological sample preparation and delivery
Participation in safety concepts for
  Magnets (together with HIBEF UC)
  Biological samples (XBI UC)

## Slide 5: Fixed targets: Fast sample scanner
Design in close cooperation with the SCS team
Electronics
  Uses Beckhoff PLCs wherever possible
  Coordinated with WPs 90 and 91
Setup and testing in Sample Environment laboratory
Contact points with instrument and machine:
  Vacuum interlock with sample chamber
  Synchronization with X-rays

## Slide 6: Fast sample scanner: Proceeding from prototype
Prototype for SCS will be day-one instrumentation
  Target area 50x50mm², µm precision, 10-9 mbar
  Available: 1Q 2017
Modifications for MID and SPB/SFX
  Larger area 100x100mm², reduced vacuum demands
  Available: 3Q 2017
Additional requirements for HED
  Electromagnetic pulse protection
  Debris shielding
  Coordination with HIBEF user consortium

## Slide 7: Deliverables – magnetic environments
Day-1 instrument for SCS and MID
4Q 2015 – prototype built and tested
DC electromagnet
Miniature pulsed coil
3Q 2017 instrument for SCS and MID
1Q 2016 – 1st prototype built
From 1Q 2016 – DAQ & Control needed (Draft definition 10.2014)
HIBEF 60T pulsed coil
HIBEF contribution for HED – lead time 18 months
WP79 responsible for XFEL integration – ongoing 2015-17

## Slide 8: Magnetism: miniature coils for pulsed fields
Agreed concept and specifications with MID and SCS
Design support by ESRF
2015 – prototype being built at Hera-Süd:
  Inserts on chamber top-flange, 15-20T split-pair coil, L-He cryostat,
  Will be tested for beamline conditions
DAQ & Control
  Testing in LabVIEW by WP79
  Later in Beckhoff/Karabo by DAQ&Control
Aim for one instrument that can be adapted to fit SCS or MID chambers

## Slide 9: Magnetism: HIBEF 60 T pulsed coil for HED
HIBEF program (High Intensity Beamline for Extreme Fields)
HLD (HZDR) will deliver 1MJ pulser and 60T coil to the HED instrument
WP79 role: Interface for pulse magnet issues and integration
Workflow items together with HLD:
  Safety assessment for pulser/coil needed for HED hutch planning
  Technical infrastructure – cable routing

## Slide 10: Bringing biology into X-rays
Methods
Liquid jets
Aerosols of neutral and charged particles
Fixed targets (solid sample scanner)
Safety aspects
Genetically modified organisms
Contamination protection
  Samples
  Outside world
Instruments
SPB/SFX is specialized for this research
MID/FXE for imaging
SCS for soft X-rays
Typical samples
Micro to nano sized protein crystals
Single living cells, viruses, organelles
Proteins and complexes
Biology users
Need preparation laboratories
Sample delivery
Data analysis

## Slide 11: Integrated sample delivery scheme
Sample injection
Liquid Jet
Delivery system
HPLC pumps
Laboratories

## Slide 12: XBI and SPB biology laboratories
Equipped for
Cell expression
Crystallization
Sample preparation
Quality control
XBI user consortium
Laboratory
User support
Computation
SPB/SFX
Preparation room
Sample lift
Preparation hutch
WP-79
Operates laboratories for SPB/SFX
Coordinates XBI UC
Takes responsibility in
  Laboratory safety
  User support

## Slide 13: Delivery of biological samples
Delivery system
HPLC pumps
Integration
With Karabo for
  Control
  Safety
Sample
Standardizes tubing to sample systems
Liquid jets
Aerosol injector
Electrospray ionization

## Slide 14: SPB/SFX sample environment integration
Upstream focus
Versatile setup for single particle imaging and crystallography
Downstream focus
Reuses the beam for high throughput serial femtosecond crystallography (SFX)
WP-79
Coordinates both sample environments
Interfaces between SPB/SFX and XBI
Gives user support

## Slide 15: WP-79: Sample Environment Group