## Slide 1: Status of test kit
J. Dopke, T. Huffman, J. J. John, M. Stanitzki with help from many others

## Slide 2: HVStripV1 hardware - stock
8 motherboards have now been produced and allocated
  1 each at Argonne, DESY, Glasgow, Oxford, SCIPP and RAL
  1 each will be sent to IHEP (Beijing) and KIT (Karlsruhe) pending tests in Oxford this week
The stock situation is:
  Zero unbonded chips
  4 daughterboards with chips – 2 alu/kapton/carbon fibre, 2 FR4/Cu
  8 bare motherboards with central cutout + 5 bare without cutout
  Components: stock to build 8 more motherboards
  28 bare daughterboards – 14 alu/kapton/carbon fibre, 14 FR4/Cu

## Slide 3: HVStripV1 build plan
Given the pending order for 100 more HVStripV1 chips,
Given that each motherboard can test 5 daughterboards (est),
We think we should order and build:
  100 more FR4/Cu daughterboards
    minimise gold coverage, add mounting hole to ease transport
  25 more motherboards in panels
  Use automated assembly (Oxford) for the passive components on the back (these are the portions of the work where you save costs by doing in bulk)
  Then “freeze” production of the boards
  Then complete the motherboards in small batches as needed, adding the more expensive IC and connector components, to manage costs
  Jaya John to check whether we can use SMA connectors instead of Lemos to reduce costs (for after our present stock of Lemos is used up)

## Slide 4: CHESS test boards
Current status:
Test board spec: first draft with authors for checking
Will shortly distribute updated draft for general review
We have improved the design to expedite testing – see next slide

## Slide 5: CHESS test boards, ctd.
CHESS motherboard – for both HV and HR daughterboards
Samtec connectors
reliable, well known to ATLAS strip community
CHESS daughterboard
3 flavours:
HV CHESS
HR CHESS “PonN”
HR CHESS “PonP”
cut line, for removing connectors prior to irradiation, if shielding cannot be used
second set of connector pads, for post-irradiation if need be
CHESS test chip
possible cut line for E-TCT (for HV CHESS d/b)