## Slide 1: Status of test kit
J. Dopke, T. Huffman, J. J. John, M. Stanitzki with help from many others

## Slide 2: HVStripV1 hardware
Current status
  Motherboard for IHEP (Beijing) being tested today; Motherboard for KIT will be tested tomorrow.
  4 more motherboards built in Oxford, now at RAL for wire-bonding to daughterboards
  1 of these new ones is for Cambridge
Build of more motherboards
  Panelised and added ground pins for ease of testing
  Artwork to be reviewed tonight, then sent for quoting
  Available ~mid-January if we use 10-day turnaround
More daughterboards
  Added solder mask to Cu/FR4 daughterboards to minimise gold
  Added mounting holes to ease transport
  Artwork to be reviewed tonight, then sent for quoting
  Also ~mid-January if we use 10-day turnaround

## Slide 3: CHESS test boards
CHESS motherboard – for both HV and HR daughterboards
Edge connector
CHESS test chip
possible cut line for E-TCT (for HV CHESS d/b)
Spec tomorrow
~120 pins needed to support both HV and HR daughterboards
Proposing keyed edge connector instead
Same quality as Samtec “FTSH” connectors used for ABC130 testing, from specs