## Slide 1: Status of test kit 17 Feb 2015
J. Dopke, T. Huffman, J. J. John, M. Stanitzki with help from many others

## Slide 2: CHESS test boards
Status
AMS-CHESS daughterboard: schematics to be completed this week
Layout during week of 2 March (away week of 23 Feb)
Motherboard-daughterboard interface
As discussed last meeting, interface is now 100 pins.
This permits the daughterboard to lie parallel to the motherboard, for probing.
The perpendicular geometry is still possible – may be advantageous for some irradiation campaigns (?)
  We had a short cooling down period in Birmingham though, so arguably this geometry is less necessary
Having both options requires two slightly different motherboard designs
  -- as Samtec made the mounting holes awkwardly overlapping, between the parallel and right-angle connector variants.

## Slide 3: Back up: interface details -- taken as agreed now
no. pins | Pins allocated on connector | no. pins | AMS-CHESS signals | no. pins | TJ-CHESS signals
2 | Low voltage supplies | 1 | VDD 3.3V | 1 | VDD 3.3V
 |  |  |  | 1 | VDD1V8
4 | Ground | 4 | GND | 4 | GND
1 | High voltage / substrate bias | 1 | HV sub | 1 | SUB
4 | Voltage biases | 1 | Casc | 1 | Bias_GR1
 |  | 1 | VPload | 1 | Bias_GR2
 |  |  |  | 1 | vPreAmpCascN
 |  |  |  | 1 | vShaperCascN
4 | Current biases | 1 | iBias | 1 | iBias_SF
 |  | 1 | iFB | 1 | iBiasPreAmp
 |  | 1 | iNSF | 1 | iBiasShaper
 |  | 1 | iN |  | 
81 | Analogue output lines | 72 | Active array pixel outputs | 81 | Outputs in all - identity depends
 |  | 7 | Outputs of isolated fast amplifiers |  | on wire-bonding
1 | Common analogue input to amplifiers | 1 | Common input to amplifiers | 1 | Common input to amplifiers
1 | Digital input to pixels |  |  | 1 | preRstInt_in - digital input
2 | Daughterboard flavour pins ("outputs" of daughterboards) | 2 | "01" | 2 | "10" PonN or "11" PonP
100 | Total pins allocated | 94 | Total pins used for AMS-CHESS | 99 | Total pins used for TJ-CHESS
Which signals are used for the AMS-CHESS daughterboard
Which signals are used for the TJ-CHESS daughterboard
Allocation of different signal/bias types on connector