## Slide 1: Latest LLRF Developments.
Sven Pfeiffer for the LLRF team
The 3rd ARD ST3 Workshop
Karlsruhe, 16.07.2015
SRF & NRF Control @ FLASH

## Slide 2: Content
MicroTCA.4 Operation @ FLASH
  Overview – SRF Control
  Statistics 2014
  FLASH1/2(/3)
NRF GUN Regulation
  Concept - single cavity regulation
  Achievements so far
  Disturbance sources and noise
  Frequency control

## Slide 3: MicroTCA.4 @ FLASH
Since ~ 2 years (8/2013) in standard operation for all SRF nodules
  Mainly software problems at beginning
  Switched 3x back to VME based backup system
Factor 4-5 improvement to VME system
Achieved XFEL specifications
  dA/A < 0.01%, dφ < 0.01 deg.
Vector Modulator (uVM)
LLRF Controller (uTC)
Down Converter (DWC)
Digitizer (uDAQ)

## Slide 4: Operation Statistics 2014 - Downtime
Chart: 
| RF-gun | RF-gun water | RF-3 | RF-stations | RF-water | RF-39 | LLRF | Magnet PS | Cryo | Power glitch | Infrstructure | Timing | Controls | Operating | Photon | Others
 | 4.19 | 49.76 | 17.54 | 39.31 | 8.8 | 16.55 | 42.87 | 15.52 | 13.05 | 4.45 | 9.85 | 8.36 | 38.49 | 18.8 | 26.69 | 37.96
RF-gun interlocks
RF-3
Other RF-stations
RF-gun temperature stabilization
RF-stations water
RF-39
LLRF
Cryogenics
Magnet PS
Infrastructure
Power glitches
Others
Photon beamlines
Operating
Controls
Timing
Chart: Downtime per week
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52
Downtime | 1.3274 | 1.0952 | 5.0476 | 2.2262 | 3.756 | 2.3095 | 1.8036 | 2.381 | 2.8155 | 9.7917 | 3.5655 | 0.10714 | 4.625 | 1.8036 | 6.2619 | 0.89286 | 9.0536 | 2.6488 | 8.2917 | 7.4464 | 7.3929 | 0 | 0.70833 | 2.9524 | 10.1845 | 3.4226 | 10.7917 | 6.9167 | 4.0655 | 1.8274 | 1.5655 | 27.1131 | 1.119 | 2.7619 | 4.7619 | 2.4167 | 7.6012 | 3.3452 | 1.75 | 2.25 | 10.4226 | 4.744 | 2.0298 | 0.70238 | 1.8571 | 1.8155 | 6.625 | 1.1429 | 0.16071
Downtime (%)
Total downtime
352 h = 4.5%
RF-Gun water stabilization
43 h
12.2 %
Operation hours
7791 h
0.55 %
Week

## Slide 5: Multi Beamline Operation - FLASH1/2 (/3)
Variation in Amplitude and Phase
Restricted transition time
  Large step  more time needed due to limited Klystron power
First lasing FLASH2
20.08.2014

## Slide 6: Content
MicroTCA.4 Operation @ FLASH
  Overview – SRF Control
  Statistics 2014
  FLASH1/2(/3)
NRF GUN Regulation
  Concept - single cavity regulation
  Achievements so far
  Disturbance sources and noise
  Frequency control

## Slide 7: RF GUN Regulation @ FLASH
NRF cavity with bandwidth ~ 60 kHz
Latency reduced < 1100 ns
  FPGA code optimization/clean-up
  Latency since 05/2015 @ 700 ns
1.3 GHz
1.3 GHz + IF
to Pre-ampl.
clk
ADC’s
MicroTCA.4 operation since 01/2015
Single cavity regulation by 2 boards with MicroTCA.4 standard
  DWC8VM1
  SIS8300L
DAC
DAC
MO
VM
Klystron
HV
Pre-
Ampl.
RF GUN
ADC
ADC
ADC
ADC
Forw
Refl
Feedback loop

## Slide 8: RF GUN Regulation @ FLASH
1) Output Vector Correction (OVC)
  Drift compensation
2) Learning Feedforward (LFF)
   Pulse to pulse FF adjustment
3) MIMO Controller (FPGA - FB)
   Intra-pulse feedback
  Currently: PI – like feedback
Limitation: Loop-delay ≈ 1.1 μs
   Limits feedback gain!
Regulation Concepts
Adapted from SRF regulation
Goal: dA/A<0.01%
dφ<0.01 deg. (rms)

## Slide 9: RF GUN Regulation @ FLASH
PI Regler
Goal: dA/A<0.01%
dφ<0.01 deg. (rms)

## Slide 10: RF GUN Regulation @ FLASH
PI Regler
Average of 800 RF pulses
Beam transient (10 Bunche@100kHz)
Pk2pk ~ 0.008 ~ 0.01% or 0.1‰

## Slide 11: RF GUN Regulation @ FLASH
PI control
0.01%
0.01deg.
Factor 3-4 improvement necessary
MTCA.4 (9MHz1MHz)
VME (1MHz)
Goal: dA/A<0.01%
dφ<0.01 deg. (rms)

## Slide 12: Control Loop @ SRF and NRF cavities
Pre-Amp,
Klystron,…
r(t)
e(t)
du(t)
dy(t)
n(t)
yr(t)
yi(t)
ui(t)
ur(t)
Delay
GM = 9 dB
KP = 2.8
limited to ~ 2.8
Error suppressed
by x3.8
KP = 100
NRF cavity regulation:
Low noise subsystems
Small errors (disturbances and noise)
= 100
Error suppressed
by 1+KP = 101
PM ≈ 60 deg.
Plant: SRF
Pulsed mode (~1 ms)
  Half Bandwidth ~ 200 Hz
  Latency ~ 2 μs
Plant: NRF
Pulsed mode (~ 1 ms)
  Half Bandwidth ~ 65 kHz
  Latency ~ 1.1 μs
x325
~ x 1/2
Controller
Cavity
Open loop
dP(t)
Plant

## Slide 13: Disturbances and Noise - Fast and Slow Distortions
Pre-Amp,
Klystron,…
Controller
r(t)
e(t)
du(t)
dP(t)
n(t)
yr(t)
yi(t)
ui(t)
ur(t)
Delay
Cavity
Plant
dy(t)
Many poster with focus on improvement
of subsystems and drift compensation
schemes
Other:
  Aging, switching in electronics (e.g. vans), ground motion and vibrations, faults in devices and components, thermal heating within macropulse, …
  Electromagnetic interference (EMI)
    F. Ludwig - Tutorial 2
  Drifts
    Talk: K. Shafak – Opt. synchronization
    C. Sydlo – Timing distribution XFEL
    M. Tikberidze - Laser2RF
    U. Mavric – CW DCM
Disturbance to plant input - du(t)
  DAC, vector modulator, temperature & humidity (PCB)
Disturbance to plant - dP(t)
  Pre-amplifier, Klystron, HV modulator, cavity length (water regulation), Beam (beam loading and multi bunch effects)
    M. Hoffmann – Meas.@REGAE
Noise – n(t)
  ADC distortions, noise, quantization noise, temperature & humidity (PCB)

## Slide 14: RF GUN Frequency Control @ FLASH
2 Control schemes
Water regulation (slow loop – sub-Hz)
  PI Control
  Sensor: IRIS Temp. (LP characteristic)
  Actuator: valve for cold mixing water
LLRF (fast loop - MHz)
  MIMO controller
  Sensor: virtual probe (Vforw and Vrefl)
  Actuator: input to Klystron
 Cascaded regulation scheme
Goal: Fast compensation of temperature drifts
 fast actuator
 fast sensor with high temperature resolution

## Slide 15: RF GUN Frequency Control @ FLASH
TIRIS and TIN are time delayed
Temperature estimation using LLRF highly suitable for control
 Frequency control by pulse width change
Idea: Estimate temp. by LLRF signals
LLRF based temp.
Resolution ~ 0.1 mK

## Slide 16: RF GUN Frequency Control @ FLASH
Detuning:
Kf/T = 21 kHz/K
QL = 10.000
f0 = 1.3 GHz
Resolution ~ 0.1 mK
(Sub-mK)
[K]
Pk2pk ~ 0.1K
[deg.]
Pk2pk ~ 0.4o
Pulsed mode
Pulse Width Modulation
to keep cavity on resonance
PWM off
NRF cavity as heater @ FLASH
Factor > 3 improvement
[K]
Pk2pk ~ 0.03K
[deg.]
Pk2pk ~ 0.17o
PWM on
Extremely precise frequency control is essential for all NRF cavities due to limited FB gain!
Same y-scaling for both panels

## Slide 17: Question?
Detuning:
Kf/T = 21 kHz/K
QL = 10.000
f0 = 1.3 GHz
Resolution ~ 0.1 mK
(Sub-mK)
[K]
Pk2pk ~ 0.1K
[deg.]
Pk2pk ~ 0.4o
Pulsed mode
Pulse Width Modulation
to keep cavity on resonance
PWM off
NRF cavity as heater @ FLASH
Factor > 3 improvement
[K]
Pk2pk ~ 0.03K
[deg.]
Pk2pk ~ 0.17o
PWM on
Extremely precise frequency control is essential for all NRF cavities due to limited FB gain!
Same y-scaling for both panels
Thank you for your attention!