## Slide 1: Status of accelerator facilities & ARD activities at DESY.
and overview who is doing what …
Holger Schlarb
3rd ARD – ST3 Workshop
KIT, 15-17.07.2015

## Slide 2: Content
FLASH - Free electron LASer at Hamburg FLASH
  sFLASH
  FLASH II
  FLASHForward
European XFEL
  AMTF
REGAE - Relativistic Electron Gun for Atomic Exploration
  LUX & LPWA@REGAE
SINBAD & ATHENAe  see talk from Barbara
AXSIS (not covered this time)
PETRA III (not covered this time)

## Slide 3: DESY activities : birds view …
FLASH
PETRA III
XFEL
FLASH2
CFEL
CSSB
nanoLab
AMTF
PETRA Extension N
PETRA Extension E
CMTB
SINBAD
REGAE
DESY II

## Slide 4: FLASH Layout
TESLA type superconducting accelerating modules 1.3 GHz
FLASH1 fixed gap undulators
3rd harmonic sc module 3.9 GHz
Normal conducting 1.3 GHz RF gun
Ce2Te cathode
Two Nd:YLF based ps photocathode lasers
FLASH1 Experimental Hall
Extraction to FLASH2
FLASH2 variable gap undulators
315 m
5 MeV
150 MeV
1250 MeV
Bunch Compressors
450 MeV
Accelerating Structures
RF Stations
Lasers
RF Gun
Soft X-ray Undulators
sFLASH
FEL Experiments
Photon Diagnostics
Beam Dump
THz
FLASH1
FLASH2
FLASH2 Experimental Hall
Albert Einstein
Kai Siegbahn
FLASH.
Free-Electron Laser
in Hamburg

## Slide 5: FLASH1 Parameters 2014 / 2015
more than 200 publications on photon science at FLASH, many in high impact journals
FEL Radiation Parameters
Wavelength range (fundamental) 4.2 – 52 nm Average single pulse energy 10 – 500 µJ Pulse duration (FWHM) < 50 – 200 fs Peak power (from av.) 1 – 3 GW Pulses per second 10 – 5000 Spectral width (FWHM) 0.3 - 2 % Photons per pulse 1011 – 1013 Average Brilliance 1017 – 1021 B* Peak Brilliance 1029 – 1031 B*
* photons/s/mrad2/mm2/0.1%bw
Energy (µJ)
Bunch number
FLASH.
Free-Electron Laser
in Hamburg

## Slide 6: FLASH 2015: Year of Celebrations
15 years of FEL lasing at DESY
  First lasing (109 nm) of Tesla Test Facility on Feb-22, 2000
10 years of SASE at FLASH
  First lasing (32 nm) of FLASH on Jan-14, 2005
10 years of FEL user operation at FLASH
  User operation started in summer 2005 as the first FEL user facility in VUV wavelengths worldwide
5 years of SASE in the water window at FLASH
  Lasing at 4.12 nm on Sep-25, 2010
1 year of simultaneous operation
  First lasing of FLASH2 (~ 40 nm) on Aug-20, 2014, FLASH1 lasing simultaneously with 250 pulses
FLASH.
Free-Electron Laser
in Hamburg

## Slide 7: FLASH: main issues & specialties & critical items
Availability and Reliability …statistics from 2014
Very frequent changing operation conditions (wavelength / pulse length / No bunches)
Experiment over 260h: SASE deliver 97%, tuning 11%, Down 2%
FLASH.
Free-Electron Laser
in Hamburg
New 2016: 10% of total beam time  ARD

## Slide 8: FLASH: main issues & specialties & critical items
RF gun & RF window & gun temp. stability
Beam feedbacks to stabilize operation (mandatory!!!)
Critical area
Quantum Efficiency of cathode over time
Required temp. stability <0.01°
FLASH.
Free-Electron Laser
in Hamburg
Critical
windows

## Slide 9: FLASH: main issues & specialties & critical items
Femtosecond stable optical reference distribution
Low Level RF System  MicroTCA
Link setup
BAM
FLASH.
Free-Electron Laser
in Hamburg

## Slide 10: Seeded FLASH: sFLASH
FLASH.
Free-Electron Laser
in Hamburg
External laser at UV (266nm) is used to seed FEL radiation in a single stage HGHG configuration
 Improve longitudinal coherence and control of radiation
First step: 7th harmonics  38 nm
Second step: Echo Enabled Harmonic Generation down to 12nm
Photon Diag.
Exp. hutch
HGHG Seeding at FLASH

## Slide 11: Seeded FLASH: sFLASH
FLASH.
Free-Electron Laser
in Hamburg

## Slide 12: Seeded FLASH: sFLASH
FLASH.
Free-Electron Laser
in Hamburg
Courtesy: J. Bödeward

## Slide 13: FLASH2
Extends user capacity: bunch train is shared between the two beamlines
Existing FLASH infrastructure up to last accelerating module used
Second undulator beamline and additional experimental hall constructed
Variable gap undulators allow wavelength changes at FLASH2 with a fixed electron beam energy
Expected FLASH2 Radiation Parameters
Wavelength range (fundamental) 4 – 60 nm Average single pulse energy 10 – 500 µJ Pulse duration (FWHM) < 50 – 200 fs Pulses per second 10 – 7000 *
* part of bunch train to FLASH1
FLASH.
Free-Electron Laser
in Hamburg

## Slide 14: FLASH2: Undulator Beamline
12 variable gap undulators
  period 31.4 mm
  K-value 0.5 – 2 (rms)
  segment length 2.5 m
FLASH.
Free-Electron Laser
in Hamburg

## Slide 15: FLASH2: Photon Diagnostics Beamline & Exp. hall
Spectrum
Profile
Beam position
Intensity Beam Position
Final version of photon diagnostics beamline in FLASH2 tunnel installed
Experimental Hall
FLASH.
Free-Electron Laser
in Hamburg

## Slide 16: FLASH2: Challenge by simultaneous operation
Fast kicker and Lambertson septum to extract a part of bunch train to FLASH2
Two injector lasers: FLASH1 and FLASH2 bunch pattern and bunch charge selected independently
Flexible RF-system: amplitude and phase adjusted - in certain limits - independently for FLASH1 and FLASH2
FLASH1
FLASH2
RF-pulse amplitude
300 μs
450 μs
FLASH1
RF-pulse flat-top 800 μs
30 μs (kicker)
99 ms (10 Hz rep.rate)
FLASH1
FLASH2
FLASH2
FLASH.
Free-Electron Laser
in Hamburg

## Slide 17: FLASHForward
Notes: DCM
SIS8300L2
REFM, RF Interferometer (?)
Smith Predictor
Decoupling of GUN/Buncher

## Slide 18: FLASHForward
Notes: DCM
SIS8300L2
REFM, RF Interferometer (?)
Smith Predictor
Decoupling of GUN/Buncher

## Slide 19: FLASHForward
Notes: DCM
SIS8300L2
REFM, RF Interferometer (?)
Smith Predictor
Decoupling of GUN/Buncher

## Slide 20: European XFEL at a Glance
Experimental Hall
Beam Dumps
Undulators
Collimation
Bunch
Compressors
Linear Accelerator
Injector
Photon Beam Lines
Electron Beam
Distribution
17.5 GeV superconducting linac, almost 1 MW beam power
27000 pulses per second in 10 Hz burst mode
Three moveable gap undulators for hard and soft X-rays
Initially 6 equipped experiments
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 21: Electron Beam Parameters / Photon energies
Quantity | Value
pulse repetition rate | 10 Hz
beam pulse length | 600 ms
bunch repetition frequency within pulse | 4.5 MHz
electron bunch length after compression | 2 – 180 fs (FWHM)
bunch charge | 0.02 – 1 nC
slice emittance | 0.4 - 1.0 mm mrad
slice energy spread | 4 – 2 MeV

## Slide 22: Many accelerator components produced

## Slide 23: … and installed
Gun conditioned at PITZ/DESY
RF operation at XFEL December 2013

## Slide 24: Finished first accelerator section (L1)

## Slide 25: Finished first accelerator section (L1)

## Slide 26: Production now on full speed …
High power RF couplers
Accelerator Modules Production & Delivery
Accelerator Module Test Facility (AMTF)
21 day, now
14 days

## Slide 27: Photon systems
August 2013

## Slide 28: Undulator Production and Tuning
Total 91 segments
> 95% measured and tuned
Installation SASE 1: 12/2015

## Slide 29: Detectors and Laser systmes
Detector
  development
200
1
10
Pixel Size [μm]
20
2
Photon Energy [keV]
200
Fast CCD
MCP
GotthardV2
pnCCD
AGIPD
DSSC
LPD
4.5 MHz
500
75
50
30
Each SASE equipped with one pump-probe laser
  R&D to overcome lack of commercially available systems
  All essential features met: pulse length & power, pulse pattern and random pulse selection, wavelength tuning, diffraction-limited laser beam
Have to fit to time structure

## Slide 30: Beam Commissioning and Parallel Operation
2015
2016
2018
First e-beam out of RF gun installed at XFEL
Injector cooldown
Injector com. up to full XFEL performance (varying charges and bunch patterns)
Linac cooldown
SA1
Initial linac com. with reduced performance
Start user operation
Full TDR performance
Continued accelerator com. to full performance (high beam power, bunch length flexibility, multiple bunch properties per rf-pulse, full wavelength tuneability, ….)
Beam line and experiment com.
1st lasing possible
SA3
SA2
Gun and injector laser com.
. First user operation
e-
g
2017

## Slide 31: REGAE - Relativistic Electron Gun for Atomic Exploration
Electron source for time resolved electron diffraction experiments Prof. Dwayne Miller, CFEL
  Coherence length of electron
  Typical diffraction pattern
  In pump-probe configuration
Lc ~ 10 nm for solid states
Lc ~ 30 nm length for proteins
n ~ 10 nm
Dwayne Miller et al. Nature 468, Nov. 2010
External injection in plasma bubble:
  Laser Plasma Wakefield Acceleration
  Florian Grüner und Andreas Meyer CFEL

## Slide 32: REGAE stability: Temperature control of acc. structures
RF-Gun Cavity
3 GHz S-Band
Gradient on cathode
≥ 110MV/m
50 Hz rep Rate
~5 µs pulse length
Buncher Cavity
3 GHz S-Band
4-cells
average gradient
~15-20 MV/m
Velocity bunching
7 fs

## Slide 33: REGAE - Relativistic Electron Gun for Atomic Exploration
Stability requirements
dA/A < 0.01 %
dφ < 0.01 deg.
RF System
New!
Trms~380uK rms
Cooling system for cavities
LLRF
dφ rms < 10mdeg achieved for RF gun!

## Slide 34: REGAE – LUX & LPWA@REGAE
High power laser
Incoupling
LUX beamline schematics
REGAE

## Slide 35
Thanks for your attention
Notes: DCM
SIS8300L2
REFM, RF Interferometer (?)
Smith Predictor
Decoupling of GUN/Buncher