## Slide 1
M. Titberidze, F. Grüner, B. Zeitler, University of Hamburg, CFEL, Hamburg, Germany H. Schlarb, M. Felber, T. Lamb, C. Sydlo, DESY, Hamburg, Germany
General Layout of REGAE Facility
Measurement setup of MZM based L2RF Synchronization System & Results.
Current DWC based synchronization system.
Laser-to-RF conversion for Titanium Sapphire Lasers.
contact: mikheil.titberidze@desy.de
3rd ARD ST3 workshop
Long term performance of the DWC based synchronization setup is in the order of several ps.
It is limited by AM/PM effects and influenced by environmental conditions.
Relativistic Electron Gun for Atomic Exploration (REGAE) is an S-band normal conducting RF Accelerator which generates ~ 10 fs duration electron bunches.
Currently, REGAE is used for Ultrafast Electron Diffraction (UED) experiments and will be used for planned Laser driven plasma acceleration experiments.
Both experiments require very precise Laser-to-RF sub-50 fs long term timing stability.
Average Beam Energy | 5.6 MeV
Energy Spread | 20 keV
Bunch Charge | 100 fC
Bunch Length | 7 fs (rms)
Transverse Beam Size | 3.2 μm
Transverse Emittance | 30 nm
New MZM based synchronization system.
The idea is, to take the incoming laser pulse train and to split it into two beams.
After splitting, a time delay is introduced to one of the pulse trains.
Laser pulses should arrive on opposite slopes of the RF.
In this particular case the time delay T=Tlaser/8 ~ 1.5 ns.
Using MZM any phase error is converted to amplitude modulation which can be detected.
It is virtually optical power fluctuation insensitive and eliminates AM to PM conversion.
Intrinsic detector stability without RF Trms = 4.1 fsec