## Slide 1: Strip CMOS progress meeting, Introduction, 2015-04-28
Have several things to discuss/announce:
TWEPP abstract
How do we deal with other abstracts?
(There was iWoRID request from Glasgow. We’ll surely have more…)
Solicitation from G. Iacobucci.
CHESS-2 design review.

## Slide 2: TWEPP Abstract
TITLE: Development on CMOS MAPS devices for the ATLAS Phase-II Strip Tracker Upgrade
TWEPP ABSTRACT (max 100 words)
ATLAS is currently studying the use of CMOS MAPS devices as a replacement for the baseline silicon strip sensors for the Phase-II Strip Tracker Upgrade. One of the key aspects is to establish whether the radiation hardness is suitable for the HL-LHC environment. Two different technologies are being studied: High-Voltage CMOS and High-Resistivity CMOS. Several test chips have already been manufactured. We present the latest results from non-irradiated and irradiated sensors including test beam results and give an outlook on the next steps.
TWEPP SUMMARY (max 500 words)
ATLAS is currently studying the use of CMOS MAPS devices as a replacement for the baseline silicon strip sensors for the Phase-II Strip Tracker Upgrade. In order to minimize the impact on the overall tracker design, a CMOS alternative sensor has to result in minimal changes to the rest of the detector. Hence ATLAS is investigating devices with long pixels which are grouped to form a virtual strip with binary-encoded z-information. Key requirements are to establish whether the radiation hardness is suitable for the HL-LHC environment, that the charge collection speed is sufficient for 25 ns bunch crossing operation, and whether the encoded z-hit design can be compatible with full-reticule size sensors.
Several test chips have been submitted using two different CMOS technologies. The AMS HV-CMOS 350 is a special process, which makes it possible to bias the sensor with up to 120 V, while the TowerJazz 180 nm HR-CMOS process uses a high resistivity epitaxial layer to speed up the charge collection. Several groups have taken part in understanding the performance of these sensors including charge collection, output signal timing, gain and noise. We present these results and also results from the irradiation campaigns with photons, neutrons and protons, which strongly support the radiation tolerance of these devices to radiation dose of the HL-LHC (60 Mrad and 2x10^15 neq/cm^2). We also show first test beam results of these devices .
Our next chip features a full-reticle length sensor. It is designed for prototyping the readout architecture and to assess large-chip effects, such as common mode noise. The hit encoding engine is capable of reading out up to 8 hits from a pre-defined region. The hits are then transferred for off-sensor readout via 320 MHz bus that runs at 8 times the bunch crossing frequency. Placement of the comparators and the bulk wafer resistivity will be varied to optimize the performance.
To conclude we give an overview of the upcoming plans for ATLAS strip CMOS detectors, including a detailed description of the first large-size chip which is going to be available for fall 2015.
Written by Marcel, modified by Richard N., Vitaliy, Todd, Richard B.
The deadline is April 30 => the last chance for comments is tomorrow.

## Slide 3: Other abstracts/talks/presentations (E.g. there is Richard Bates’s request for iWoRID)
Propose a simple approval process:
Presentation/briefing at the CMOS progress meeting or circulation via email list
Approval by Richard/Marcel/Vitaliy

## Slide 4: Other CMOS project
G. Iacobucci is soliciting collaboration from strip CMOS community for fully-monolithic CMOS development:
https://indico.cern.ch/event/387388/contribution/5/material/slides/0.pdf http://arxiv.org/pdf/1408.5536v1.pdf
As I understand it:
  Based on Mu3e experiment’s chip, in AMS H18
  To have 3 triplet layers in strips volume.
  Currently have Geneva/Liverpool/Heidelberg/Karlsruhe participating.
  They could use help for chip testing/beamtests/simulations/modules.

## Slide 5: CHESS-2 Design Review
Doodle poll for the 1st CHESS-2 review converged on May 4th, at 16:00 CERN time (7am CA) .
Connection details:
Here is the indico link, with the agenda to be filled in as it develops: https://indico.desy.de/conferenceDisplay.py?confId=12358 We can use our standard Vidyo connection: Auto-join Vidyo URL : http://vidyoportal.cern.ch/flex.html?roomdirect.html&key=VzILMDp484zc Room name : ATLAS_Strips_CMOS_meeting Extension : 109322183