## Slide 1: MCH-RTM-BM Status
Michael Fenner
Warsaw, 10.06.2014

## Slide 2: MCH-RTM-BM Status
Passed tests, general
  Power supply via Zone3 (MCH) and power supply via Zone2 (RPM)
  Programming of Atmel, NAT-MachXO, Ethernet Controller
  ComExpess module ok
  USB, Display Port, Ethernet interfaces at face plate
  PCIe to Ethernet controller, Ethernet link via Ethernet controller
  Temperature reporting via I2C - OS
  Boot via SATA connection
Passed Tests, ZYNQ:
  Programing of MachXO via programming connector
  Programming via MCH firmware does not work  Redesign v1.1
  Output voltage range of Zynq related DC-DC converters
  I2C Buffer and pull resistors for RF Backplane are switched on
  DRAM Test
Open:
  Firmware integration on MCH side
  Missing: System Integration – nobody responsible
  Board is broken and sent to repair (0.5mm Pitch BGA)
  Boot from SPI Flash did not work yet
  PM functionality for eRTM15: - Not tested!
Furher work now happening on „MicroZed Board“