## Slide 1: Status of test kit 12 May 2015
J. J. John with help from many others

## Slide 2
AMS-CHESS-1 daughterboard
Bias distribution revised following review – somewhat time-consuming.
We felt it best to be quite careful with revising the layout, due to the limited number of chips available.
The board will go out for quoting tomorrow and I will send it to Dima, Jens, Todd, Hervé and Forest (UCSC) for a last check.
CHESS-1 hardware design

## Slide 3
TJ-CHESS-1 daughterboard
PonP layout in progress.
Initial footprint was not feasible to track out. Ok in isolation but not when all pads present.
Working on new footprint using continuous “bars” of bond pad, for ground, power supplies and biases.
CHESS-1 hardware design

## Slide 4
Motherboard
Schematics in progress. See block diagram on next slide.
Draft attached to DESY Indico page for today.
CHESS-1 hardware design

## Slide 5
4
SPI
4
SPI
4
CHESS-1 motherboard block diagram
Samtec MEC6-150-02-L-D-RA1
100 position socket for edge connector
= interface to 3 variants of daughterboard
ADG714
octal switch #1
ADG714
octal switch #2
ADG714
octal switch #10
analogue outputs
8
8
8
SPI
LMH6559
Buffer #1
LMH6559
Buffer #2
LMH6559
Buffer #10
analogue outputs
1
1
1
SMA #1
SMA #2
SMA #10
DAC128s085
octal voltage DAC
7
SMA #11
analogue input
voltage
biases
SPI
4
4
SPI
4
SPI
4
SPI
Molex 71430-0013
68 position VHDCI receptacle
= interface to DAQ = Digilent Atlys FPGA board
LM4132
voltage reference
LP3964EMP-1.8
1.8V regulator
LP3964EMP-3.3
3.3V regulator
LP3964EMP-5
5V regulator
LT1964-5
-5V regulator
+7V in
-7V in
ground
(4mm sockets)