## Slide 1: Optimizing the built-in amplifier in HV-CMOS CHESS1
Vitaliy Fadeyev, Zach Galloway , Herve Grabas
Alexander Grillo , Zhijun Liang , Abe Seiden
Jennifer Volk, Forest Martinez-Mckinney
University of California, Santa Cruz

## Slide 2: Isolated amplifier in CHESS1 chip
HV-CMOS CHESS1 chip has built-in isolated amplifiers
designed to optimize amplifier performance
  Six amplifier biasing control
  Optimization can be done with pulser, without using laser injection or beta source.
  Change its gain and output signal shape by changing biasing control
Try to study the amplifier performance as input to CHESS2 design

## Slide 3: Amplifier Biasing
iN
Vpload
Casc
INSF
iFB
Casc -Cascode bias
iNSF – Source Follower Bias
iN – Amplifier current source bias
VPLoad – Amplifier Resistive Load bias
iNBias – Nwell resistive path bias
iPFB – Feedback current bias

## Slide 4: Setup to test amplifier performance
Chess1 chip
iBias
iFB
iNSF
iN
Casc
Vpload
Input to amplifier
output
Home grown test board Forest built
To test CHESS1 chip

## Slide 5: Setup to test amplifier performance
Isolated Amplifier on CHESS1 chip
Pulser
Scope
Input pulse
Amplifier output
Voltage source
3.3V bias for amplifier
Time (s)
Voltage (V)
Voltage (V)
Source follower
50fF coupling capacitance
Falling edge

## Slide 6: 4 configuration of amplifier setting
  Keep iBias,Cacs, Vpload, iN constant
    iBias=0.34V. Cacs =2.6V, Vpload=2.1V, iN=1.4
  Varying iFB and iNSF to optimize the performance
  Config1:
    iFB=2.664V, iNSF=0.569V
  Config 2
    iFB=2.597V,iNSF=0.576V
  Config 3
    iFB=2.71V,iNSF=0.766V
  Config 4
    iFB=2.682V,iNSF=0.566V

## Slide 7: Output pulse Vs input charge
Time (s)
Output (V)
Time (s)
Output (V)
Time (s)
Time (s)
Output (V)
Output (V)
config1
config2
config4
config3

## Slide 8: Gain Vs signal size
Assuming Gain=V_out/Q_in
gain is designed to be 500 mV/fC
  Measured gain is higher
Config 2 is bad for small signal
Gain (mV/fC)
Input charge ( k e-)
Input charge ( k e-)
Output (mV)

## Slide 9: Amplifier Noise
Noise of the amplifier (upper limit) can be estimated by measuring the event-by-event variation in signal peak
Output (V)
Time (s)
Input =1mV
Charge ?
Config 1
Different color is
From different events
8mV output noise
750 mV/fc measured gain for 1mV signal
66.5 e- measured input noise
<100 e- input noise expected
Output at peak (V)
count

## Slide 10: Amplifier Noise
  Input Noise : 40~80 e- (<100 e- expected)
Input charge (k e-)
Input Noise (e-)

## Slide 11: Amplifier output signal rise time
Output signal rise time(s)
Input =0.3k e-
Config 1
Rise time =30ns
Output signal rise time(s)
Input =1.5k e-
Config 1
Rise time =13ns
Output signal rise time(s)
Input =3.1k e-
Config 1
Rise=25ns
Pulser input signal has 9ns rise time
Amplifier output Rise time (10%-90%) vary between 13ns – 30ns
  Depending on the input signal amplitude

## Slide 12: Amplifier output signal rise time
Rise time : 10~30 ns depending on signal size
Full width at half maximum is from 80ns ~360ns depending on signal size.
Input charge (k e-)
Rise time (ns)
Config 1
FWHM(ns)
Input charge (k e-)
Config 1

## Slide 13: Summary
first exercise on optimizing the built-in CMOS based amplifier in CHESS1 chip
  As input to CHESS2 active array design
Measured Amplifier performance
  Gain : 500 ~ 1300mV/fC ( 500 mV/fc is expected)
  Input Noise : 40~80 e- (<100 e- expected)
    Input noise is good
    But It is measured in isolated amplifier without sensor
    It may be nosier in real detector
  Rise time : 10~30 ns depending on signal size (15ns expected)
  Full width at half maximum is from 80ns ~360ns depending on signal size.
Configuration 1 gave the best performance
  Best balance between gain and output signal shape.
  iBias=0.34V. Cacs =2.6V, Vpload=2.1V, iN=1.4
  iFB=2.664V, iNSF=0.569V
Next steps:
  Try to reduce power consumption by reducing Amplifier current source bias(iN)
  Study signal to noise using laser injection in active pixel array