## Slide 1: HWR Cavities for China ADS
Weiming Yue, Yongming Li
On behalf of Linac Center
Institute of Modern Physics
Chinese Academy of Sciences
TTC, 2th December, 2015 SLAC

## Slide 2: Contents
Introduction of background
RF design
Mechanical Study Results
Fabrication
Vertical test result

## Slide 3: Motivation
~3 mA ion
10 mA H+
ADS
HIAF
Cooperated with IHEP
Neutron Source ~10mA D+

## Slide 4: SC Cavity developed at IMP
162.5 MHz HWR015
1.3 GHz Single-cell

## Slide 5: Physics design of ADS injector II

## Slide 6: HWR 010
f (MHz) | 162.5
βopt | 0.101
Epeak / Eacc | 5.9
Bpeak / Eacc | 12.1
G = Rs×Q0 (Ω) | 28.4
R / Q0 | 153
Q0 (4.4K, Rs=71.4 nΩ) | 4E8
Vacc (MV) | 0.78
Epeak (MV/m) | 25
Bpeak (mT) | 50
Pdiss(W) (4.4K, Rs=71.4nΩ) | 10
RF Parameters
models

## Slide 7: HWR010 Mechanical Analysis
Pressure Sensitivity：— 5.657Hz/mbar
Pressure Sensitivity ：— 1 Hz/mbar
Test result: Pressure sensitivity 20 Hz/mbar
Pressure Sensitivity
Tuner R&D
Tuning range >200Hz @4.2K

## Slide 8: Beam Condition
ECRIS + LEBT + RFQ + MEBT + TCM1, 2.5 MeV
RFQ commissioning, validate CM design.
Feb. 13th, 2015, 2.55 MeV/11 mA/CW
162.5 MHz HWR010
ECRIS+LEBT+RFQ+MEBT+CM6, 5 MeV
Dec 28th, 2015, 4.6 MeV/4 mA/CW
limitation is the RFQ Power source
162.5 MHz HWR010

## Slide 9: HWR015 EM Design
f(MHz) | βopt | Emax/Eacc | Bmax/Eacc (mT/(MV/m)) | R/Q0 (Ω) | G(Ω)
162.41 | 0.15 | 4.8 | 6.1 | 292 | 51
f(MHz) | 162.5
Vacc(MV) | 1.8
Bpeak(mT) | 40
Epeak(MV/m) | 32
R/Q(Ω) | 292
G（Ω） | 51
Eacc(MV/m) | 6.6
P(W)(Rs=70nΩ) | 16
βopt | 0.15
Q0 | 7.2E+08
EM Results
Design Goal
Notes: 9

## Slide 10: Mechanical analysis
Fixed the beam port
Free the beam port
B-field: 6.07Hz/mbar
E-field: -4.02Hz/mbar
Fixed the outer
conductor
Fixed the inner
conductor

## Slide 11: Preparation and test of #02 HWR
The final results with Helium Vessel will be given after further optimization.
Cavity parameter | Without ribs | With ribs | Test with ribs
Frequency (MHz) | 162.5 |  | 
Bandwith (Hz) | 243 |  | 
Pressure Sens. (Hz/mbar) Free the beam port | -32.7 | -26 | -21
Pressure Sens. (Hz/mbar) Fixed the beam port | 2.09 | 0.82 | 

## Slide 12: Fabrication
Four HWR015s Fabricated in two companies
  #01, #02 in Ningxia
  #03, #04 in Haerbin
Material
  OTIC，RRR>300，partly RRR>380
Drawing, machining and BCP
  Punching die，Al 7075
  Surface survey before every step of fabrication
  BCP (65%HNO3:40%HF:85%H3PO4=1:1:2) 10um, resin by UPW, drying in cleanroom of class 100，before EBW
  Polishing every weld seam after EBW

## Slide 13: Fabrication
Haerbin
Ningxia

## Slide 14: Processing
Ultrasonic
rinsing
BCP
6h
130um
Annealing 850℃, 3h
BCP
50min
12um
Ultrasonic
rinsing
Clean room class100
Drying 24h
Clean room class100 assembly
HPR
84bar
7h
Pumping and leak checking
baking120℃，50h

## Slide 15: Vertical test

## Slide 16: Summary
The fabrication and treatment of HWRs have been qualified by Vertical testing.
The df/dp test result is larger than the simulation result, The final results with Helium Vessel will be given after further optimization.
The helium Vessel and Tuner are being constructed now.
HWR010 Cavities has passed the 10mA beams

## Slide 17: Thanks for your attention!