## Slide 1
TTC Meeting at SLAC – 03 november 2015
Tuner development at IPNO : Spiral2 and ESS
N. Gandolfo

## Slide 2
Outline
Part 1 : Spiral 2 plunger tuner for b=0.12 QWR
  Tuner principle
  Successfully testing 7 cryomodules
  Technical issues
Part 2 : ESS piezo tuner for b=0.5 Spoke cavities
  Tuner principle
  2015, a year of testing
  Technical issues
Future plans
Tuner development at IPNO : Spiral2 and ESS

## Slide 3
Ambient air
Thermal insulation vacuum
LHe
Room temperature motorization
Provided Motion
Nb Cavity
Ti LHe vessel
Nb Plunger (actively cooled)
Sliding parts
An external motorization provides motion to a Nb plunger that is moving up and down inside the cavity.
Tuning sensitivity : ~1 kHz/mm
Nominal stroke : 10 mm
Nb Plunger
D. Longuevergne & al. "A Cold Tuner System With Mobile Plunger ". SRF’13.
Spiral2 tuner : Working principle

## Slide 4
Status : 14 cavities + tuners inside 7 cryomodules successfully tested at IPNO prior transport in tunnel at GANIL (France) (last cryomodule tested last December)
Note : MB05 and MB06 were equipped with prototype parts of the tuner, this explain why the range seems shifted compared to the others, and why it goes negative also.
On some tuners, the first 2 millimeters show a slope slightly different.
Spiral2 tuner : Scope on results
Tuning sensitivity of 14 tuners

## Slide 5
Spiral2 tuner : Back and forth tilting issue
2
1
1
3
2
4
3
4
Motor command (normalized in Hz)
Frequency shift (Hz)
During small displacement operation, for instances in a regulation mode while the tuner tracks the nominal frequency, a non-linearity (overshoot, hysteresis,… difficult to find an appropriate name) of the system occurs each time the direction of the motion is changed.
On Spiral2 b=0.12 cavities the bandwidth is around 88 Hz
Sometimes the measured overshoot exceeded 100 Hz !
df (Hz)
overshoot

## Slide 6
Spiral2 tuner : Tilting issue whole story
[fall 2010] Problem detected, during DLLRF trials on the 1/7 series cryomodule qualification
Confirmed on 2nd cryomodules : 4/4 tuners failed
Trying to look the problem at room temperature by a lot of different ways :
  Frequency reading : not accurate enough due to large Q
  Position sensors : mechanical access difficult
Put both prototype and series tuners on a table, play at “find the differences” game
Trying improve mechanical assembly and parts : some improvement but not enough.
Take the problem in another way : If we don’t know why the series tuner fails, let’s understand why the prototype tuner worked ?
Re-test one of the first prototype tuner that "worked": problem appeared also
Prototype tuner was not qualified on small displacement, only large one (1k Hz steps) so maybe the problem was here and not seen …back again in the start position
Find a way to track the resonant frequency at room temperature with a precision around 1 Hz : Found it ! (using a lock in amplifier and a useful guy (thanks D. Longuevergne))
Suspecting a tilt of the plunger  Proven it with a laser pointer
Reduce the tilt : Not possible, due to residual play necessary inside the stainless steel guides.
Discover that the tilt direction have an incidence on the frequency hysteresis.
Modifying the position of the guides (related to the cavity support flange) : It works ! But not really at each assembly…
Applying systematic frequency measurement loop after cavity+coupler+tuner assembly, prior finishing to assemble cryomodule to verify the tuner is OK
And most important thing : practice extensive test of the tuners with large and low displacement and check hysteresis at different tuner positions
2 years

## Slide 7
ESS tuner
Second part : ESS tuner

## Slide 8
A ball screw system driven by a stepper motor acts on a double lever arm mechanism to provide a significantly reduced displacement of the cavity flange along the beam axis.
Vacuum
Motor
Ball screw (p = 2 mm)
Rods
Flange frame
Cavity flange
Lever arm (D/d = 10)
Bellow
LHe bath
Cavity vacuum
Insulation vacuum
Slow tuner principle
D
d
Cavity body
LHe vessel
N. Gandolfo & al. "Deformation Tuner Design for a Double Spoke Cavity". SRF’13.
ESS tuner : Working principle

## Slide 9
ESS tuner : 2015, a year of testing
First tuner version
Second tuner version
« only » modification : allow to put longer piezo 50 mm  90 mm

## Slide 10
Thermal improvement to accelerate cooling down
09 feb.
10 feb.
11 feb.
12 feb.
w/o thermal braids
Nearly 3 days to reach T<50 K
Chart: 
w/ thermal braids
After putting copper 16 copper braids, most of the tuner was under 30 K within a day (except motor and ballscrew which are the hottest spot) and stabilize between 10 and 20 K over few days
T(K)
Time (hours)
ESS tuner : Cooling down
Copper braids
Top of the cavity (vertical position) equipped with the tuner

## Slide 11
Chart: 
| -2 | 18 | 37 | 57 | 77 | 97 | 117 | 137 | 157 | 178 | 196 | 178 | 157 | 137 | 117 | 97 | 77 | 57 | 37 | 17 | -2 | -22 | -42 | -62 | -82 | -102 | -121 | -141 | -164 | -184 | -203 | -184 | -164 | -141 | -121 | -101 | -82 | -62 | -42 | -22 | -2 | 18 | 37 | 57 | 77 | 97 | 117 | 137 | 157 | 178 | 196
P2 Noliac 50 mm | 424 | 446 | 471 | 495 | 522 | 551 | 579 | 609 | 644 | 680 | 717 | 695 | 675 | 648 | 623 | 597 | 564 | 533 | 504 | 466 | 434 | 399 | 362 | 323 | 281 | 241 | 194 | 150 | 93 | 45 | 0 | 15 | 41 | 67 | 89 | 118 | 144 | 171 | 200 | 233 | 269 | 301 | 339 | 380 | 422 | 467 | 511 | 559 | 609 | 663 | 713
P1 Noliac 50 mm | 588 | 613 | 645 | 679 | 713 | 745 | 784 | 819 | 868 | 915 | 953 | 934 | 901 | 868 | 834 | 797 | 760 | 722 | 682 | 642 | 598 | 550 | 500 | 451 | 397 | 337 | 277 | 222 | 138 | 68 | 0 | 26 | 56 | 90 | 124 | 160 | 196 | 232 | 275 | 314 | 360 | 406 | 458 | 510 | 567 | 626 | 686 | 748 | 814 | 886 | 944
df (Hz)
Piezo voltage (V)
ESS tuner : Piezo detuning measurement @2K
Systematic difference depending on the piezo location on the tuner, due to asymmetric mechanical architecture has been observed on every tests

## Slide 12
Nominal no load stroke : 136.4 µm
Measured stroke @300K : 110 µm
Measured stroke @77K : 24 µm
Measured stroke @30K : 15 µm
Piezo breakdown occurred accidentally probably due to vacuum  a.p. transition (while injecting nitrogen gas).
Excitation voltage over time
90 mm Noliac piezo equipped with strain gage sensor
Piezo breakdown
T = 100 s
Piezo cycle measurement during warming up the cryostat for 3 days
Piezo after breakdown, no visible damage, 3 ohm resistance, < 0.1 nF capacitance
Unipolar operation 0200 V
ESS tuner : Piezo strain measurement 30K  300K
Breakdown during test (around 260K)

## Slide 13
Chart: 
0200V 14 Hz sine drive : 85 K reached in 2 hours
At room temperature, piezo voltage for nominal operation must remain quasi-unipolar.
At low temperature (77K and below), it is possible to operate them at full bipolar voltages, in order to obtain higher strain.
Test with 14Hz sine drive show that self-heating warm the piezo above the 77K limit.
POWER ON
POWER OFF
Time (min)
T(K)
www.noliac.com
ESS tuner : Piezo self-heating measurement
dT= 50K

## Slide 14
Chart: 
300K | 0 | 0.238 | 0.476 | 0.555 | 4.206 | 6.984 | 10.317 | 13.968 | 17.222 | 13.492 | 10.238 | 6.666 | 4.127 | 1.269 | 0 | 0.079 | 0
Chart: 
Tuner #3 on cavity #2
Two problems occured on 3/3 low temperature tests :
Problem of large hysteresis (graph 1 and 2)
Problem of tuner getting stuck (graph 3)
Never observed on the first version (tuner #1 and #2)
ESS tuner : Slow tuner issue on second version
Motor displacement (mm)
Motor displacement (mm)
df (kHz)
df (kHz)
Chart: 
Motor displacement (mm)
df (kHz)
Tuner #3 on cavity #1
Tuner #4 on cavity #1
STUCK !
Graph 1
Graph 2
Graph 3

## Slide 15
Putting both version disassembled on a table for detailed check.
From few differences observed, one has been keeping our attention.
The largest bearing (spherical roller bearings) were not provided by the same supplier for both version, and for the second version, significant amount of residual oil was seen on the rolling elements.
Liquid nitrogen test of both version revealed the following :
- On the first version, bearing were rolling but with significant friction torque. [A]
- On the second version, bearing were not rolling, they were completely stuck. [B]
Degreased them with ultrasonic cleaner and Tycopur for few minutes.
At room temperature : Bearings are ok even if they sounds no happy.
In nitrogen liquid : Bearing are rolling, even slightly better than the first version. [C]
Next steps :
1- Test second version tuner with cleaned bearing to verify the origin of the problem
2- Looking now for dry lubrication methods to apply on actual bearing… or replacement for already dry lubricated bearing. WS2 ? MoS2 ? Graphite ? PTFE ?
ESS tuner : Slow tuner issue on second version
1st version
2nd version
A
B
C

## Slide 16
Spiral2 : Waiting for the first cooling down of the linac, scheduled for early 2016
ESS :
Investigate the inefficiency of the long piezo
Solve the problem of tuner getting stuck / hysteresis, improve bearing lubrication
Solve the piezo over-heating issue : Thermalizing piezo ? Using only unipolar operation ?
Prepare for mass production (2016..)
Also, developing a dedicated test bench (maybe low temperature capable) to qualify each tuner prior cryomodule assembly may be envisaged
R&D :
Extensive test of piezos on a dedicated compression test bench, low to room temperature characterization + lifetime test at LN2 temperature
Test a system of disengagement (recent development) to provide cavity safety against motor failure
Future plans
Thank you

## Slide 17
Back up slides

## Slide 18
Low displacement measurement (first tuner version)
Sample of low motion back and forth to check hysteresis :
around 12 Hz for 0.01 mm motor position ( eq. ~ 694 Hz shift)
Time (s)

## Slide 19
ESS Spoke tuner overview
Stepper motor
Piezo electric actuators (x2)
Stainless steel ball screw with MoS2 lubrication
Working principle :
A ball screw system driven by a stepper motor acts on a double lever arm mechanism to provide a significantly reduced displacement of the cavity flange along the beam axis.
Protection tube (Aluminum)
Top part (AISI 316L)
Ceramic ball (ZrO2)
Piezo
Special encapsulation design to protect the piezo stacks and ease the assembly
N. Gandolfo & al. "Deformation Tuner Design for a Double Spoke Cavity". SRF’13.

## Slide 20
Tuning sensitivity of ESS first version tuners
Chart: Tuning sensitivity ZA01
Fit 2K | 39.459 | 39.021 | 38.592 | 38.201 | 37.792 | 37.305 | 36.789 | 36.257 | 35.722 | 35.196 | 34.665 | 34.133 | 33.599 | 33.065 | 32.53 | 32.172 | 32.167 | 32.117 | 31.652 | 31.116 | 30.578 | 30.055 | 29.532 | 29.008 | 28.478 | 27.945 | 27.417 | 26.896 | 26.379 | 25.859 | 25.343 | 24.825 | 24.302
Fit 4K | 47.468 | 47.471 | 47.338 | 46.808 | 46.264 | 45.716 | 45.171 | 44.628 | 44.086 | 43.541 | 42.997 | 42.451 | 41.92 | 41.391 | 40.859 | 40.322 | 39.785 | 39.452 | 39.457 | 39.443 | 39.455 | 39.451 | 39.449 | 39.25 | 38.71 | 38.173 | 37.64 | 37.107 | 36.575 | 36.044 | 35.507 | 34.973 | 34.44 | 33.903 | 33.373 | 32.847 | 32.313 | 31.785 | 31.542 | 31.543 | 31.537 | 31.538 | 31.539
Chart: Tuning sensitivity ZA02
Fréquence relative @2K (kHz) | 45.204 | 36.503 | 27.275 | 18.449 | 10.224
Fréquence relative @2K (kHz) | 0 | 0.046 | 3.157 | 7.183 | 11.422 | 15.701 | 20.06 | 24.569 | 29.484 | 36.69 | 45.204 | 36.503 | 27.275 | 18.449 | 10.224 | 3.197 | 0.216 | 0.216 | -0.02 | -0.023 | -0.023

## Slide 21
Magnetic field distribution on b=0.12 Spiral2 QRW

## Slide 22: Thermal shrink fit coupling
Introduction : During operation, part of the cavity body is highly stressed (up to 311 MPa) by the tuner action, much far away from the ambient temperature elasticity limit (around 40 MPa). This can lead to cavity damage risk in a case where the tuner is stuck.
Goal : Get the possibility to release the cavity from the tuner prior any warming-up, even in case of failure of motor/gearbox/ballscrew.
Idea : Put inside the tuner a shrink fit coupler that rely on association of two different materials to :
Release the system at above a temperature (> Thigh)
Couple the system at low temperature (< Tlow)
A heater located on the outside member would provide heating to the whole assembly.

## Slide 23
Compression test bench