## Slide 1: European-XFEL tuners
Review of quality control strategy
Rocco Paparella
On behalf of WP07-Tuner group
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)

## Slide 2: The XFEL Tuning System
Main linac
  Double asymmetric leverage
  Cold stepper motor with HD gearbox
  Cold piezo actuators
    Fast action introduced for TTF by DESY
    Two stacks in a single preloading frame
Third-Harmonic module
  Tuners are a scaled replica of ILC coaxial Blade Tuners
  Same motor drive unit than main linac
  No piezo: moderate gradient and LFD sensitivity.

## Slide 3: Starting point
Priceless experience at DESY with TTF/FLASH, cold piezo and motors since almost two decades
    Qualifications from R&D, specially on piezo
      Radiation hardness: http://accelconf.web.cern.ch/AccelConf/e06/PAPERS/MOPCH144.PDF
      Cryogenic performances: http://cdsweb.cern.ch/record/943229/files/care-conf-05-022.pdf
      Life-time, unipolar: http://wwwsrf.mi.infn.it/publications/papers/2005/file/note-2005-020-SRF.pdf
      Life-time, bipolar: INFN, DESY, to be published soon
  Currently at FLASH:
    7 CMs with 8 cavity each, same tuners than XFEL:
      LFD compensation routinely operated, up to +35 MV/m
        FeedForward scheme, single pulse
        Single piezo used, second as sensor or for redundancy
        4 piezo failures recorded, out of standard operations
          During DC scan, fast transition from -70 to + 70 V
          Other piezo driver related events
      piezo and motors from different vendors already in use

## Slide 4: Key choices - Before CFTs
Tuner performances already assessed, focus should be on preservation of manufacturing and assembling quality with industrialization.
Minimize the number of parts to be procured. Tuner systems divided into three main subsets:
    Mechanics: leverage, joints
    Drive unit: motor, gearbox, shaft and nut
    Piezo system: piezos, frame
Get the most out of industrial partner know-how
  i.e.: let piezo company assemble piezo system, so for motors
  Subsets parts delivered as “ready-to-use” at CEA
Competition between vendors, test at labs on prototypes
  At least 2 companies for each subset to be qualified by DESY
Introduce an additional QC upon tuner assembly at CEA
  Must be performed by non-expert personnel
Notes: Before you start editing the slides of your talk change to the Master Slide view:
Menu button “View” > Slide Master:
Edit the following items:
1. On the Title slide (second master slide)
a) Click to add title of your talk
b) Click to add subtitle (conference, location, name of the speaker, date)
2. On the Slide Master (first master slide)
a) The 1st row in the violet header: Delete the existent text and write the title of your talk into this text field b) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
Close Master View

## Slide 5: Qualification of vendors - actuators
Gather all DESY “in-house” developments
  Recipe settled for motor ball-bearings coating
  Parts purchased from different sources, integrated at DESY
Training provided to companies to deliver complete and cold tested drive unit
  Transfer to industry DESY coating recipe
Large effort in order to avoid the sole-supplier dependency:
  Qualify at least a 2nd option for motor and gear
  For both technical and commercial reasons
Prototypes verification
  Single-cavity HT long run in operating conditions at CHECHIA cryostat
  Life-time measured against maximum expected workload of 14 Msteps
Gather all the improvements made on piezo fixture assembly in the past
  Grant piezo proper pre-load
  Avoid loose piezo scenario
Few companies already qualified for piezo stacks but that’s not enough:
  Ability to assemble the whole piezo fixture system is required. The idea is to use experience of piezo manufacturer to integrate piezos
  So far, operations of handling, assembling and pre-loading piezo stacks used to be ”hand-crafted” by DESY experts
Prototypes verification
  Permanent test bench setup for driver electronics at FLASH
  Single long run at cold in bipolar mode in a devoted facility at INFN
Motor Drives
Piezo system

## Slide 6: At CFTs – Requirements and specs
820 motor drives
Life-time 50 Msteps and 30 h run-time
  14 Msteps expected at most
200 N axial load on spindle
  0.3 Nm maximum torque
Remnant magnetic field at assigned distance
Ability to provide the complete unit
  Mechanical assembly
  Lubricant and hardening coating
Acceptance test at factory
  On 100% of units, including test at 77 K
Packaging and storage
  ESA standard for dry-lubricated gears
  Hermetically sealed, double plastic bag with inert gas, desiccant gel, humidity indicator
FAT reports uploaded to EDMS
824 piezo fixtures
UHV and Cryo compatibility
Radiation hardness
  int. fluence > 1014 n/cm2 (20 y of ops.)
Cabling:
  Assigned ETFE twisted cable
  Center soldering with stress relief
  Insulation by kapton tape
Ability to provide mechanical assembly
  Incoming QC on Fixture mechanics
  Special focus on piezo support plates
Burn-in test on piezo
  On 100% of units
  RT test considered as sufficient
FAT reports uploaded to EDMS
Motor Drives
Piezo system

## Slide 7: Motor drives Factory Acceptance Tests
Dimensional check on each assembled unit
Cold test at LN2 temperature (77 K) for each assembled drive unit
Motor parameters cross-checked at both room temperature and cold
  Motor temperature in operation
  Windings impedance and inductivity
  Starting current, with axial load of 200 N on spindle
    Both «boost» and «run» at 1 A nominal
  Threshold current for steps loss, with axial load of 200 N on spindle
    Lowering run current from 1 A

## Slide 8: Piezo system Factory Acceptance Test
Burn-in test on each unit, done after assembly and in addition to standard internal QCs
Test done at room temperature, margins exist once at cold
DC test
  100 % of nominal voltage for 2 hours
AC test
  100% of nominal piezo voltage amplitude
  Sinusoidal half wave pulse, frequency of 1 kHz
  100 Hz repetition rate
  1 Million cycles in total
Stack parameters cross-checked before and after
  Electrical capacitance
  Leakage current at nominal voltage
  Stroke
Reports uploaded on EDMS for each test

## Slide 9: Production
Two vendors finally qualified for XFEL with two different technical solutions
  Phytron proposal with stepper motor and planetary gearbox (200 steps/turn, 50:1)
  Harmonic Drive proposal with Sanyo Denki stepper motor and coated harmonic drive gearbox (200 steps/turn, 88:1)
Contract awarded to Harmonic Drive, Limburg, Germany.
Several feedbacks from manufacturer gathered and implemented into actual process
  Minimal review of drawings
  Alternative motor coating proposal
  1 mm spindle pitch in place of 1.5 mm
  Minimize exposure of drive unit to air (humidity)
    ESA standard compliant packaging
    Reduce time window with vented module
Two vendors finally qualified for XFEL
  PI GmbH
  Noliac A/S
  Few other vendors were available but not fullfilling cryogenic and radiation hardness specification
Contract awarded to PI, Karlsruhe, Germany.
  PI Ceramics piezo model successfully passed the long-run test at INFN: 3,3·109, +/- 70 V, 500 Hz, bipolar, sinusoidal cycles at LN2 temperature
Feedbacks from manufacturer gathered and implemented into actual process
    Increases thickness of the plates used for pressing the piezo elements
    Explicitly define the required surface quality for the plates
    Better fixation of the wiring
Motor Drives
Piezo system

## Slide 10: Automatic Tuner test during Module Assembly
Constraints:
  Minimally perturbing
  VNA not be used
  Performed by non-expert personnel in a non-testing environment
Functionalities of tuner are checked indirectly
  LVDT displacement sensor at the cavity
  Piezo coupling and polarity passively checked through reverse piezoelectric effect
Main objectives are to detect:
  Failing actuators
  Loose mechanics assembly
  Cabling failures, polarity inversion
Test sequence
  +2 motor turns
  Measure piezo charging on 2nd turn
  Measure LVDT stroke on 2nd turn
  Back -2 turns

## Slide 11: QCs and measurements at later stages
Incoming Cryomodule Inspection at DESY
  Piezo electrical capacitance
  Cavity frequency shift in response to +1 drive turn
Cryomodule Cold LLRF Test at AMTF
  Piezo electrical capacitance
  Steps-to-tune, from CD frequency to 1.3 GHz
  Motor drive tuning sensitivity and hysteresis (+/- 1200 steps around working point at cold)
  Cavity frequency shift in response to piezo DC scan (-65 V to +65 V)
  Complete data set for LFD compensation
    LFD static and dynamic coefficients
    Best LFD compensating pulse (AC, DC, delay, frequency)
    Residual detuning

## Slide 12: Assembly instructions
A large effort has been devoted to the realization of assembly instruction document sets for each tuner stage
  Very detailed, step-by-step
  Assembly procedure initially written and debugged by experts, then reviewed by operators
  Meant to guide assembly for non-expert personnel
  Jointly developed and reviewed by the partners involved
Final revision in use at Assembly stages:
  Complete BOM for parts and tools
  Reference to EDMS p/n

## Slide 13: Drive unit – Numbers and stats
Source / Phase | Measurement | Statistics |  |  | Acceptance | Comments
 |  | Counts | Mean | Std. Dev. |  | 
FAT, room temp. | Step-loss curr. | 852 | 0.43 A | 0.16 A |  | Spread 37%
FAT, LN2 temp. | Step-loss curr. | 852 | 0.60 A | 0.14 A |  | Spread 23%
Automated Test, CEA | LVDT stroke | 548 | 0.22 V | 0.10 V | 0.175 V | Spread +/- 47%
 |  |  |  |  |  | Within 0.07 ÷ 0.42 V !
Incoming Inspection | Cavity freq. shift | 551 | 15.6 kHz | 1.3 kHz | 15 +/- 2 kHz | Spread +/- 8.1%
Cold test, AMTF | Tun. Sensitivity | 447 | -0.49 Hz/step | -0.028 Hz/step |  | Spread +/- 5.9%
Cold test, AMTF | Tun. Hysteresis | 454 | -83 step | -65 step | 300 steps | Spread +/- 78%
 |  |  |  |  |  | 2 with larger hysteresis than acceptance
 |  |  |  |  |  | 8 short-circuited
Only few minor issues, basically all solved (or soon solved) by re-soldering at vessel feed-through connectors. Namely:
  Bad soldering, missing thermo-retractable tube, easily detached cable
Coil center tap (grounding pin) is used by XFEL motor driver but not by the driver in use for tests at Module Assembly stage (unipolar vs bipolar)
  Cabling/problem on center tap were not detected

## Slide 14: Piezo system - Numbers and stats
Source / Phase | Measurement | Statistics |  |  | Acceptance | Comments
 |  | Counts | Mean | Std. Dev. |  | 
Datasheets | Stroke, free |  | 30 um |  |  | Spread +/- 10%
Burn-in at factory | Passed y/n | 1648 |  |  |  | 3 failed and replaced
FAT, before burn-in | Stroke, ass. | 1644 | 22.7 um | 1.8 um |  | Spread +/- 7.9%
FAT, after burn-in | Stroke, ass, | 1641 | 22.8 um | 1.7 um | 10 ÷ 26 um | Spread +/- 7.5%
Automated Test, CEA | Piezo charging | 1083 | 0.82 V | 0.26 V | > 0.5 V | Spread +/- 32%
 |  |  |  |  |  | Within 0.2 ÷ 1.6 V !
Cold test, AMTF | Cavity freq. shift | 949 | 1040 Hz | 135 Hz | > 850 Hz | Spread +/- 13%
 |  |  |  |  |  | 37 rev. polarity
 |  |  |  |  |  | 6 short-circuited
 |  |  |  |  |  | Both ss on XM5-C1
Only few minor issues, basically all solved (or soon solved) by re-soldering at vessel feed-through connectors. Namely:
  Assembly problem, cable pressed into isovac seal (1 case)
  Handling problem, damaged FT plug (3 cases, 2 CMs)
  Soldering problem, short-circuit at the FT (2 cases, 2 CMs)
  ?? (see below), reverse stack polarity (37 cases, 5 CMs)

## Slide 15: Notable facts
Reversed piezo polarity at module cold test stage
  37 piezo stacks in 5 CMs
  Not detected by any of previous QC stages
    Auto test at Module Assembly routinely cross-checked by reversing cables on purpose and error is always detected
  Inspection at vessel flanges always revealed correct cabling (red on +, black on -)
  A regular pattern is almost always found
    All P1 or all P2 with reverse polarity in the same module
  Piezo stacks were not coming from homogeneus production batches
  Reverse soldering at the vessel FT was decided
  ??

## Slide 16: Wrapping up – Lessons learned
Fully successful story so far, each cavity has functional tuner. As of today:
  XM76 at Assembly stage
  XM72 at Incoming Inspection, 68 CMs inspected
  XM71 at cold test, 64 CMs tested
Still some minor issues, all solved or soon to be solved
  For actuators, by re-soldering at vessel FTs
  For mechanics, by small reworking before assembly
The largest contributions to this achievement are coming from pre-assembly stages:
  Large effort spent in qualifying alternative options
  Fruitful collaboration with manufacturers to achieve rigorous requirements including decisive feedbacks from companies
  Detailed, thoroughly reviewed and jointly approved step-by-step instructions.
Auto test at module assembly stage revealed to be not consistent enough
  Constraints and problems prevented the measurement to be performed homogeneously for each module
  Anyway, large scatter compared to other measurements. Still somehow unable to detect puzzling polarity errors

## Slide 17: Acknowledgments
Many people from different Working Groups contributed with their work, support and measurements to the activity presented here:
L.Lilje, A. Bosotti and the WP07 team
O. Napoly, C. Madec and the CEA Module Assembly Team
J. Branlard, M. Grecki and the WP02 team
S. Barbanotti, K. Jensch and the WP03 team
The WP10 and IFJ-PAN teams

## Slide 18
Addendum

## Slide 19: Qualification of vendors - mechanics
Mechanics originally supplied by CEA
  Drawings and production adapted to local supplier in France
In view of XFEL series production, companies experienced in mass production of precision machined pieces (for Airbus etc.) have been contacted
  Cost reduction
  Adequate control on material quality (low magnetic permeability)
Drawings details significantly simplified and tolerances relaxed to reduce costs for precision machine time
Contract awarded to Astro-und-Feinwerktechnik, Berlin, Germany.
  Minor adaption of drawings
  Agreement on essential measures at part survey
  Pre-series cross-checked at DESY, series at CEA
    Good numbers from current records, see T. Trublet talk
  Piezo fixture incoming check at Piezo company
  QC protocols delivered into DESY EDMS

## Slide 20: Qualification of vendors – 3H mechanics
All technical solutions have been acquired from «larger brother»
  Titanium blades EBW in full penetration
  Large simplification of machining
Small series, 1+1 CMs, 16 tuners in total
  No further qualification stage, E. Zanon has been awarded after producing the 1.3 GHz model
  Inspection at Zanon by INFN
  RT acceptance tests at INFN with cavity mock-up for loaded vs. unloaded test
  HT at AMTF with a single cavity adapter

## Slide 21: Notable facts - 2
Cavity 1 tuner seems to exihibit, on average, a sligthly lower mechanical coupling
  Tuner design is specular compared to cavities 2-8, modification required to have clereance for gate-valve

## Slide 22: Notable facts - 3
No discrepancy between piezo parameters before and after the burn-in test at factory with 106 cycles
  See stroke, 22.7 +/- 1.8 vs 22.8 +/- 1.7 um
What happened at the manufacturer at the middle of piezo system production?