## Slide 1: LCLS-II Cryomodule Design
Joshua Kaluzny
December 1, 2015
Technical Challenges

## Slide 2: Outline
Introduction
Large Dynamic Heatloads
Liquid Helium Management
Cooldown to Preserve High Qo
Thermal Cycle to Reset Qo of Cavities
Instrumentation
Summary

## Slide 3
Introduction - Layout
Thirty-five 1.3 GHz 8-cavity cryomodules
Two 3.9 GHz 8-cavity cryomodules
Four cold segments (L0, L1, L2 and L3) which are separated by warm beamline sections.

## Slide 4: Introduction - CAD model
From Yuriy Orlov

## Slide 5: Introduction - CAD model

## Slide 6: Introduction - SLAC Tunnel
Tunnel size: 10x11 Feet
Tunnel slope: 0.5%

## Slide 7: Large Dynamic Heatloads - CW operation
CW operation of cavities
  80-150 watts per cryomodule
RF compensation heaters
  25 watts per cavity
Eliminated 5K shield
  Marginal value due to large heatloads
Increased chimney size to 4 inch tube (~100mm)

## Slide 8: Large Dynamic Heatloads - Two-phase Pipe
Increased size of two-phase pipe to 4 inch tube (~100mm)
  Reduces vapor velocity
Connection to GRP in center
  Reduces vapor velocity

## Slide 9: Liquid Helium Management
Manage liquid and vapor within and between cryomodules
  0.5% slope
  Magnet end lower and therefore a higher liquid level
Two-phase pipe closed at each end of the cryomodule
  Allows for each cryomodule to have different liquid level
Two-phase vapor analysis
  Slope and varying surface area accounted for
Cooldown line closed in cryomodule
  Prevents liquid transfer from one cryomodule to another
Connection to GRP in center
  A downhill connection would have made the connection too low

## Slide 10: Liquid Helium Management

## Slide 11: Liquid Helium Management
Increased two-phase pipe size
  Cover cavities but not spill into HGRP
Full 2-phase pipe
just starts to spill into
the HGRP
  Two-phase pipe is half full at connection to HGRP

## Slide 12: Liquid Helium Management
Bottom of two-phase pipe is above top of helium vessel
  The cavity is covered when there is liquid in the two-phase pipe

## Slide 13: Liquid Helium Management
Connection from two-phase pipe to HGRP
  650 mm upstream of center

## Slide 14: Cooldown to Preserve High Qo – Mass Flow Rate
Fast cool-down of a single cryomodule involves replacing ~200 liters of helium volume as quickly as possible.
A “fast” cooldown is 2-3 K/min
Start at 50 K and replace in 13 min
Flow into the cryomodule at 15 liters/min = 31 g/s liquid helium per cryomodule
  ~2 liters/min for each helium vessel
Cryoplant can produce ~130 g/s in liquefier mode
  Can cool ~4 cryomodules at 31 g/s
  May be able to use plant liquid storage to cool more than 4 cryomodules at once

## Slide 15: Cooldown to Preserve High Qo – Mass Flow Rate
Maximum mass flow rate in cooldown circuit (line H)

## Slide 16: Thermal Cycle to Reset Qo of Cavities
Cavity can trap flux during quench
  Thermal cycle above transition to reset Qo
  RF compensation heaters on each helium vessel and/or liquid level can heaters could be used to burn off liquid

## Slide 17: Thermal Cycle to Reset Qo of Cavities
Cooldown valve allows 0.5 g/s flow
  15% valve position with 1:1000 eq% profile
150 W heater to raise temp of low flow gas to ~50K

## Slide 18: Instrumentation
Prototype cryomodules well instrumented
  Including sensors inside helium vessels
No cold flanges or feedthroughs
  capillary tube to bring wires to warm feedthroughs
Sensors in helium vessels
  4 cavities per prototype cryomodule instrumented
    4 cernox sensors wired
    2 fluxgate sensors

## Slide 19: Instrumentation - Capillary Tube

## Slide 20: Summary

## Slide 21: Acknowledgments
This presentation includes information from many people at Fermilab, Jlab, and SLAC involved in cryomodule design, cryogenic distribution design, and overall cryogenic system design.
Special thanks to Tom Peterson, Camille Ginsburg, Chuck Grimm, Elvin Harms, Yun He, Arkadiy Klebaner, and Yuriy Orlov who provided information and slides for this presentation.

## Slide 23: Backup slides - Additional information

## Slide 24: Downstream end with magnet and BPM

## Slide 25: Another view, from the aisle side

## Slide 26: Upstream end, receives the sliding vacuum bellows

## Slide 27: Upstream end

## Slide 28
All the dimensions,
for reference

## Slide 29: TESLA-style cryomodules compared