## Slide 1: Optimizing the built-in amplifier in HV-CMOS CHESS1
Vitaliy Fadeyev, Zach Galloway , Herve Grabas
Alexander Grillo , Zhijun Liang , Abe Seiden
Jennifer Volk, Forest Martinez-Mckinney
University of California, Santa Cruz

## Slide 2: Isolated amplifier in CHESS1 chip
HV-CMOS CHESS1 chip has built-in isolated amplifiers
designed to optimize amplifier performance
  Six amplifier biasing control
  Optimization can be done with pulser, without using laser injection or beta source.
  Change its gain and output signal shape by changing biasing control
Try to study the amplifier performance as input to CHESS2 design

## Slide 3: Setup to test amplifier performance
Isolated Amplifier on CHESS1 chip
Pulser
Scope
Input pulse
Amplifier output
Voltage source
3.3V bias for amplifier
Time (s)
Voltage (V)
Voltage (V)
Source follower
50fF coupling capacitance
Falling edge

## Slide 4: Reminder of the output from CMOS amplifier (from last update)

## Slide 5: Amplifier output signal rise time (from last update)
Rise time : 10~30 ns depending on signal size
Full width at half maximum is from 80ns ~360ns depending on signal size.
Input charge (k e-)
Rise time (ns)
FWHM(ns)
Input charge (k e-)
Jitter dominated region ?
Significant background contribution
Signal Time walk ?

## Slide 6: Timing distribution at a fixed threshold example 1:
Output Threshold =0.05V
Input charge =0.6 k e-
Threshold
Time (ns)
Number of events

## Slide 7: Timing distribution at a fixed threshold example 2:
Output Threshold =0.05V
Input charge =3.1 k e-
Threshold
Time (ns)
Number of events

## Slide 8: Timing jitter Vs output threshold
Larger jitter for smaller input charge (as expected )

## Slide 9: Signal width Vs Threshold

## Slide 10: summary
Timing Jitter of the amplifier has been measured.
  Less than 5ns
  Larger jitter for smaller input charge (as expected )