## Slide 1: CHESS2
Design SLAC – UCSC – KIT

## Slide 2: CHESS2 pixels
IFB
1.8
3.3
InSF
Injection
1/2
In
Casc
Load
Comp
Th
1/2/4/8
RowENB
ColENB
RAMWrEn

## Slide 3: RAM cell
PMOS added to RAM cell to allow configuration from 1 up 128 cells in parallel.
Disconnects the inverter from driving the DataIn line during configuration.
Simulation OK: with the additional PMOS we can configure a full row or a full column with a single SACI command (see SLAC presentations).
Load
DataIn

## Slide 4: Pixel geometry
8 connected NWELLs
50% diode fraction
P-contact around each NWELL
120V rules
Size to be adjusted to strip length
Amplifier.
Half comparator.
RAM controlled -
- charge injection
Row/Col selection
Trim RAM
Trim DAC

## Slide 5: Pixel M3 lines
Metal 3
32 Signal
+
1 Row select
+
1 Injection
7.5µm space
for connectivity

## Slide 6: Amplifier & ½ comparator
Amplifier
AC
coupling
½ Comp.
Inj. RAM
Row/Col sel.
Amplifier & Comp. bias analog lines
Digital RAM & Inj. lines

## Slide 7: Amplifier & ½ comparator control signals
Amplifier
AC
coupling
½ Comp.
Inj. RAM
Row/Col sel.
Col sel.
Bias from DACs - periphery
Row sel.
Injection
Supply

## Slide 8: Trim RAM & Trim DAC
4bit TRIM RAM
x1 & x8
current sources
x2 & x4
current sources
Trim current
to ½ comp.

## Slide 9
NWELLs interconnect
M2 NWELL shield (gnd/vdd)

## Slide 10: Modification since the review
Pixels
- NWELL bias scheme modified to reduce the noise (observed during CHESS1 testing).
- Layout modified to include additional pmos in the RAM cell.
- Further layout modification required when chaining the 32 pixels.
- Reduced the size of the pixel and optimized power distribution (wider traces).
Periphery
- Large layout changes required for assembly of the 32 chained encoders (very difficult layout with 2 metals available only).
- pmos included in the RAM cell.
- Small Schematic and layout adjustment to reduce number of controls required, conserving the same functionality.

## Slide 11: CHESS periphery
1/2
Hit Latch
x32
5 bit hit address
1 bit hit flag
1 bit hit to encoding
Reset
Kill sig.
Ck
HitPrev
HitNext
Sel
RowENB
ColENB
RAMWrEn
Hit Flag Logic
Hard coded pixel address
Comparator latching
Hit encoding

## Slide 12: CHESS2 assembly – 128 connected pixels

## Slide 13: CHESS2 – 3 array of pixels and encoding periphery. Strip encoding to be connected.

## Slide 14: Last things to do
- Bias pads layout and on chip decoupling.
- Bloc assembly and routing.
- Global power distribution and routing – decoupling where we can.
- Global DRC and LVS.
- Global simulations.

## Slide 15: CHESS2 architecture
Doesn’t reflect actual size or placement
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Hit encoding
Strip Encoder
Row Decoder
…
Records Hits
Select 1 Hit/Strip
Select 8 Hits
Configure
CHESS2
LVDS output
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX
…
DONE
DONE