## Slide 1: Beta test of CHESS1 chip
Vitaliy Fadeyev, Zach Galloway , Herve Grabas
Alexander Grillo , Zhijun Liang , Abe Seiden
Jennifer Volk, Forest Martinez-Mckinney
University of California, Santa Cruz

## Slide 2: Beta test setup
CHESS1 chip Mount on daughter board from Jaya John
Sr90 beta source is used
Trigger rate ~0.1 Hz , self trigger
CHESS chip Biased at 110V

## Slide 3: Reminder of active array in CHESS1 chip
Active array APA08 is used
Channel 7,8 is connected for readout
Self trigger
  Trigger on pixel 8

## Slide 4: Pulse shape in usual case
Ch1
Ch2
Time (s)
Output(V)

## Slide 5: Signal amplitude distribution
No visible MIP peak yet
Self triggering on channel 1.
The noise peak (red curve) is obtained without beta source
Ch2 amplitude (V)
Ch1 amplitude (V)
Beta signal+BG
Background noise
Beta signal+BG
Background noise

## Slide 6: Why no MIP peak ?
SR90 Beta source we used has lots of low energy electrons.
  Self triggering includes both low energy electrons and high energy electrons -
  dE/dx of these low energy electrons are different from MIP.
  We need to select to high energy electron ( MIP )

## Slide 7: New setup for beta testing
Try to add scintillator in the setup
  Use scintillator trigger to select the high energy electron
Met a problem that
  The hole in daughter board is not big enough
  Electron can not go through APA08 and hit scintillator
    Blocked by the board.
  The plan is Milling part of the board
Scintillator
Daughter board
Sr90
CHESS1

## Slide 8: Milling the daughter board
After Milling
Before Milling
Milling part of the daughter board
  So that beta particle can go through pixel array APA08.

## Slide 9: Summary
Observe significant signal from active pixel in beta source test .
Still trying to find the MIP peak yet.
  Self triggering does not work well
  Need to select high energy electrons from Sr90 by using Scintillator trigger
Milling part of the daughter board.
  So that beta particle can go through pixel array APA08.
  Going to bond a CHESS1 chip on this new board.
Next step :
  Quantify the landau peak position of MIP in beta test
  Quantify the fraction of charge sharing between pixels
  Reduce the readout noise by optimizing the built-in amplifier configuration.

## Slide 10: backup

## Slide 11: Correlation in signal amplitude between two pixel
Ch1 amplitude (V)
Ch2 amplitude (V)
Charge sharing events