## Slide 1: The universal PCI Express Device Driver for MTCA.4
L.Petrosyan

## Slide 2: The Universal PCI Express Device Driver
Basic PCI Express functionality
  Mapping memories
  Read, write and some common ioctl
  Error handling
  Hot Plug
Standards or Guidlines functionalty
  Standard Registers Set
  SHAPI Registers Set (PICMG)
  PICMG Standard Device Model
  PCIe HotPlug functionality
Device specific but has common API
  DMA
Device specific functionality
User Application
API
PCI Express
Device
PCI Express
Device
API
DriverAPI
DriverAPI
Device Driver
Device Driver

## Slide 3: The Universal PCI Express Device Driver
Split Device Driver into two parts follow the Linux Device Driver stacking Model
Add all common functionality and API into universal part
  Basic PCI Express functionality
  Standards or Guidlines functionalty
Add Common API for Device specific functionality into universal part but keep functionality in Device Driver side
  Device specific but has common API
User Application
PCI Express
Device
PCI Express
Device
DriverAPI
DriverAPI
Device Driver
Device Driver
Universal
Device Driver
Common API
API
API
API

## Slide 4: The Universal PCI Express Device Driver
this approach facilitates creation of new drivers and user applications
The Device Driver created on the top of universal driver has all necessary PCI Express functionalty
It could be binded to any PCI Express Device
echo „10EE:0088“ > /sys/bus/devices/xxx/driver/new_id
facilitates integration of new devices into the existing software
User Application
PCI Express
Device
PCI Express
Device
DriverAPI
DriverAPI
Device Driver
Device Driver
Universal
Device Driver
Common API
PCI Express
Device 10EE:0088
API
API
API

## Slide 5: The Universal PCI Express Device Driver
Drivers and tools set
PCIe ID 10EE:0088
Functions:
ictrl()
  read_dma()
  write_dma()
UPCIEDEV base level driver
API header:
read (structure rw)
write (structure rw)
ioctrl (structure io)
DMA (structyre dma_io)
Functions:
attuch (PCIe IDs)
io_map()
remove()
read()
write()
ictrl() (slot, info, bit …)
PCIEDEV top level driver
common
Read
Write
Common IOCTRL
DMA
MTCAMONITOR
OS (device drivers)
User applications

## Slide 6: The Universal PCI Express Device Driver
MTCAMONITOR
MTCAMONITOR shows all
Attached AMC(PCIe) boards
And provides read/write access

## Slide 7: The Universal PCI Express Device Driver
X2TIMER MODULE
FPGA FW based on DESY START_UP PROJECT
Has separate device driver, but based on the universal
driver API
PCIe ID 10EE:0020
SIS8300 DIGITIZER
STRUCK FW with DMA R/W
PCIe ID 1796:0018, 1796:0019
SIS8300 BOARD LCBPM
FPGA FW based on DESY START_UP PROJECT
PCIe ID 10EE:0088

## Slide 8: The Universal PCI Express Device Driver
Switch ON the crate
SIS8300 board with the LCBPM project was binded to pciedev driver.
No drivers for X2TIMER and SIS8300 with the STRUCK FM boards
The “Bind pciedev” button activated for the boards which has no driver binded
We can bind pciedev driver to X2TIMER and SIS8300 boards

## Slide 9: The Universal PCI Express Device Driver
We can get board information pushing “INFO"

## Slide 10: The Universal PCI Express Device Driver
We can read from and write to board

## Slide 11: The Universal PCI Express Device Driver
pciedev driver attached to X2TIMER and SIS8300 boards

## Slide 12: The Universal PCI Express Device Driver
We can read from and write to the boards

## Slide 13: The Universal PCI Express Device Driver
Custom drivers:
X1TIMER driver:
Separate driver created
does not use the upciedev
functionality but based on the
upciedev API.
SIS8300 driver:
Based on the upciedev driver
added only IOCTRL for DMA.
SIS8300 LCBPM project:
pciedev driver.
Three different boards, three
Drivers one user application.

## Slide 14: The Universal PCI Express Device Driver
We have read/write access
to the boards

## Slide 15: The Universal PCI Express Device Driver
We could get all information

## Slide 16: The Universal PCI Express Device Driver
Fast access to lspci for current
board

## Slide 17: The Universal PCI Express Device Driver
Fast access to lspci for current
MCH PCIe Switch port

## Slide 18: The Universal PCI Express Device Driver
Status
this architecture was developed in DESY group MCS4 and till today with success is used
the following drivers, tools and libraries are developed used
UPCIEDEV
PCIEDEV
(MPS, BLM
DAMC2)
Common API
X2TIMER
SIS8300
DAMCBPM
(DMAC2)
MTCA TOOL
DOOCS UTCApcielib
(O.Hensler)
Use only Basic Functionality
Use Common API
Contains Device specific part
LCBPM
(SIS8300)
TAMC100
TAMC200
ESD ADIO
TAMC532

## Slide 19: The Universal PCI Express Device Driver
THANK YOU