## Slide 1: MTCA PCI Express and PCI Express Hot Plug
L.Petrosyan

## Slide 2: PCI Express Link and Lanes
PCI Express is a serial point-to point connection.
Each device sits on its own dedicted bus, which in PCIe lingo is called Link.
on one bus (Link) there can be only two devices
Each link is composed of one or more Lanes.
Each Lane is a differential signal pair in each direction
PCIe Device A
PCIe Device B
Link (x1, x2, x4, x8, x16 or x32 Lines)
Lane (x1 Differential signal pair)
PCI Express (Peripheral Component Interconnect Express) is a computer bus which moves information between the internal Hardware of a computer system (including the CPU and RAM) and peripheral devices.
It is a collection of wires and protocols that allows for the expansion of a computer.

## Slide 3: PCI Express Port
Port is the interface between a PCI Express component and the Link
It consists of differential transmitters and receivers
PCIe
Device
Port
PCIe
Device
Port
PCIe
Device
Port
PCIe
Device
Port
PCIe
Device
Port
PCIe
Device
Port
The number of Link lines and transmitters of the port can differ
The PCI express Device is identified by Vendor/Device IDs are commonly called the PCI ID.
The 16-bit vendor ID is allocated by the PCI-SIG. The 16-bit device ID is then assigned by the vendor.
The PCI express Device addressed by Bus number or/and by Memory address assigned to the current device

## Slide 4: PCI Express
PCI Express is a point-to-point connection between two devices
To add more devices
we need more buses
PCI Express Switch add buses and controls several point-to-point serial connections.
PCI Express Switch
PCIe Endpoint
Port
PCIe Endpoint
Port
PCIe Endpoint
Port
PCIe Switch
Port
Port
Port
Switch has two or moe logical PCI-to-PCI bridges, each bridge associated with a switch port
Port
Port
Port
PCI Bridge
PCI Bridge
PCI Bridge

## Slide 5: PCI Express
The Root Complex denotes the device that connects The CPU and memory subsystems to the PCI Express fabric
It may support one or more PCI Express Ports
PCI Express Root Complex
PCIe Endpoint
Root Complex
Bus 0
CPU
Memory
Port
PCIe Endpoint
Port
1
2
Port
Port
Root Complex generates PCI Express configuration and enumerates the System
PCI Express transactions use the address (bus:device) and memory routing
The Root Complex Bus number initialize to 0

## Slide 6: PCI Express
multiple switch devices can be connected to ports on the root complex or cascaded
PCI Express
Root Complex
Bus 0
CPU
Memory
Port
PCIe Endpoint
Port
1
10
Port
PCIe Endpoint
Port
Port
PCIe Endpoint
Port
PCIe Endpoint
Port
PCIe Endpoint
PCIe Endpoint
Port
Port
Port
Port
Port
Port
Port
Port
Port
Root Complex
Upstream Port
Downstream Port
4
2
5
6
8
9
3
7

## Slide 7: PCI Express
PCI Express and MTCA
Root Compl
CPU
Memory
Port
AMC
PCIe Switch
MCH in MCH Slot
CPU in Upstream Slot
AMC Modules
MCH
Back Plane

## Slide 8: PCI Express
PCI Express and MTCA
Root Compl
CPU
Memory
Port
AMC
PCIe Switch
AMC
PCIe Switch
MCH in MCH Slot
CPU in Upstream Slot
AMC Modules
MCH
Back Plane

## Slide 9: PCI Express
PCI Express and MTCA
MCH sets Up Upstream Port of the PCIe Switch
Device Driver
AMC 1
AMC 2
PCIe
Switch
MCH
MCH
link_status
CPU
Root Complex
PCIe Bus Driver

## Slide 10: PCI Express
PCI Express and MTCA
MCH sets Up Upstream Port of the PCIe Switch
MCH connects links to AMC slots
Device Driver
AMC 1
AMC 2
PCIe
Switch
MCH
MCH
link_status
CPU
Root Complex
PCIe Bus Driver

## Slide 11: PCI Express
PCI Express and MTCA
MCH sets Up Upstream Port of the PCIe Switch
MCH connects links to AMC slots
Root Comples configurates and enumarates the PCI Express Busses
OS provided PCI Express Bus Driver crates system Devices for all PCI Express devices and allocates memories
  At this point all devices visible in lspci
  The user application could uses system Device Files to map Device memory for accessing to the device
Device Driver
AMC 1
AMC 2
PCIe
Switch
MCH
MCH
link_status
CPU
Root Complex
PCIe Bus Driver
Sys
Device
Sys
Device
Sys
Device
OS PCIe Bus
Driver
lspci
/sys/bus/pci/devices/xxx

## Slide 12: PCI Express
PCI Express and MTCA
MCH sets Up Upstream Port of the PCIe Switch
MCH connects links to AMC slots
Root Comples configurates and enumarates the PCI Express Busses
OS provided PCI Express Bus Driver crates system Devices for all PCI Express devices and allocates memories
  At this point all devices visible in lspci
  The user application could uses system Device Files to map Device memory for accessing to the device
RCI Express Bus Driver call for every Device appropriate driver, according of PCI Vendor/Device IDs
Device Driver maps Device memories and crates Device File as entry piont
  The user application uses Device File for accessing to the Device by means of File Operation functions
Device Driver
AMC 1
AMC 2
PCIe
Switch
MCH
MCH
link_status
CPU
Root Complex
PCIe Bus Driver
Device
Driver
Device
Driver
Device
Driver
Sys
Device
Sys
Device
Sys
Device
Driver
Device
Driver
Device
Driver
Device
OS PCIe Bus
Driver
lspci
/dev/dvicename
/sys/bus/pci/devices/xxx

## Slide 13: PCI Express
PCI Express and MTCA
Device Driver
AMC 1
AMC 2
PCIe
Switch
MCH
MCH
link_status
CPU
Root Complex
PCIe Bus Driver
Device
Driver
Device
Driver
Device
Driver
Sys
Device
Sys
Device
Sys
Device
Driver
Device
Driver
Device
Driver
Device
OS PCIe Bus
Driver
lspci
/dev/dvicename
/sys/bus/pci/devices/xxx
Does lspci list the device
Does lspci list MCH Switch
NO
YES
Is the AMC in M4 state
Is the device file in /dev
GOOD
Check the kernel log file and call expert
Is the device driver loaded
YES
NO
YES
YES
Is the device driver installed
NO
NO
NO
NO
Install the device driver
Is the another driver for the same ID loaded
Unload the driver
YES
YES
Is the AMC links are connected
Try to reboot MCH, call expert
YES
YES
Try to reboot CPU, call expert
NO
Try to reboot AMC, call expert
Is the device BARs enabled
YES
NO
NO

## Slide 14: PCI Express
PCI Express and MTCA
lspci
00:00.0 Host bridge: Intel Corporation 2nd Generation Core Processor Family DRAM Controller (rev 09)
00:01.0 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:01.1 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:02.0 VGA compatible controller: Intel Corporation 2nd Generation Core Processor Family Integrated Graphics Controller (rev 09)
00:19.0 Ethernet controller: Intel Corporation 82579LM Gigabit Network Connection (rev 04)
00:1a.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #2 (rev 04)
00:1c.0 PCI bridge: Intel Corporation 6 Series/C200 Series Chipset Family PCI Express Root Port 1 (rev b4)
00:1d.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #1 (rev 04)
00:1f.0 ISA bridge: Intel Corporation QM67 Express Chipset Family LPC Controller (rev 04)
00:1f.2 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 4 port SATA IDE Controller (rev 04)
00:1f.3 SMBus: Intel Corporation 6 Series/C200 Series Chipset Family SMBus Controller (rev 04)
00:1f.5 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 2 port SATA IDE Controller (rev 04)
01:00.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
01:00.2 System peripheral: Integrated Device Technology, Inc. [IDT] Device 808f
02:08.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
02:0c.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
03:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:01.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:02.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:08.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:09.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0a.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0b.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:10.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:11.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:12.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:13.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
07:00.0 Communication synchronizer: Xilinx Corporation Device 0020
0a:00.0 Signal processing controller: Xilinx Corporation Device 0088
12:00.0 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
12:00.1 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
AMC 1
PCIe
Switch
MCH
CPU
Root Complex
PCIe Bus Driver
MCH
link_status
OS PCIe Bus
Driver
lspci
Device Driver
Device Driver
SIS8300 board
Vendor ID 10EE (XILINX)
Device ID 0088 (DESY dev. ID)

## Slide 15: PCI Express
PCI Express and MTCA
lspci
00:00.0 Host bridge: Intel Corporation 2nd Generation Core Processor Family DRAM Controller (rev 09)
00:01.0 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:01.1 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:02.0 VGA compatible controller: Intel Corporation 2nd Generation Core Processor Family Integrated Graphics Controller (rev 09)
00:19.0 Ethernet controller: Intel Corporation 82579LM Gigabit Network Connection (rev 04)
00:1a.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #2 (rev 04)
00:1c.0 PCI bridge: Intel Corporation 6 Series/C200 Series Chipset Family PCI Express Root Port 1 (rev b4)
00:1d.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #1 (rev 04)
00:1f.0 ISA bridge: Intel Corporation QM67 Express Chipset Family LPC Controller (rev 04)
00:1f.2 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 4 port SATA IDE Controller (rev 04)
00:1f.3 SMBus: Intel Corporation 6 Series/C200 Series Chipset Family SMBus Controller (rev 04)
00:1f.5 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 2 port SATA IDE Controller (rev 04)
01:00.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
01:00.2 System peripheral: Integrated Device Technology, Inc. [IDT] Device 808f
02:08.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
02:0c.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
03:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:01.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:02.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:08.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:09.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0a.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0b.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:10.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:11.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:12.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:13.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
07:00.0 Communication synchronizer: Xilinx Corporation Device 0020
0a:00.0 Signal processing controller: Xilinx Corporation Device 0088
12:00.0 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
12:00.1 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
lspci -t
-[0000:00]-+-00.0
+-01.0-[01-11]--+-00.0-[02-11]--+-08.0-[03-10]----00.0-[04-10]--+-00.0-[05-06]----00.0-[06]----04.0
| | | +-01.0-[07]----00.0
| | | +-02.0-[08]--
| | | +-08.0-[09]--
| | | +-09.0-[0a]----00.0
| | | +-0a.0-[0b]--
| | | +-0b.0-[0c]--
| | | +-10.0-[0d]----00.0
| | | +-11.0-[0e]--
| | | +-12.0-[0f]--
| | | \-13.0-[10]--
| | \-0c.0-[11]--
| \-00.2
+-01.1-[12]--+-00.0
| \-00.1
+-02.0
+-19.0
+-1a.0
+-1c.0-[13]--
+-1d.0
+-1f.0
+-1f.2
+-1f.3

## Slide 16: PCI Express
PCI Express and MTCA
lspci
00:00.0 Host bridge: Intel Corporation 2nd Generation Core Processor Family DRAM Controller (rev 09)
00:01.0 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:01.1 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:02.0 VGA compatible controller: Intel Corporation 2nd Generation Core Processor Family Integrated Graphics Controller (rev 09)
00:19.0 Ethernet controller: Intel Corporation 82579LM Gigabit Network Connection (rev 04)
00:1a.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #2 (rev 04)
00:1c.0 PCI bridge: Intel Corporation 6 Series/C200 Series Chipset Family PCI Express Root Port 1 (rev b4)
00:1d.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #1 (rev 04)
00:1f.0 ISA bridge: Intel Corporation QM67 Express Chipset Family LPC Controller (rev 04)
00:1f.2 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 4 port SATA IDE Controller (rev 04)
00:1f.3 SMBus: Intel Corporation 6 Series/C200 Series Chipset Family SMBus Controller (rev 04)
00:1f.5 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 2 port SATA IDE Controller (rev 04)
01:00.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
01:00.2 System peripheral: Integrated Device Technology, Inc. [IDT] Device 808f
02:08.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
02:0c.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
03:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:01.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:02.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:08.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:09.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0a.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0b.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:10.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:11.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:12.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:13.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
07:00.0 Communication synchronizer: Xilinx Corporation Device 0020
0a:00.0 Signal processing controller: Xilinx Corporation Device 0088
12:00.0 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
12:00.1 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
lspci -vvv -s 0a:00.0
0a:00.0 Signal processing controller: Xilinx Corporation Device 0088
Subsystem: Device 3300:0088
Physical Slot: 6
Control: I/O+ Mem+ BusMaster+ SpecCycle- MemWINV- VGASnoop- ParErr- Stepping- SERR- FastB2B- DisINTx+
Status: Cap+ 66MHz- UDF- FastB2B- ParErr- DEVSEL=fast >TAbort- <TAbort- <MAbort- >SERR- <PERR- INTx-
Latency: 0, Cache Line Size: 64 bytes
Interrupt: pin A routed to IRQ 79
Region 0: Memory at c4000000 (32-bit, non-prefetchable) [size=64M]
Region 1: Memory at c0000000 (32-bit, non-prefetchable) [size=64M]
Region 2: Memory at c8000000 (32-bit, non-prefetchable) [size=16M]
Expansion ROM at <ignored> [disabled]
Capabilities: [40] Power Management version 3
Flags: PMEClk- DSI- D1- D2- AuxCurrent=0mA PME(D0-,D1-,D2-,D3hot-,D3cold-)
Status: D0 NoSoftRst- PME-Enable- DSel=0 DScale=0 PME-
Capabilities: [48] MSI: Enable+ Count=1/1 Maskable- 64bit+
Address: 00000000fee005d8 Data: 0000
Capabilities: [60] Express (v1) Endpoint, MSI 00
DevCap: MaxPayload 512 bytes, PhantFunc 1, Latency L0s unlimited, L1 unlimited
ExtTag+ AttnBtn- AttnInd- PwrInd- RBE+ FLReset-
DevCtl: Report errors: Correctable- Non-Fatal- Fatal- Unsupported-
RlxdOrd+ ExtTag- PhantFunc- AuxPwr- NoSnoop+
MaxPayload 128 bytes, MaxReadReq 512 bytes
DevSta: CorrErr- UncorrErr- FatalErr- UnsuppReq- AuxPwr- TransPend-
LnkCap: Port #0, Speed 2.5GT/s, Width x4, ASPM L0s, Latency L0 unlimited, L1 unlimited
ClockPM- Surprise- LLActRep- BwNot-
LnkCtl: ASPM Disabled; RCB 64 bytes Disabled- Retrain- CommClk-
ExtSynch- ClockPM- AutWidDis- BWInt- AutBWInt-
LnkSta: Speed 2.5GT/s, Width x4, TrErr- Train- SlotClk+ DLActive- BWMgmt- ABWMgmt-
Capabilities: [100 v1] Device Serial Number 00-00-00-00-00-00-00-00
Kernel driver in use: pciedev
Kernel modules: pciedev

## Slide 17: PCI Express
PCI Express and MTCA
lspci
00:00.0 Host bridge: Intel Corporation 2nd Generation Core Processor Family DRAM Controller (rev 09)
00:01.0 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:01.1 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:02.0 VGA compatible controller: Intel Corporation 2nd Generation Core Processor Family Integrated Graphics Controller (rev 09)
00:19.0 Ethernet controller: Intel Corporation 82579LM Gigabit Network Connection (rev 04)
00:1a.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #2 (rev 04)
00:1c.0 PCI bridge: Intel Corporation 6 Series/C200 Series Chipset Family PCI Express Root Port 1 (rev b4)
00:1d.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #1 (rev 04)
00:1f.0 ISA bridge: Intel Corporation QM67 Express Chipset Family LPC Controller (rev 04)
00:1f.2 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 4 port SATA IDE Controller (rev 04)
00:1f.3 SMBus: Intel Corporation 6 Series/C200 Series Chipset Family SMBus Controller (rev 04)
00:1f.5 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 2 port SATA IDE Controller (rev 04)
01:00.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
01:00.2 System peripheral: Integrated Device Technology, Inc. [IDT] Device 808f
02:08.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
02:0c.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
03:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:01.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:02.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:08.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:09.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0a.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0b.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:10.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:11.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:12.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:13.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
07:00.0 Communication synchronizer: Xilinx Corporation Device 0020
0a:00.0 Signal processing controller: Xilinx Corporation Device 0088
12:00.0 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
12:00.1 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
lspci -vv -s 04:09.0
04:09.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba) (prog-if 00 [Normal decode])
Control: I/O+ Mem+ BusMaster+ SpecCycle- MemWINV- VGASnoop- ParErr- Stepping- SERR- FastB2B- DisINTx+
Status: Cap+ 66MHz- UDF- FastB2B- ParErr- DEVSEL=fast >TAbort- <TAbort- <MAbort- >SERR- <PERR- INTx-
Latency: 0, Cache Line Size: 64 bytes
Bus: primary=04, secondary=0a, subordinate=0a, sec-latency=0
Memory behind bridge: c0000000-c8ffffff
Secondary status: 66MHz- FastB2B- ParErr- DEVSEL=fast >TAbort- <TAbort- <MAbort- <SERR- <PERR-
BridgeCtl: Parity- SERR- NoISA- VGA- MAbort- >Reset- FastB2B-
PriDiscTmr- SecDiscTmr- DiscTmrStat- DiscTmrSERREn-
Capabilities: [40] Power Management version 3
Flags: PMEClk- DSI- D1- D2- AuxCurrent=0mA PME(D0+,D1-,D2-,D3hot+,D3cold+)
Status: D0 NoSoftRst+ PME-Enable- DSel=0 DScale=0 PME-
Capabilities: [48] MSI: Enable+ Count=1/8 Maskable+ 64bit+
Address: 00000000fee00478 Data: 0000
Masking: 000000fe Pending: 00000000
Capabilities: [68] Express (v2) Downstream Port (Slot+), MSI 00
DevCap: MaxPayload 512 bytes, PhantFunc 0, Latency L0s <64ns, L1 <1us
ExtTag- RBE+ FLReset-
DevCtl: Report errors: Correctable- Non-Fatal- Fatal- Unsupported-
RlxdOrd+ ExtTag- PhantFunc- AuxPwr- NoSnoop+
MaxPayload 128 bytes, MaxReadReq 128 bytes
DevSta: CorrErr+ UncorrErr- FatalErr- UnsuppReq+ AuxPwr- TransPend-
LnkCap: Port #9, Speed unknown, Width x4, ASPM L0s L1, Latency L0 <4us, L1 <4us
ClockPM- Surprise+ LLActRep+ BwNot+
LnkCtl: ASPM Disabled; Disabled- Retrain- CommClk-
ExtSynch- ClockPM- AutWidDis- BWInt- AutBWInt-
LnkSta: Speed 2.5GT/s, Width x4, TrErr- Train- SlotClk- DLActive+ BWMgmt+ ABWMgmt-
SltCap: AttnBtn+ PwrCtrl+ MRL+ AttnInd+ PwrInd+ HotPlug+ Surprise-
Slot #6, PowerLimit 25.000W; Interlock+ NoCompl-
SltCtl: Enable: AttnBtn+ PwrFlt- MRL+ PresDet+ CmdCplt+ HPIrq+ LinkChg-
Control: AttnInd Off, PwrInd On, Power- Interlock-
SltSta: Status: AttnBtn- PowerFlt- MRL- CmdCplt- PresDet+ Interlock-
Changed: MRL- PresDet- LinkState+

## Slide 18: PCI Express
PCI Express and MTCA
nat> show_fru
FRU Information:
----------------
FRU Device State Name
==========================================
0 MCH M4 NMCH-CM
3 mcmc1 M4 NAT-MCH-MCMC
5 AMC1 M4 CCT AM 310/302
6 AMC2 M4 ADB7000
7 AMC3 M4 X2TIMER
8 AMC4 M4 AMC-ADIO24
9 AMC5 M4 DAMC2V2
10 AMC6 M4 SIS8300
11 AMC7 M1 SIS8300
14 AMC10 M4 CCT AM 900/412
40 CU1 M4 Cooling Unit
41 CU2 M4 Cooling Unit
53 PM4 M4 NAT-PM-DC
60 Clk1 M4 MCH-Clock
61 Hub1 M4 MCH-PCIe
nat> show_link_state
AMC 1 Port 0 is Ethernet - 1000Base-BX
AMC 1 Port 4 is PCIe - x4 - 2,5 GT/s
AMC 1 Port 5 is PCIe - x4 - 2,5 GT/s
AMC 1 Port 6 is PCIe - x4 - 2,5 GT/s
AMC 1 Port 7 is PCIe - x4 - 2,5 GT/s
AMC 3 Port 4 is PCIe - x1 - 2,5 GT/s
AMC 4 Port 4 is PCIe - x1 - 2,5 GT/s
AMC 6 Port 4 is PCIe - x4 - 2,5 GT/s
AMC 6 Port 5 is PCIe - x4 - 2,5 GT/s
AMC 6 Port 6 is PCIe - x4 - 2,5 GT/s
AMC 6 Port 7 is PCIe - x4 - 2,5 GT/s
AMC 10 Port 0 is Ethernet - 1000Base-BX
AMC 10 Port 4 is PCIe - x4 - 8,0 GT/s
AMC 10 Port 5 is PCIe - x4 - 8,0 GT/s
AMC 10 Port 6 is PCIe - x4 - 8,0 GT/s
AMC 10 Port 7 is PCIe - x4 - 8,0 GT/s
Checking MCH Link connections

## Slide 19: PCI Express
PCI Express and MTCA
lspci
00:00.0 Host bridge: Intel Corporation 2nd Generation Core Processor Family DRAM Controller (rev 09)
00:01.0 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
...........................................
02:08.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
02:0c.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
03:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:01.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:02.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:08.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:09.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0a.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0b.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:10.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:11.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:12.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:13.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
07:00.0 Communication synchronizer: Xilinx Corporation Device 0020
12:00.0 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
12:00.1 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
AMC 1
PCIe
Switch
MCH
CPU
Root Complex
PCIe Bus Driver
MCH
link_status
OS PCIe Bus
Driver
lspci
Device Driver
Device Driver
SIS8300 board
Vendor ID 10EE (XILINX)
Device ID 0088 (DESY dev. ID)
We could see the MCH PCIe Switch but not our Device
The problem is here
Check is the Device powered ON
Check Link_state in MCH
Check Kernel log file for any PCIe errors

## Slide 20: PCI Express
PCI Express and MTCA
lspci -H1
00:00.0 Host bridge: Intel Corporation 2nd Generation Core Processor Family DRAM Controller (rev 09)
00:01.0 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:01.1 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
00:02.0 VGA compatible controller: Intel Corporation 2nd Generation Core Processor Family Integrated Graphics Controller (rev 09)
00:19.0 Ethernet controller: Intel Corporation 82579LM Gigabit Network Connection (rev 04)
00:1a.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #2 (rev 04)
00:1c.0 PCI bridge: Intel Corporation 6 Series/C200 Series Chipset Family PCI Express Root Port 1 (rev b4)
00:1d.0 USB controller: Intel Corporation 6 Series/C200 Series Chipset Family USB Enhanced Host Controller #1 (rev 04)
00:1f.0 ISA bridge: Intel Corporation QM67 Express Chipset Family LPC Controller (rev 04)
00:1f.2 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 4 port SATA IDE Controller (rev 04)
00:1f.3 SMBus: Intel Corporation 6 Series/C200 Series Chipset Family SMBus Controller (rev 04)
00:1f.5 IDE interface: Intel Corporation 6 Series/C200 Series Chipset Family 2 port SATA IDE Controller (rev 04)
01:00.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
01:00.2 System peripheral: Integrated Device Technology, Inc. [IDT] Device 808f
02:08.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
02:0c.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
12:00.0 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
12:00.1 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
AMC 1
PCIe
Switch
MCH
CPU
Root Complex
PCIe Bus Driver
MCH
link_status
OS PCIe Bus
Driver
lspci
Device Driver
Device Driver
SIS8300 board
Vendor ID 10EE (XILINX)
Device ID 0088 (DESY dev. ID)
We could not see the MCH PCIe Switch
The problem is here
Check is the CPU in Upstream Slot
Try to reboot the MCH and CPU

## Slide 21: PCI Express
PCI Express and MTCA
lspci
00:00.0 Host bridge: Intel Corporation 2nd Generation Core Processor Family DRAM Controller (rev 09)
00:01.0 PCI bridge: Intel Corporation Xeon E3-1200/2nd Generation Core Processor Family PCI Express Root Port (rev 09)
...........................................
02:08.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
02:0c.0 PCI bridge: Integrated Device Technology, Inc. [IDT] Device 808f
03:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:00.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:01.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:02.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:08.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:09.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0a.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:0b.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:10.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:11.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:12.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
04:13.0 PCI bridge: PLX Technology, Inc. Device 8748 (rev ba)
0a:00.0 Signal processing controller: Xilinx Corporation Device 0088
07:00.0 Communication synchronizer: Xilinx Corporation Device 0020
12:00.0 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
12:00.1 Ethernet controller: Intel Corporation 82580 Gigabit Backplane Connection (rev 01)
AMC 1
PCIe
Switch
MCH
CPU
Root Complex
PCIe Bus Driver
MCH
link_status
OS PCIe Bus
Driver
lspci
Device Driver
Device Driver
SIS8300 board
Vendor ID 10EE (XILINX)
Device ID 0088 (DESY dev. ID)
The Device is on the PCIe Bus
Check is the Device driver binded to the Device
Check lspci –vvv
Check Decvice Driver File in /dev

## Slide 22: PCI Express
PCI Express Hot Plug
PCI Express Hot Plug
A Method of replacing failed expansons cards keeping the OS and other services rinning during the repair
Shutting down and restarting software associated wiht the failed device
To accomplish those task the Hot Plug has to:
Monitor of the PCI Express slot events and reports these events to software via interrupts
Selectively turns ON and OFF the Power and Attention Indicators
Prepares the Card, Slot and proccesses for the card‘s removal or insertion
Remove or applay power to the Card connector

## Slide 23: PCI Express
PCI Express Hot Plug
Hardware Componenets
PCI Express Switch Hot Plug Hot Plug Controller
Receives and processes commands Issued by the Hot Plug Software componenets and Port interface
One controller for each Root or Switch port
PCI Express Port Interface
Controls Port componenets: power, Indicators and Switches
Software Componenets
User Interface
Permits the end user to control and monitor Hot Plug
Hot Plug Services
A OS provided software componenets that processes Hot Plug requests issued by User and Hardware
Hot Plug System Driver
Controls the Hot Plug Controller
Device Driver
Prepares the Device to be removed or initialise the Device after insertion
For performance above the stated conditions some new components step on the stage
PCIe Card
Port
Interface
Hot Plug
Controller
PCIe Switch
CPU
OS
User Interface
Hot Plug
Services
Hot Plug
Driver
PCIe Bus
Driver
Device
Driver

## Slide 24: PCI Express
PCI Express Hot Plug and MTCA
PCIe Card
Port
Interface
Hot Plug
Controller
PCIe Switch
CPU
OS
User Interface
Hot Plug
Services
Hot Plug
Driver
PCIe Bus
Driver
Device
Driver
Port
Interface
Hot Plug
Controller
PCIe Switch
MCH
MCMC
MMC
IPMI
AMC
CPU
OS
User Interface
Hot Plug
Services
Hot Plug
Driver
PCIe Bus
Driver
Device
Driver

## Slide 25: PCI Express
PCI Express Hot Plug and MTCA
AMC
MCH
OS
MMC
MCMC
Hot Plug
Controller
Hot Plug
Driver
Device
Driver
Hot Plug
Service
IPMI
Hot Swap Open
IPMI
Blue LED Blink
Hot Plug
Interrupt
Check Slot Status
5 sec
Call Device Driver
Remove
Back frpm Device Driver Remove
Set Slot Controll
Power OFF
IPMI Quiesce
Remove Payload
Red LED ON
Green LED OF
Blue LED ON
udev

## Slide 26: PCI Express
PCI Express Hot Plug and MTCA
AMC
MCH
OS
MMC
MCMC
Hot Plug
Controller
Hot Plug
Driver
Device
Driver
Hot Plug
Service
IPMI
Hot Swap Close
IPMI
Blue LED Blink
IPMI Enable
Payload
Red LED OFF
Green LED ON
Blue LED OFF
IPMI Set Port State
Hot Plug
Interrupt
5 sec
Set Slot Status
Check Slot Status
Link training
Call Device Driver
udev

## Slide 27: PCI Express
PCI Express Hot Plug test
AMC
The PCI Express Hot Plug on the MTCA depends on:
  Linux Hot Plug Driver
  MCH PCI Express Switch with the Hot Plug controller

## Slide 28: PCI Express
PCI Express Hot Plug test
AMC
Hot Plug generated by the Hardware (Hardware Hot Plug)
  Hot Plug triggered by pulling/pushing Module Latch
  System‘s and Device Driver Nodes created/deleted
  MCH turns AMC Power ON/OFF
Hot Plug generated from the user side (Soft Hot Plug)
  Hot Plug triggered by writting 1/0 to power file
  System‘s and Device Driver Nodes created/deleted
  The AMC module remains powered
AMC
MCH PCIe
Switch
OS Hot Plug
Driver
Device Driver
User Interface
The PCI Express Hot Plug on the MTCA depends on:
  Linux Hot Plug Driver
  MCH PCI Express Switch with the Hot Plug controller

## Slide 29: PCI Express
PCI Express Hot Plug test
AMC
Is device listed in lspci
NO
NO
NO
NO
YES
NO
YES
YES
YES
YES
Go to PCIe check
Check pciehp driver
Enable pciehp
Check /sys/bus/pci/slots and power file
Check MCH
Go to Soft Hotplug check
Disable device
(write 0 to “power” file)
Run lspci
Pull out the AMC handle
Run lspci
Enable device
(write 1 to “power” file)
Run lspci
Go to Hard Hotplug check
Check kernel log
Call OS expert
Check kernel log
Call OS expert
Check kernel log
Call MCH expert
Check kernel log
Call MCH expert
Push the AMC handle
Run lspci
Use Hotplug
NO
NO
YES
YES

## Slide 30: PCI Express
PCI Express Hot Plug test
AMC
The PCI Express Hot Plug on the MTCA depends on:
  Linux Hot Plug Driver
  MCH PCI Express Switch with the Hot Plug controller
To enable the PCI Express Hot Plug we have to:
  Enable Hot Plug Controller of the MCH PCI Express Switch for all ports conneted to crate slots

## Slide 31: PCI Express
PCI Express Hot Plug test
AMC
The PCI Express Hot Plug on the MTCA depends on:
  Linux Hot Plug Driver
  MCH PCI Express Switch with the Hot Plug controller
To enable the PCI Express Hot Plug we have to:
  Enable Hot Plug Controller of the MCH PCI Express Switch for all ports conneted to crate slots
  Enable Linux PCI Express Hot Plug Driver
    The PCI Express Hot Plug Driver by default is not enabled. To load the driver the follwing boot parameters have to be setted
      UBUNTU 10 (Kernel version up to 2.8x)
        pciehp.pciehp_force=1 pciehp.pciehp_debug=1
        add these parameters in /boot/grub/menu.lst file
        reboot the CPU
      UBUNTU 12 (Kernel version 3.0 ->)
        pciehp.pciehp_force=1 pciehp.pciehp_debug=1 pcie_ports=native
        add these parameters in /etc/default/grub file and call update-grub
        reboot the CPU

## Slide 32: PCI Express
PCI Express Hot Plug test
AMC
Checking Hot Plug Driver and PCI Express Switch
PCI Express Hot Plug driver creates subdirectories in /sys/bus/pci/slots for every existing PCI Express slots. In case of MTCA for every physical slot. The name of each directory is the physical slot number

## Slide 33: PCI Express
PCI Express Hot Plug test
AMC
Checking Hot Plug Driver and PCI Express Switch
PCI Express Hot Plug driver creates subdirectories in /sys/bus/pci/slots for every existing PCI Express slots. In case of MTCA for every physical slot. The name of each directory is the physical slot number
Check the /sys/bus/pci/slots directory:
  The directors is empty
    root@hostname:~# ls /sys/bus/pci/slots
    . ..
      PCI Express Hot Plug Driver is not loaded
        Check MCH configuration and OS boot parameters

## Slide 34: PCI Express
PCI Express Hot Plug test
AMC
Checking Hot Plug Driver and PCI Express Switch
PCI Express Hot Plug driver creates subdirectories in /sys/bus/pci/slots for every existing PCI Express slots. In case of MTCA for every physical slot. The name of each directory is the physical slot number
Check the /sys/bus/pci/slots directory:
  The directors is empty
    root@hostname:~# ls /sys/bus/pci/slots
    . ..
      PCI Express Hot Plug Drivar is not loaded
        Check MCH configuration and OS boot parameters
  Strange numbers (subdirectories names)
    root@hostname:~# ls /sys/bus/pci/slots
    . .. 0 9 17 (could not be physical slot number 0 and slot number 17 in 12 slots crate)
      Wrong PCI Express Switch configuration (Switch‘s Port Number and Slot number are same)
      Hot Plug Controller of the PCI Express Switch is not enabled

## Slide 35: PCI Express
PCI Express Hot Plug test
AMC
Checking Hot Plug Driver and PCI Express Switch
PCI Express Hot Plug driver creates subdirectories in /sys/bus/pci/slots for every existing PCI Express slots. In case of MTCA for every physical slot. The name of each directory is the physical slot number
Check the /sys/bus/pci/slots directory:
  OK
    root@hostname:~# ls /sys/bus/pci/slots
    . .. 10 11 12 2 3 4 5 6 7 8 9 (CPU in Slot 1)

## Slide 36: PCI Express
PCI Express Hot Plug test
AMC
Checking Hot Plug Driver and PCI Express Switch
PCI Express Hot Plug driver creates subdirectories in /sys/bus/pci/slots for every existing PCI Express slots. In case of MTCA for every physical slot. The name of each directory is the physical slot number
Check the /sys/bus/pci/slots directory:
  OK
    root@hostname:~# ls /sys/bus/pci/slots
    . .. 10 11 12 2 3 4 5 6 7 8 9 (CPU in Slot 1)
  There is file power in each subdirectory. In this file written 1 if there is AMC module in the current slot.
    root@hostname:~# ls /sys/bus/pci/slots/8
    . .. adapter address attention cur_bus_speed lutch max_bus_speed module power
    root@hostname:~# cat /sys/bus/pci/slots/8/power
    1

## Slide 37: PCI Express
PCI Express Hot Plug test
AMC
Checking Hot Plug Driver and PCI Express Switch
PCI Express Hot Plug driver creates subdirectories in /sys/bus/pci/slots for every existing PCI Express slots. In case of MTCA for every physical slot. The name of each directory is the physical slot number
Check the /sys/bus/pci/slots directory:
  OK
    root@hostname:~# ls /sys/bus/pci/slots
    . .. 10 11 12 2 3 4 5 6 7 8 9 (CPU in Slot 1)
  There is file power in each subdirectory. In this file written 1 if there is AMC module in the current slot.
    root@hostname:~# ls /sys/bus/pci/slots/8
    . .. adapter address attention cur_bus_speed lutch max_bus_speed module power
    root@hostname:~# cat /sys/bus/pci/slots/8/power
    1
    If there is AMC module in the Slot but reading from the power file returns 0 check MCH configuration
    Usualy Hot Plug Controller of the MCH PCI Express Switch is not enabled

## Slide 38: PCI Express
PCI Express Hot Plug test
Checking Soft Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Trigger Hot Plug writting 0 to power file
  echo 0 > /sys/bus/pci/slots/6/power

## Slide 39: PCI Express
PCI Express Hot Plug test
Checking Soft Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Trigger Hot Plug writting 0 to power file
  echo 0 > /sys/bus/pci/slots/6/power
Check kernel log file and use lspci to check the module is gone
kernel: pciehp 0000:04:09.0:pcie24: disable_slot: physical_slot = 6
kernel: pciehp 0000:04:09.0:pcie24: pciehp_unconfigure_device: domain:bus:dev = 0000:0a:00
kernel: REMOVE CALLED
kernel: REMOVE: UNMAPPING MEMORYs
kernel: PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 247 MINOR 0

## Slide 40: PCI Express
PCI Express Hot Plug test
Checking Soft Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Trigger Hot Plug writting 0 to power file
  echo 0 > /sys/bus/pci/slots/6/power
Check kernel log file and use lspci to check the module is gone
Enable module writting 1 to the power file
  echo 1 > /sys/bus/pci/slots/6/power
kernel: pciehp 0000:04:09.0:pcie24: disable_slot: physical_slot = 6
kernel: pciehp 0000:04:09.0:pcie24: pciehp_unconfigure_device: domain:bus:dev = 0000:0a:00
kernel: REMOVE CALLED
kernel: REMOVE: UNMAPPING MEMORYs
kernel: PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 247 MINOR 0

## Slide 41: PCI Express
PCI Express Hot Plug test
Checking Soft Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Trigger Hot Plug writting 0 to power file
  echo 0 > /sys/bus/pci/slots/6/power
Check kernel log file and use lspci to check the module is gone
Enable module writting 1 to the power file
  echo 1 > /sys/bus/pci/slots/6/power
Check kernel log file and use lspci to check the module is in
kernel: pciehp 0000:04:09.0:pcie24: disable_slot: physical_slot = 6
kernel: pciehp 0000:04:09.0:pcie24: pciehp_unconfigure_device: domain:bus:dev = 0000:0a:00
kernel: REMOVE CALLED
kernel: REMOVE: UNMAPPING MEMORYs
kernel: PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 247 MINOR 0
kernel:pciehp 0000:04:09.0:pcie24: __pciehp_link_set: lnk_ctrl = 0
kernel:pciehp 0000:04:09.0:pcie24: pciehp_green_led_blink: SLOTCTRL 80 write cmd 200
kernel:PCIEDEV_PROBE CALLED
kernel:pciedev 0000:0a:00.0: enabling device (0000 -> 0002)
kernel:PCIEDEV_PROBE: mem_region 0 address C0000000 SIZE 3FFFFFF FLAG 40200
kernel:PCIEDEV: mem_region 1 address C4000000
kernel:PCIEDEV: mem_region 2 address C8000000
kernel:PCIEDEV_PROBE: CREAT DEVICE MAJOR 247 MINOR 0 F_NAME pciedevs6 DEV_NAME
The Software side works.
Checking Hardware part

## Slide 42: PCI Express
PCI Express Hot Plug test
Checking Hradware triggered Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Pull out the AMC handle

## Slide 43: PCI Express
PCI Express Hot Plug test
Checking Hradware triggered Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Pull out the AMC handle
Check kernel log file and use lspci to check the module is gone
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering off due to button press.
kernel:PCIEDEV_REMOVE: SLOT 6 DEV 257949696
kernel:REMOVE: UNMAPPING MEMORYs
kernel:PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 246 MINOR 0

## Slide 44: PCI Express
PCI Express Hot Plug test
Checking Hradware triggered Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Pull out the AMC handle
Check kernel log file and use lspci to check the module is gone
Switch ON the module pushing AMC Handle
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering off due to button press.
kernel:PCIEDEV_REMOVE: SLOT 6 DEV 257949696
kernel:REMOVE: UNMAPPING MEMORYs
kernel:PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 246 MINOR 0

## Slide 45: PCI Express
PCI Express Hot Plug test
Checking Hradware triggered Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Pull out the AMC handle
Check kernel log file and use lspci to check the module is gone
Switch ON the module pushing AMC Handle
Check kernel log file and use lspci to check the module is in
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering off due to button press.
kernel:PCIEDEV_REMOVE: SLOT 6 DEV 257949696
kernel:REMOVE: UNMAPPING MEMORYs
kernel:PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 246 MINOR 0
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering on due to button press.
kernel:pciehp 0000:04:09.0:pcie24: pciehp_check_link_status: lnk_status = 6041
kernel:PCIEDEV_PROBE CALLED
kernel:PCIEDEV_PROBE: mem_region 0 address C0000000 SIZE 3FFFFFF FLAG 40200
kernel:PCIEDEV_PROBE: CREAT DEVICE MAJOR 246 MINOR 0 F_NAME pciedevs6 DEV_NAME

## Slide 46: PCI Express
PCI Express Hot Plug test
Checking Hradware triggered Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Pull out the AMC handle
Check kernel log file and use lspci to check the module is gone
Switch ON the module pushing AMC Handle
Check kernel log file and use lspci to check the module is in
Run lspci with –vvv option to checl are the boards memories mapped
Cneck Device Driver file in /dev
Try to access to the Device using Device Driver
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering off due to button press.
kernel:PCIEDEV_REMOVE: SLOT 6 DEV 257949696
kernel:REMOVE: UNMAPPING MEMORYs
kernel:PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 246 MINOR 0
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering on due to button press.
kernel:pciehp 0000:04:09.0:pcie24: pciehp_check_link_status: lnk_status = 6041
kernel:PCIEDEV_PROBE CALLED
kernel:PCIEDEV_PROBE: mem_region 0 address C0000000 SIZE 3FFFFFF FLAG 40200
kernel:PCIEDEV_PROBE: CREAT DEVICE MAJOR 246 MINOR 0 F_NAME pciedevs6 DEV_NAME

## Slide 47: PCI Express
PCI Express Hot Plug test
Checking Hradware triggered Hot Plug
Use /var/log/kern.log to watch kernel messages and lspci to checl PCI Express Device
Check the module using lspci
Pull out the AMC handle
Check kernel log file and use lspci to check the module is gone
Switch ON the module pushing AMC Handle
Check kernel log file and use lspci to check the module is in
Run lspci with –vvv option to checl are the boards memories mapped
Cneck Device Driver file in /dev
Try to access to the Device using Device Driver
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering off due to button press.
kernel:PCIEDEV_REMOVE: SLOT 6 DEV 257949696
kernel:REMOVE: UNMAPPING MEMORYs
kernel:PCIEDEV_REMOVE: DESTROY DEVICE MAJOR 246 MINOR 0
kernel:pciehp 0000:04:09.0:pcie24: pcie_isr: intr_loc 1
kernel:pciehp 0000:04:09.0:pcie24: Attention button interrupt received
kernel:pciehp 0000:04:09.0:pcie24: Button pressed on Slot(6)
kernel:pciehp 0000:04:09.0:pcie24: PCI slot #6 - powering on due to button press.
kernel:pciehp 0000:04:09.0:pcie24: pciehp_check_link_status: lnk_status = 6041
kernel:PCIEDEV_PROBE CALLED
kernel:PCIEDEV_PROBE: mem_region 0 address C0000000 SIZE 3FFFFFF FLAG 40200
kernel:PCIEDEV_PROBE: CREAT DEVICE MAJOR 246 MINOR 0 F_NAME pciedevs6 DEV_NAME
According of the kernel log the module is ON but not listed in lspci
  Module initialisation is slow, try to enable it wriiting 1 to the power file

## Slide 48: PCI Express
PCI Express Hot Plug test
enjoy PCIe and Hot Plug...
Thank You