## Slide 1: CHESS2 Design Status ATLAS Strip CMOS Meeting
P. Caragiulo*, C. Tamma, A. Dragone, C. Kenney, P. Grenier, Su Dong, H. Grabas, V. Fadeyev
September 29th 2015
(* pietroc@slac.stanford.edu)

## Slide 2: Outline
CHESS2 ASIC Architecture and Specifications
Pixel
Read-Out
  Hit Encoding
  Serializer
  LVDS TX/RX
Configuration
  SACI
  Control Unit
    Global Register
    Row and Column register for pixel selection
    Row and Column decoders
    Digital control signal distribution

## Slide 3: CHESS2 ASIC Architecture
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
Acquisition
Encoding
Configuration and Calibration
Read-out

## Slide 4: Specifications
 | Specs
Substrate resistivity | 20Ohms to 1000Ohms
Substrate high voltage bias | 120V
Pixel size | 40µm x ~800µm
Number of pixel per strip | 32
Number of strips | 128
Timing resolution | 25ns
Maximum number of hits per strip | 1 + flag
Maximum number of hits per 128 strips | 8
Readout speed | 320MHz
Additional constraint | Rad-hard design
Slide from H. Grabas

## Slide 5: CHESS2 pixel
IFB
1.8
3.3
InSF
Injection
1/2
In
Casc
Load
Comp
Th
1/2/4/8
RowENB
ColENB
RAMWrEn
Slide from H. Grabas

## Slide 6: Hit Encoding and Read-out blocks
hit
column address (5b) + double hit (1b)
for each row the hit encoder has:
every 25ns
column address (5b) + double hit (1b) + row address (7b)
It receives:
every 25ns
detect the pixel address of the first 8 hits
INPUTS
OUTPUTS
HIT ENCODER
column address (5b) + double hit (1b) + row address (7b)
It returns:
every 3.125ns
INPUTS
OUTPUTS
LVDS TX
8x
Parallel transmission of the 13b lines
every 3.125ns
It returns:

## Slide 7: Hit Encoding – Processing the Strip Encoding
row0
row1
row2
row3
row4
row5
row6
row7
row8
row9
0
1
0
0
1
1
0
0
0
1
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
+1
0
SKIP
+1
SKIP
+1
SKIP
+1
SKIP
+1
SKIP
+1
SKIP
+1
SKIP
+1
SKIP
+1
SKIP
+1
SKIP
closed switch
open switch
Control lines
8b Memory

## Slide 8: Hit Encoding – Processing the Strip Encoding
SKIP
+1
Bit line settling
Time to get the bit lines ready is based on number of hits
Can be as high as 64ns if are all hits.
Write Bit
Write Memory
time
25ns
We are interested in the first 8 hits so the worst case using this architecture is when we have no hit on the first 120 rows and hit on the last 8 rows -> 22ns
Avoid ghost from previous cycle
introducing a reset phase
reset
500ps
150ps
4ns
300ps

## Slide 9: Write Memory and Reset Line Signal
WriteMemory
Line Reset
t1
t3
t2
Programmability on Reset Delay (t1), Reset Duration (t2) and Reset-Write Distance (t3)

## Slide 10: Hit Encoding – Processing the Strip Encoding
Find first 8 hits in 128 rows
2x Find first 8 hits in 32 rows (2 stage in a pipeline-like behavior)
13 x 8b Memory
Serializer
Worst case scenario:
22ns
7.6ns
11 x 8b Memory
11 x 8b Memory
11 x 8b Memory
11 x 8b Memory
Serializer

## Slide 11: Fast Adder x32 (Layout)
1280 µm
600 µm
Adders
Bus Line Selector
Bus Lines

## Slide 12: LVDS TX/RX and Sync
Serializer
13
13x LVDS Driver
13
13
1 LVDS Receiver
320MHz Clock
Sync pad

## Slide 13: Serializer
PISO 1b
p
s
o
PISO 1b
p
s
o
PISO 1b
p
s
o
PISO 1b
p
s
o
PISO 1b
p
s
o
PISO 1b
p
s
o
PISO 1b
p
s
o
PISO 1b
p
s
o
8 x 13 1bit PISO Cell.
Parallel input with 25ns period (synchronized to the 40MHz external clock).
Serial Output has 3.125ns period (synchronized to the 320MHz external clock).
150 µm
400 µm

## Slide 14: LVDS Driver – Simulated Performance
Specs | Typical | Min | Max
Differential Output Voltage (@ RLOAD =100Ω) | 600mV |  | 
Output Common Mode | 1.2V | 0.5 | 2.8
Current | 3mA | 0.2mA | 3.5mA*
Speed | 320MHz |  | 500MHz
Supply | 3.3V |  | 
* Can meet standard LVDS requirements.
Schematic simulated at all condition (wo,wz,ws,wp) at room temperature.

## Slide 15: LVDS Receiver - Performance
Specs | Typical | Min | Max
Differential Input Voltage (@ RLOAD =100Ω) | 600mV |  | 
Output Common Mode | 1.2V |  | 
Input Current | 3mA* |  | 
Speed | 320MHz |  | 500MHz
Supply | 3.3V |  | 
* Can meet standard LVDS requirements.
Schematic simulated at all condition (wo,wz,ws,wp) at room temperature.

## Slide 16: SLAC ASIC Control Interface (SACI)
Serial Interface with handshake protocol
5 Signals
  3 shared: saciClk, saciCmd, saciRsp.
  1 dedicated select line per slave: saciSelL.
  1 Reset Line (RstL) can be shared with the ASIC Global Reset.
Operated between 0V and 3.3V
Allows multiple SACI on same bus (parallel mode).
SLAC ASIC Control Interface (SACI)
CLK
ACK
Control Logic
Global Registers
Row Pointer
Column Pointer
RstL
EXEC
R/W
CMD[0..6]
ADDR[0..11]
DATA[0..31]
saciClk
saciCmd
saciRsp
saciSelL
SACIcmd (serial signal):
SET (1bit)
1
RW (1bit)
R/W
CMD (7bit)
CMD
ADDR (12bit)
ADDR
DATA (32bit)
DATA

## Slide 17: SACI – Multiple ASIC connection
SACI-0
CLK
CMD
SEL
RSP
SACI-1
CLK
CMD
SEL
RSP
SACI-2
CLK
CMD
SEL
RSP
SACI-3
CLK
CMD
SEL
RSP
SACI Response<0:3>
Shared Clock
Shared Command
Sel0
Sel1
Sel2
Sel3
Response line can be shared if only 1 SACI is selected when the command arrives.

## Slide 18: SACI - Commands
SET (1bit)
1
RW (1bit)
RW
CMD (7bit)
CMD
ADDR (12bit)
ADDR
DATA (32bit)
DATA
RW | CMD | ADDR | DATA | Function
0/1 | 1 | Register Address | Data | Read/Write Global Register
1 | 4 | 0 | Data | Write Matrix
0/1 | 5 | 0 | Data | Read/Write Pixel
1 | 8 | 0 | 0 | START Matrix Configuration
0 | 0 | 0 | 0 | END Matrix Configuration
1 | 2 | 0 | 0 | Write all Columns (used to configure a single row)
1 | 3 | 0 | 0 | Write all Row (used to configure a single column)
18
The ASIC decodes the command last 4 bits. Any given command longer than 4 bits will be interpreted as a 4 bit command.

## Slide 19: Control Unit
700 µm
2000 µm
Global Register
Row and Column register for pixel selection
SACI
Command Logic
Digital control signal distribution

## Slide 20: Control Unit
SACI Core
ADDRESS Buffer
CMD, CLK Buffer
DATABUS Buffer
SACI System
Rad Hard Register
+
Rad Hard Bits
Logic
Command Logic
Command Decoder
Command Logic
Bits
Logic
Row Reg
Bits
Logic
Col
Reg
Pixel Write
DataBus to Matrix
Buffers
+
+
Bus to ASIC
Internal Bus

## Slide 21: Next step toward the submission
Individual blocks have been simulated and pass LVS and DRC
Integration of top level blocks
Full chip simulation and verification

## Slide 22: Additional Slides
Additional Slides

## Slide 23: Matrix and Strip Encoding Layout
Images from H. Grabas

## Slide 24: Address and Databus buffer
Address and Command Buffer
Databus Buffer
Guarantees that SACI is writing the data bus only in WRITE mode and it is reading the data bus in READ mode.
Writing and reading of the data bus are permitted only when the EXEC signal is HIGH in order to save power
SACI is reading the data bus only when the ACK signal is HIGH in order to avoid buffer high current consumption when the bus is floating.
Sending address and command to the command logic only when the EXEC signal is HIGH in order to save power.

## Slide 25: Column and Row Selection Register
Row Selection Register
Column Selection Register
7 bits row register and 5 bits column register that store row and column pointers.

## Slide 26: Column and Row decoders
Row decoders
Column decoders
Decode the digital word coming from the row and column selection register in 1 hot digital output.
Allow single row, single column or matrix configuration.
Row decoder is synchronous with the CCKpix clock.

## Slide 27: SACI - Signals
SACIcmd (serial signal):
SACIclk
SACIselL
SACIcmd
SACIrsp
SACIrstL
SET (1bit)
1
RW (1bit)
R/W
CMD (7bit)
CMD
ADDR (12bit)
ADDR
DATA (32bit)
DATA
SACIrsp (serial signal):
SET (1bit)
1
RW (1bit)
1
CMD (7bit)
CMD
ADDR (12bit)
ADDR
SET (1bit)
1
RW (1bit)
0
CMD (7bit)
CMD
ADDR (12bit)
ADDR
DATA (32bit)
DATA
Write Mode
Read Mode

## Slide 28: Pixels Configuration
SET (1bit)
1
RW (1bit)
0
CMD (7bit)
8
ADDR (12bit)
0
DATA (32bit)
0
CMD = End Configuration
Matrix configuration time pixel by pixel is: 110ms

## Slide 29: Global Register Map
The registry store the ASIC configuration settings needed for the DACs and the control unit.
Radiation tolerant register.
Set the initial condition to guarantee correct DACs and control unit settings using the global reset signal (GR).

## Slide 30: Global Registers Configuration
SET (1bit)
1
RW (1bit)
1
CMD (7bit)
1
ADDR (12bit)
ADDR
DATA (32bit)
DATA
- WRITE Configuration Registers:
- READ Configuration Registers:
SET (1bit)
1
RW (1bit)
0
CMD (7bit)
1
ADDR (12bit)
ADDR
DATA (32bit)
x

## Slide 31: Hit Encoding – Processing the Strip Encoding
SKIP
+1
Bit line settling
Write Bit
500ps
150ps
4ns
300ps
SKIP
+1
Bit line settling
Write Bit
500ps
150ps
0.8ns
300ps
Worst case scenario:
22ns
7.6ns