## Slide 1
HR-CHESS2 Update
D. Das, STFC-RAL, UK
29/09/15
ATLAS CMOS Strip
Regular Meeting
29/09/15
Notes: 1

## Slide 2
HR-CHESS2 Pre-Amplifier v2 Block Diagram
2
Leakage Compensation
Active Feedback
AC coupled to block leakage current, MOS device used to bias diode
Integrated AC coupling capacitor
Constant current feedback
Folded cascode architecture with source-follower inside feedback loop

## Slide 3
HR-CHESS2 Pre-Amplifier v3 Block Diagram
3
Leakage Compensation
Active Feedback
- Removed source-follower from feedback loop

## Slide 4
HR-CHESS2 Time-Walk Specification
Dependence of comparator fire time on signal must be < 1 BX i.e. 25ns
≤ 16 ns time difference between comparator leading edges for input signal of size
500 e- and 5000 e- with a threshold set at 275 e-

## Slide 5
 | NOM | FAST | SLOW
+40°C | 10.54ns | 9.37ns | 11.02ns
-40°C | 7.5ns | 7ns | 8ns
Time-Walk (~10ns charge collection time)
 | NOM | FAST | SLOW
+40°C | 6.95ns | 6.5ns | 7.9ns
-40°C | 5.32ns | 4.9ns | 6.2ns
Time-Walk (~1ns charge collection time)
HR-CHESS2 Time-Walk Simulations
Threshold adjusted for each
process corner (small differences)
Specification < 16ns
Meets specification in all corners

## Slide 6
HR-CHESS2 Design Progress Summary
Modified pre-amplifier design to make it faster & more immune to leakage current
Looking into design of pre-amplifier feedback capacitor as it’s small ≈ 1fF
Simulating Trim DAC for comparator offset compensation
Preparing for layout of the design
Preparing documentation for the first design review of HR-CHESS2
to be held mid to late October

## Slide 7
3-D structure for leakage current simulation
Pixel Volume = 40µm x 40µm x 25µm
Epi Depth = 25µm
No. of Pixels = 3
Type of Diode = N-Well/p epi
No. of Diodes per Pixel = 4
N-Well Bias = 1V
P-Well Bias = 0V
Back Contact Bias = 0 to -200V
Electronics inside Deep P-Well
Constant doping of epi and substrate
N-Well and P-Well has analytical doping profiles
HR p epi
>1KΩ-cm
P Substrate
Pixel 1
Pixel 2
Pixel 3
N-Wells
40µm
40µm
25µm

## Slide 8
Leakage current vs bias at different fluences
Back Bias varied from 0V to -200V (until breakdown)
Current of Pixel 2 (middle) recorded
Leakage current < 500pA for fluence of 1x1016 neq [cm-2]
Radiation Damage Model Used:
D. Pennicard et al. / Simulations of radiation damaged 3D detectors for the Super-LHC NIMA 592 (2008) 16–25 IEEE Trans. Nucl. Sci., vol. 53, pp. 2971–2976, 2006 “Numerical Simulation of Radiation Damage Effects in p-Type and n-Type FZ Silicon Detectors”, M. Petasecca, F. Moscatelli, D. Passeri, and G. U. Pignatel
Temp. = 27° C
Breakdown voltage increases
with fluence because effective
doping concentration increases
with irradiation!

## Slide 9
Leakage current vs geometry
During simulated irradiation dark current increases linearly with fluence:
From simulation results at 27°C:
α ≈ 80 x 10-18 A/m
Bias = -60V
Temp. = 27° C
Geometry | Leakage Current @ 1 x 1016 neq [cm-2]
40µm x 25µm x 40µm | 3.2pA
40µm x 25µm x 80µm | 6.4pA
40µm x 25µm x 120µm | 9.6pA
40µm x 25µm x 200µm | 1.6nA
40µm x 25µm x 400µm | 3.2nA
40µm x 25µm x 800µm | 6.4nA