## Slide 1: Overview and Status of the AGIPD Project December 2015- XDAC - Meeting

## Slide 2: AGIPD ASIC
AGIPD 1.0
Pixel (4096)
Readout chain
CDS stage
Preamplifier stage
Cf, high
Cf, mid
Cf, low
Preamp RST
Ccouple
CDS RST
Cf, CDS
Vref
Dynamic
gain
switching
DAC
Storage
cell matrix
Storage
cell matrix
Pixel buffer
PXB RST
Cf, PXB
Double column
buffer (64)
even row
odd row
Mux
Offchip drver
(4)
Cmd based IF, periphery, DACs
Correlated double sampling
Adaptive gain
Cf=60fF, 3pF, 10pF
Analog RAM 352 images

## Slide 3
2 x 8 chips = 128 x 512 pixels
Module

## Slide 4: AGIPD 1Mpixel-system
Independently movable quadrants
Modules of 2x8 chips
Variable hole in size & shape
Image plane out of vessel
External electronics

## Slide 5
Mechanical System Assembly started
Cooling blocks, adapters, counter weights, mounting tables + tubes holders, parts for adjustment of cooling blocks
Cooling blocks: ready (2 pcs.)
Adapters: ready
Counter weights: ready
Mounting tables: ready
Tube Holders: ready
Parts for Adjustment: ready

## Slide 6
Mechanical System Assembly started
Holders and bits and pieces to assemble the quadrants  ready
Device to turn assembled quadrants  ready
6

## Slide 7
Vacuum chambers nearly finished
Vacuum chambers  delivery scheduled for week 50
Tables for vacuum chambers: ready

## Slide 8
Firmware ready for multi-modules
Status
  Pixel descrambling in FW 
  Prototype: Ctrl FPGA 4x Readout (Quadrant)
    All 4 simultaneously working modules behavior as expect 
    No ASICs Module attached yet: More tests!
  Real time parameters adjustment for different systems (network parameters, readout modes, delays, automatic ADC tuning, …) 
  Dedicated Readout configuration regardless number of used modules and type of Back-up system 
  Versatile communication protocol ( already implemented in TANGO server, moving to KARABO)
  10GE train data in XFEL Train builder format 
  10GE Train images can be sorted in increasing Pulse Id order

## Slide 9
Calibration framework established
Data from PC
Data from CS
Gain from X-ray
Dark (noise)
Droop
Gains for H/M/L
Gain bits for H/M/L
Noise value
Droop effect
3-N-tuple
Event structure
Each module has 512 (pixel Y) x 128 (pixel X) x 352 (cells/pixel) = 23068672 memory units (=events).
  Define criterion of quality:
    Which magnitudes to evaluate?
    Which threshold?
2-Data processing
  5 groups of data
  Gain and gain bits for H/M/L evaluated according to the information from PC, CS, and X-ray.
  Evaluation of noise
  Quantification of droop
  Results in 3D matrix shape for each
    D1: Pixel X
    D2: Pixel Y
    D3: Cell
4-Report
Pixel X
Pixel Y
Cell
Measurements
2D matrix (1 event per row).
  Include extra processed information: electronically dead? disconnected?
5-Reprocess data
  Define better approaches to the fittings
  Reinsert new data into old one
6-Exit loop
  According to fraction of units recovered?
  Fixed #iterations?
  Fixed #good units?
Pixel X
Pixel Y
Cell
Patterns
Raw measurements
Detector instrument
1-Operation AGIPD module
  Biasing to be optimized for -20C
  Data acquisition at 1G (Java) and data in binary files
  Data acquisition at 10G (TANGO) and data in HDF5 files
Gains for H/M/L
Gain bits for H/M/L
Noise value
Droop effect

## Slide 10
AGIPD1.0 is already useable for first experiments
All non-perfect issues observed in AGIPD 1.0 understood and remediated in AGIPD 1.1
AGIPD 1.1 uploaded to MOSIS end of November; usual discussions ongoing
If all goes well AGIPD 1.1 back in April 2016
ASIC redesigned and “submitted”

## Slide 11
Mechanical integration ongoing
First version Firmware for multi-modules working
Calibration framework established and most routines coded (remaining work not to be underestimated)
ASIC redesign finished and uploaded to MOSIS
Status summary

## Slide 12
Assembly of mechanics (1st part) finished January; 2nd part April 2016
Electronics and operational testing multi-module system finished early 2016
Calibration framework finished early 2016
Assembly and testing entire system finished June 2016
Delivery to XFEL summer 2016
Replacement of AGIPD1.0 with AGIPD 1.1 possible before first beam
Planning