## Slide 1
Status & Summary from last meeting
Way Forward
Modules Design
Petal Layouts

## Slide 2
Identify Folks willing to:
  Consider module concepts, including assembly
    Will help but not drive
  Interact with petal/stave designers over sensor sizes, power, new tape layout, …(probably subsumed into first)
  Work on hybrid electrical design & sensor backend layouts
  Interact with chip designers over HCC/ABCN’/EoS
  Build dummy modules & then Build electrical modules
  Evaluate thermal performance of staves/petals
    (Transverse thermal conductivity dominated by silicon)
  ABCn’ FPGA version
  Test
    Electrical
    mechanical
Way Forward
Possible interest expressed

## Slide 3
Organisation:
Meet regularly & report to main meeting
  Monthly
  Generates deadlines for work
Goals for end of calendar 2015 :
  Conceptual module design selected
  Detailed sensor layout agreed to match existing mechanics
  Assembly process
  Dummy module planned & parts on order

## Slide 4
Module Concepts
Two basic variants identified
Baseboard
thermally conductive
rigid
low mass
Sensor
Hybrid
ABCn’
stripCMOS module - A
Baseboard may be hybrid
Extra mass?
(half shown, reflected through LHS)

## Slide 5
Sensor
ABCn’
stripCMOS module - GK
Hybrid

## Slide 6
X < 22 mm
Y < 26 mm
Whole reticule must fit inside a circle of diameter 31.112 mm
  (so max sized square has a side of length 21.9995 mm)
  ( ymax = sqrt[967.9565 – x2] )
  (20,23.83); (19,24.64); …
Circle (x2)
Max X by Max Y (x2)
cant have both at the same time (maybe)
AMS 350
Reticule size limitations

## Slide 7
10cm
20 x 23.83 reticules
47.66
10 x 43 active
Use of wafer?
Not good width to make blocks
Barrel relatively ‘easy’

## Slide 8
Petal Concepts
Ragged edge vs Thermal asymmetry

## Slide 9
Still need to identify someone to drive concepts
  In interim will be done by Marcel, Richard, Vitaliy
Need to identify a route for ABCn’ FPGA version
  Ideas for people to date not viable
Summary
Once monthly meetings
Goals for 2015 identified