## Slide 1: CMOS Petal Design First Ideas ..
Richard, Marcel, Vitaliy

## Slide 2: Assumptions
Need to cover same sensor area as baseline petal
Can’t do trapezoids etc in CMOS
But we can use front and back of the petal
As these are 3D space points, rotation, etc, don’t matter
Keep it simple
  Tile Petal with one set of sensor
  Stay close to barrel design

## Slide 3: New Idea
Petal Module
  Basic building block
  4 x 8 cm
  8 chips (2 x 2 cm)
Front Side
  20 Modules
Back Side
  15 Modules
35 Modules per Petal
Front
Back

## Slide 4: Overlap…
There is a non-zero overlap between front and back
  Red area is where one will get 2 3D Points (bonus ..)

## Slide 5: Gaps …
There are “non-zero gaps
  Butting modules
  Dead area from end-of-chip electronics
Idea: Staggering
  May introduce some bonding issues ….

## Slide 6: Food for thought
If we are lucky (and all fits ..)
  One set of “Module” for the Tracker
Questions
  Will Tracking be able to cope with ~5 degree rotated pixels of 40 x 800 µm?
  Bustape, Power, etc will need adjustments
  Which gaps are tolerable ?