## Slide 1: Lab report : Johannes Gutenberg-Universität Mainz „Photocathodes for high brightness beams“ „HOPE“/“HOPE-II“
Kurt Aulenbacher, for JGU-team
K.A, Victor Bechthold, Monika Dehn, Simon Friederich,
Nahid Scahill

## Slide 2: Mainz Labs
Photocathode research issues at JGU
Status: „PKAT“-LAB - Photocathode physics with time resolved techniques (PCHB-project)
New: - STEAM/MELBA-Set-up for high average bunch charge operation (Hope/Hope-II)

## Slide 3
Photocathodes: Crystals….
- Epitactically grown semiconductor (Superlattice) crystal
Grown in MBE-apparatus
Commercial supply (e.g. SVTA)
or research institution (e.g. SPTU)
Theoretically well understood
- Enables spin polarization
High(est?) brightness (NEA, thermalization)
Best Quantum efficiency
-but extremely sensitive...too sensitive?
Research issues:
-Extremely low work function:
 field emission?
NEA&diffusion
 diffusive longitudinal Halo?
Inelasitic escape process
 transit time spread is limiting
response time
L. Gerchikov, E. Riehn, JGU 2011
Jin et al. , ULTRAMICROSCOPY
130 (2013) 44-48
F~1,5eV

## Slide 4
Photocathodes: …. and Films
Films on substrates
- KCsSb
-Cs2Te
Crystal composition
requires sophisticated
control see data
Lower QE
But More robust
Work function depends
on material 1-4 eV
Research issues:
- Energy spectrum?
Exponential longitudinal halo?
Field emission/field tolerance?
F~2eV
V. Bechthold
V. Bechthold
KCsSb@JGU

## Slide 5
Experimental Setup at PKAT
e- Bunch
Laser
Deflector Cavity
Slit in
“Thomson-
Chamber”
RF Deflection
700 mm
Channeltron
Generation of short electron bunches:
Laser pulse (red), Electron bunch (green), synchronously with RF
Electron Gun
Spin-rotator
Spin-detector
(Mott Polarimeter)
Faraday Cup

## Slide 6
Experimental Setup at PKAT- 3 Functionalities
1.) Pulse response measurement
e- Bunch
Laser
Deflector Cavity
Generation of short electron bunches:
Laser pulse (red), Electron bunch (green), synchronously with RF
Electron Gun
Short bunch, high
dynamic range diagnostics

## Slide 7: Time Response Measurements Principles
Active Phase Stabilization
≈
RF Master
Solid State Amplifier
Deflector
Cavity
:32
Freq. Divider
Cathode
DBM
76MHz-Filter/ Photodetector
Phase Shifter
Laser
Slit
YAG Screen
Detector/
Channeltron
CCD Camera
Beamsplitter
Conversion of the longitudinal profile into transversal profile by TM-110 RF Deflector Cavity
Electron bunches must be emitted synchronously to RF Master
Longitudinal profile directly visible on the screen (intensity) or can be sampled by a Channeltron Detector
Time resolution essentailly limited by measurement speed, streak amplitude
(improved during PCHB project s<1ps)

## Slide 8: Time Response Measurements Comparison of Different Types of Photocathodes
Surprise: GaAs at 400nm almost as good as PCA (higher absorption!)
10-4 long. Halo: Laser artefacts?
Present measurements (V. Bechthold, M. Dehn): Deconvolution + optimization Dynamic range, clarify systematic errors & artefacts
Preliminary
Source: Kirsch, E.: Johannes Gutenberg Universität Mainz, Diplomarbeit, 2014
Data obtained 2013
Long period of
Apparatus failures and
Repairs
M. Dehn, E. Kirsch

## Slide 9
L. G. Gerchikov, K. Aulenbacher, Yu. A. Mamaev,
E. J. Riehn and Yu. P. Ya-
shin in Journal of Physics: Conference Series
298 (2011) 012013
Polarization Response Measurements Comparison of Different Types of Superlattices
Remark: Spin rotatator dismantled in 2011 new arrangement based on Wien filter
(Nahid Scahill) is ready for installation.

## Slide 10
New SOURCE is available:
Inverted Gun with VARIABLE Extraction Field
Objectives (HOPE-II application)
- Measure Energy spectrum via transit time spread (0.4-3.5 MV/m)
- Measure field-tolerance of low workfunction cathodes to fields >3.5 MV/m
Chart: Envelopes
M. Dehn

## Slide 11
The STEAM project (Hope/Hope-2):
Objective: Make use of thermalized ensembles T~300K
 Small Thermalized Electron-source At Mainz (STEAM)
 To achieve ‚relevant‘ bunch charges Potential and field should be large enough
- Assume that an accelerator has an acceptance given by elim and electron
source is limited by (external) space charge
- In „flat field“ approximation on observes

## Slide 12
The STEAM project (Hope/Hope-2):
STEAM:= small thermalized Electron apparatus at MAINZ
high brightness at „reasonable“ Bunch charge?
Reasonable means FemtoScienceFacility or MESA
200keV source with Gradient ~5MV/m
Bunch characterization by MESA low energy beam apparatus (MELBA)

## Slide 13
The STEAM project (Hope/Hope-2):
STEAM:= small thermalized Electron apparatus at MAINZ
Predicted vacuum space charge effects for ‚reasonable‘ MESA bunch length (200ps)
Compared to MESA standard source PKA2
Transverse normalized emittance (CST-simulations)
MESA-1/2
Preliminary)

## Slide 14
The STEAM project (Hope/Hope-2):
STEAM:= small thermalized Electron apparatus at MAINZ
Predicted vacuum space charge effects for ‚reasonable‘ MESA bunch length
Preliminary)

## Slide 15: Conclusion
Two projects (PCHB, HOPE)
Photcathode apparatus are difficult to handle, slow progress
Nevertheless some good results (PCA available , GaAs response, )
New hardware developed which may clarify many issues concerning
field tolerance of low work function cathodes, low intensity halo, high brillance...

## Slide 16: Time Response Measurements Limits of the Resolution
Limits by the Experimental Setup
  Phase Stability (Jitter and Drift of the RF Cavity)
    Jitter (fast) mainly due to the Laser Systems
    Drifts (slow) by thermal effects
     depends on measurement time  (2002)  <0.5ps (1s) (2015)
  Finite transversal size of the electron bunch
    “Deflection speed“ on the screen ~400µm/ps at minimum transversal size of ~200µm  , can be improved by smaller emittance
    Size of Laser spot on Cathode affects bunch size (Emittance)   
  
“x”, Physical Limits (beam transport)
  Longitudinal dispersion caused by distribution of kinetic energy at emission
  
 Varying electrical field gradient allows disentengling energy and time response!

## Slide 17: Inverted Electron Gun
Insulator for Power Supply (-90kV – 0kV)
Laser
Electron Beam
Cathode
Exchange
Insulator for Power Supply (-100kV)
Cathode: Puck with Semiconsuctor
Intermediate Electrode
Anode
10 NEC-Modules
30mm
150mm
600mm
400mm

## Slide 18: Inverted Electron Gun Electrical Field Simulations with CST© Studio Suite
Intermediate electrode:
U = 0kV
Intermediate electrode:
U = -90kV
3.5 MV/m
0.5 MV/m

## Slide 19: Inverted Electron Gun Particle Tracking: Envelopes
The beam can come out of the source, with reasonable paramters
for all extraction fields
Chart: Envelopes

## Slide 20: Inverted Electron Gun Particle Tracking: Emittances
Chart: Emittances

## Slide 21: Inverted Electron Gun Mechanism for Cathode Exchange
A challenge for the workshop
  A new cathode exchange mechanism was need
Moving the manipulator / closes the ‚scissors‘
30mm

## Slide 22: Status and Outlook
Status
  Vacuum chamber
    The chamber is ordered and the company is finishing the blueprint.
  Vacuum pumps
    NEC-Modules and power-supply are already delivered.
    IGP and power-supply is ordered.
  Other mechanical components
    The blueprints have to be finalized for the mechanical workshop in house.
Outlook and timescale
  September 2015
    All mechanical and electrical components should be delivered and/or manufactured.
    Start of mounting the components.
  October 2015 – January 2016
    Mounting inside the laboratory.
  February 2016 – August 2016
    Commissioning of the new electron source.
    Time resolved measurements.

## Slide 23
Thank you for attention.

## Slide 24
Backup

## Slide 25: Fundamentals Semiconducting photocathodes
Cs:GaAs
  Homogenous crystalline structure
  Negative electron affinity (NEA)
K2CsSb
  = PCA (Potassium Cesium Antimonide)
  Multicrystalline structure
  Positive electron affinity (PEA)
EVal
EL
optical pumping
e-
transport
tunneling
e-
thermalization
EV
solid
vacuum
χ
E
valence band
x
EVal
EL
optical pumping
e-
thermalization
e-
emission
no emission
EV
solid
vacuum
χ
E
x
valence band

## Slide 26: Fundamentals Photoemission from Semiconductors
Absorption
  Condition:
  Absorption coefficient:
Diffusion model for GaAs-photocathodes
  Electron motion only by diffusion, not by scattering: And the solution
  Emitted current: with and
Zeit [ps]
Normierte Intensität
λ=800 nm
λ=400 nm
Time [ps]
Normalized Intensity

## Slide 27: Time Response Measurements Principles
Active Phase Stabilization
≈
RF Master
Solid State Amplifier
Deflector
Cavity
:32
Freq. Divider
Cathode
DBM
76MHz-Filter/ Photodetector
Phase Shifter
Laser
Slit
YAG Screen
Detector/
Channeltron
CCD Camera
Beamsplitter
Conversion of the longitudinal profile into transversal profile by TM-110 RF Deflector Cavity
Electron bunches must be emitted synchronously to RF Master
Longitudinal profile directly visible on the screen (intensity) or can be sampled by a Channeltron Detector

## Slide 28
Time Response Measurements Experimental Setup at PKAT
e- Bunch
Laser
Deflector Cavity
YAG Screen/
Slit
RF Deflection
700 mm
Channeltron
Generation of short electron bunches:
Laser pulse (red), Electron bunch (green), synchronously with RF
Electron Gun

## Slide 29: Time Response Measurements Measurements with Bulk-GaAs
= 2.37 ps
= 2.29 ps
Beam profile YAG-screen
  CW-beam (no single bunch)
  Intensity distribution complies to the convolution of the transverse beam profile and the time response
Source: Kirsch, E.: Johannes Gutenberg Universität Mainz, Diplomarbeit, 2014
241 µm
Time structure
Transverse beam profile
Without RF
With RF
241 µm
Longitudinal Beam Profile, σ = 2.37ps
Transverse Beam Profile, σ = 0.58ps
Bunch length, σ = 2.29ps
Normalized Intensity
Time [ps]

## Slide 30: 100keV Electron Gun Variable Extraction Field Gradient
Purposes of the new electron gun
  Variable field gradient at the surface of the cathode
  Examination of longitudinal divergence, i.e. comparison of different bunch lengths at same charge
Compact design based on the inverted gun of CEBAF at JLAB
  HV supply with cone shaped Insulator reaching into the vacuum chamber
    Lesser field emission compared to conventionally used larger ceramics
    Well-proven design of the insulator (X-Ray tubes)