## Slide 1: Enstore Demo
10th international dCache users workshop
April 11-12, 2016, Hosted by PIC
Barcelona, Catalunya
Dmitry Litvintsev

## Slide 2: Intent
Goal of this demo is to perform installation and configuration of Enstore system on 4 computers provided to us by PIC
Basically we will just follow Enstore Administration guide:
  http://www-ccf.fnal.gov/enstore/Enstore_Administrator_Guide.pdf

## Slide 3: Preliminaries
We have 4 hosts:
  ensws01, ensws02, moverws01, moverws02
moverws01 has rsh access to SL8500 ACSLS control host (Automated Cartridge System Library Software).
moverws01 and moverws02 are connected to drives in SL8500 library (one drive per node).
Media is LTO4
Chimera NFS server is dccore01-pps

## Slide 4: System Layout
ensws01 will be our “main” node, running databases, clerks, configuration, web-server and Inquisitor.
ensws02 will run Library Managers, “null” movers and host database backup.
moverws01 will run Media Changer and mover
moverws02 will run mover

## Slide 5: Distribute Enstore Repo file
cat enstore.repo
[enstore]
name=Enstore
baseurl=ftp://ssasrv1.fnal.gov/en/sl6x/$basesearch
enabled=1
gpgcheck=0
for host in ensws01 ensws02 moverws01 moverws02;
do
scp enstore.repo root@${h}:/etc/yum.repos.d;
done

## Slide 6: Install Postgresql
for h in ensws01 ensws02 moverws01 moverws02
do
ssh root@${h} "yum install -y http://yum.postgresql.org/9.4/redhat/rhel-6-x86_64/pgdg-redhat94-9.4-1.noarch.rpm”
ssh root@${h} "yum install -y postgresql94 postgresql94-libs postgresql94-server postgresql94-contrib”
done
setup alternatives on ensws01 (this step is needed only b/c we run postgres as user enstore)
VER="9.4"
for PROG in "initdb" "pg_ctl" "pg_config" "postmaster" "psql"; do
rm -f /var/lib/alternatives/pgsql-${PROG};
/usr/sbin/alternatives --install /usr/bin/${PROG} pgsql-${PROG} /etc/alternatives/pgsql-${PROG} 920 --slave /etc/alternatives/pgsql-${PROG} pgsql-${PROG} /usr/pgsql-${VER}/bin/${PROG};
rm -f /var/lib/alternatives/pgsql-${PROG}man;
/usr/sbin/alternatives --install /usr/share/man/man1/${PROG}.1 pgsql-${PROG}man /etc/alternatives/pgsql-${PROG}man 920 --slave /etc/alternatives/pgsql-${PROG}man pgsql-${PROG}man /usr/pgsql-${VER}/share/man/man1/${PROG}.1;
done
(above gets initdb, pg_config, postmaster, psql into /usr/bin)

## Slide 7: Install Enstore and dependencies
export HOSTS="ensws01 ensws02 moverws01 moverws02"
for h in ${HOSTS};
do
ssh root@${h} “yum -y install mt-st tcl tk enstore”;
done
#enstore installs into /opt/enstore
#on ensws01 install:
yum -y install ncompress gnuplot ImageMagick httpd

## Slide 8: Enstore environment
# copy .bashrc from distribution
for h in ${HOSTS};
do
ssh root@${h} "cp /opt/enstore/external_distr/.bashrc ~enstore”;
done

## Slide 9: ensws01
# web pages will go here:
mkdir -p /var/www/html/enstore/web-pages
chown -R enstore:enstore /var/www/html/enstore
# setup files
su enstore
cd ~enstore
mkdir –p site_specific/config
cp /opt/enstore/site_specific/config/setup-enstore \ site_specific/config
cp /opt/enstore/etc/enstore_configuration_template \ site_specific/config/enstore.conf

## Slide 10: Configuration
# define enstore environment
# edit ~enstore/site_specific/setup-enstore and
# define:
export ENSSH=/usr/bin/ssh
export ENSCP=/usr/bin/scp
export ENSTORE_CONFIG_HOST=ensws01
export ENSTORE_CONFIG_PORT=7500
export ENSTORE_CONFIG_FILE=/home/enstore/\ site_specific/config/enstore.conf ENSTORE_MAIL=youmail@example.com
export FARMLETS_DIR=/usr/local/etc/farmlets
# now copy ~enstore/site_specific/setup-enstore to other 3 hosts

## Slide 11: Edit configuration file (1)
# straightforward but tedious, editing
~enstore/site_specific/config/enstore.conf
system_name="EnstoreWS”
enstore_head_node="ensws01.pic.es”
monitoring_and_web=enstore_head_node
enstore_DB=enstore_head_node
enstore_backup="ensws02.pic.es”
enstore_library="ensws02.pic.es”
enstore_pnfs="dccore01-pps.pic.es”
media_changer_host="moverws01.pic.es"
html_dir = "/var/www/html/enstore/web-pages"
log_dir = "/var/log/enstore"
backup_dir = "/home/enstore/backups"
inventory_dir = "/home/enstore/db-inventory"
httpd_dir = "/var/www/html/enstore”
ratekeeper_dir = "/home/enstore/ratekeeper"
db_basedir = "/home/enstore/databases”

## Slide 12: Edit configuration file (2)
# we need connection to chimera to be able
# to mark files bad when they appear in
# t_location_info_trash table
configdict['namespace'] = {
system_name : {'dbname' : 'chimera',
'dbhost' : enstore_pnfs,
'dbport' : 5432,
'dbuser' : 'srmdcache' },
}

## Slide 13: Edit configuration file (3)
# allow these subnets to connect to config server:
configdict['domains'] = {
'invalid_domains’: [],
'valid_domains’ : ['192.168.20','193.109.174','193.109.172'],
}

## Slide 14: Edit configuration file (4)
# configure crons
configdict['crons'] = {
'web_node' : monitoring_and_web,
'html_dir' : html_dir,
'log_dir' : log_dir
'tmp_dir' : "/tmp",
'email' : ”litvinse@fnal.gov", # put here operation email address
'developer_email' : "moibenko@fnal.gov", # put here developers email
'backup_node' : enstore_backup,
'backup_dir' : backup_dir,
# Only on the following nodes are the ecron outputs monitored
'monitored_nodes' : [
enstore_head_node,
enstore_DB,
enstore_backup,
enstore_library,
enstore_pnfs,
],
'farmlets_dir' : "/usr/local/etc/farmlets",
'url_dir' : "http://ensws01.fnal.gov/enstore/", # make it up
'enstore_name' : "EnstoreWS", # make it up
'spool_dir' : "/home/enstore/MigrationSpool", #make_failed_copies
'backup2tape_dir' : "/pnfs/pic.es/data/enstore-ws/backup", # replace with name of backup directory in name space
'copy_ran_file_log_dir' : "/home/enstore/copy_ran_file",
}

## Slide 15: Edit configuration file (5)
# configuration for presentation of system by inquisitor on web \ page(s)
configdict['www_server'] = { 'system_tag' : "EnstoreWS: Enstore for the Enstore Workshop", # make up the name
'media' : {
'1' : 'Robot at PIC',
},
'inq_ignore' : 1 }

## Slide 16: Edit configuration file (6)
# configure Library Manager
configdict['LTO4.library_manager'] = {
'host':library_manager_host,
'port':8546,
'logname':'LTO4LM',
'norestart':'INQ',
'max_encp_retries':3,
'max_file_size':(5000L*GB) - 1,
'min_file_size':300*MB,
'max_suspect_movers':3,
'max_requests':15000,
'restrict_access_in_bound': True,
'CleanTapeVolumeFamily': 'CLEAN.CleanTapeFileFamily.noWrapper',
'suspect_volume_expiration_time':3600*24,
'legal_encp_version':legal_encp_version,
'blank_error_increment': blank_error_increment,
'mover_port': 7020,
'encp_port':7021,
'use_threads':False,
'use_raw_input': 1,
}

## Slide 17: Edit configuration file (7)
# STK media changer
configdict['SL8500.media_changer'] = {
'host':media_changer_host,
'port':7508,
'logname':'SL8500G1MC',
'type':'STK_MediaLoader',
'norestart':'INQ',
'max_work':6,
'acls_host':'acsls', # ACSLS controller host
’acls_uname':'acsss', # ACSLS user name
'DriveCleanTime':{'LTO3':[60,1],
'LTO4':[60,1],
'T10000T2':[60,1],
},
'tape_library':"GCC StreamLine 8500",
}

## Slide 18: Configure Movers (1)
# build tape devices
# on moverws01 as a root:
source ~enstore/.bashrc
/etc/rc.local
Making SCSI device files: [ OK ]
[root@moverws01 ~]# ls -al /dev/rmt
total 0
drwxr-xr-x 2 root root 80 Mar 25 18:14 .
drwxr-xr-x 20 root root 3880 Mar 25 18:14 ..
crw-rw-rw- 1 root root 9, 0 Mar 25 18:14 tps9d0
crw-rw-rw- 1 root root 9, 128 Mar 25 18:14 tps9d0n
goes to config

## Slide 19: Configure Movers (2)
# build tape devices
# on moverws02 as a root:
source ~enstore/.bashrc
/etc/rc.local
Making SCSI device files: [ OK ]
[root@moverws02 ~]# ls -al /dev/rmt
total 0
drwxr-xr-x 2 root root 80 Apr 8 23:54 .
drwxr-xr-x 20 root root 3920 Apr 8 23:54 ..
crw-rw-rw- 1 root root 9, 0 Apr 8 23:54 tps3d0
crw-rw-rw- 1 root root 9, 128 Apr 8 23:54 tps3d0n
goes to config

## Slide 20: Configure Movers (3)
# determine mc device
# on moverws01:
[root@moverws01 ~]# ls -1 /dev/tape/by-path
pci-0000:05:02.1-fc-0x500104f000a42443-lun-0
pci-0000:05:02.1-fc-0x500104f000a42443-lun-0-nst
# on moverws01 query acsls
rsh -l acsss acsls "echo 'display drive * -f wwn \r logoff' | bin/cmd_proc -l -q " | egrep ”42$"
--------Oracle ACSLS (Automated Cartridge System Library Software) 8.2.0-------
Copyright 1989, 2012 Oracle and/or its affiliates. All rights reserved.
0 3 1 0 50.01.04.f0.00.a4.24.42
Look for number that is 1 less
Goes to config

## Slide 21: Configure Movers (4)
# determine mc device
# on moverws02:
[root@moverws02 ~]# ls -1 /dev/tape/by-path
pci-0000:05:02.1-fc-0x500104f000a424c7-lun-0
pci-0000:05:02.1-fc-0x500104f000a424c7-lun-0-nst
# on moverws01 query acsls
rsh -l acsss acsls "echo 'display drive * -f wwn \r logoff' | bin/cmd_proc -l -q " | egrep "c6$"
--------Oracle ACSLS (Automated Cartridge System Library Software) 8.2.0-------
Copyright 1989, 2012 Oracle and/or its affiliates. All rights reserved.
0 0 1 1 50.01.04.f0.00.a4.24.c6
Look for number that is 1 less
Goes to config

## Slide 22: Configure Movers (5)
configdict['LTO4_01.mover'] = {
'host':'moverws01',
'data_ip':'moverws01',
'port':7903,
'logname':'LTO4_01MV',
'statistics_path':'/tmp/enstore/enstore/LTO4_01.stat',
. . .
'check_written_file':lto4_mvr_check_f,
'check_first_written_file':lto4_mvr_check_1st,
'min_buffer':lto4_min_buffer,
'max_buffer':lto4_max_buffer,
'max_rate': lto4_rate,
'mount_delay':15,
'update_interval':lto4_update_interval,
'library':'LTO4.library_manager',
'device':'/dev/rmt/tps9d0n',
'driver':'FTTDriver',
'mc_device':'0,3,1,0',
'media_changer':'SL8500.media_changer',
. . .
'dismount_delay': lto4_dismount_delay,
'single_filemark': 1,
}

## Slide 23: Configure Movers (6)
configdict['LTO4_02.mover'] = {
'host':'moverws02',
'data_ip':'moverws02',
'port':7903,
'logname':'LTO4_02MV',
'statistics_path':'/tmp/enstore/enstore/LTO4_02.stat',
. . .
'check_written_file':lto4_mvr_check_f,
'check_first_written_file':lto4_mvr_check_1st,
'min_buffer':lto4_min_buffer,
'max_buffer':lto4_max_buffer,
'max_rate': lto4_rate,
'mount_delay':15,
'update_interval':lto4_update_interval,
'library':'LTO4.library_manager',
'device':'/dev/rmt/tps3d0n',
'driver':'FTTDriver',
'mc_device':'0,0,1,1',
'media_changer':'SL8500.media_changer',
. . .
'dismount_delay': lto4_dismount_delay,
'single_filemark': 1,
}

## Slide 24: We are done with Config!
# lets start the config server
# on ensws01:
enstore start –-just config
# check that it works:
enstore conf –show

## Slide 25: Make Farmlets
# Farmlets are used to run enstore
# cluster commands (like Estart and Estop)
# on ensws01 as root:
source ~enstore/.bashrc
/opt/enstore/external_distr/make_farmlets.sh
ls /usr/local/etc/farmlets/
dccore01-pps enstore enstore-down ensws01 ensws02 movers moverws01 moverws02 servers

## Slide 26: Create web-serer config
[root@ensws01 ~]# /opt/enstore/sbin/install_enstore_html
Stopping httpd: [FAILED]
CONF /etc/httpd//conf/httpd.conf
Writing file /etc/httpd//conf/httpd.conf Root /etc/httpd/
exists False /var/www/html/enstore/html/enstore
log directory /var/log/enstore
CONF /etc/httpd//conf/httpd.conf
Starting httpd: [ OK ]
[root@ensws01 ~]#
# check that this worked:
http://ensws01.pic.es/enstore/

## Slide 27: Databases
# create databases, on ensws01:
as root
source ~enstore/.bashrc:
python $ENSTORE_DIR/sbin/create_database.py enstoredb
python /opt/enstore/sbin/update_database_schema.py enstoredb
psql -h ensws01.pic.es -p 8888 -U enstore enstoredb -f enstoredb_update.sql
python $ENSTORE_DIR/sbin/create_database.py accounting
python /opt/enstore/sbin/update_database_schema.py accounting
psql -h ensws01.pic.es -p 8800 -U enstore accounting -f accounting_update.sql
python $ENSTORE_DIR/sbin/create_database.py drivestat
python /opt/enstore/sbin/update_database_schema.py drivestat
psql -h ensws01.pic.es -p 8802 -U enstore drivestat -f drivestat_update.sql

## Slide 28: Install crons
#install crons:
# as root pm ensws01:
source ~enstore/.bashrc
python $ENSTORE_DIR/tools/install_crons.py

## Slide 29: Start Enstore
# either run
enstore Estart
# or run
enstore start
# on each node

## Slide 30: Define tapes
# on ensrvws01:
for v in G05501 G05502 G05503 G05504 G05505; do
enstore vol --VOL1OK --bypass-label-check --add ${v} LTO4 none none none LTO4 800GB
done

## Slide 31: Install encp client
# on dccore01-pps
wget ftp://ssasrv1.fnal.gov/en/slf6x/x86_64/encp-ups-opt-dcache-v3.11c-1.x86_64.rpm
rpm –iencp-ups-opt-dcache-v3.11c-1.x86_64.rpm

## Slide 32: Create directory tags
# on dccore01 (for instance):
mount -v -o vers=3 dccore01-pps:/pnfs /mnt
mkdir /mnt/pic.es/data/enstore-ws
chown enstore:enstore /mnt/pic.es/data/enstore-ws
cd /mnt/pic.es/data/enstore-ws
echo “test” > “.(tag)(file_family)”
echo “2” > “.(tag)(file_family_width)”
echo “cpio_odc” > “.(tag)(file_family_wrapper)”
echo “LTO4” > “.(tag)(library)”
echo “enstore” > “.(tag)(storage_group)”

## Slide 33: Try write and read file
export ENSTORE_CONFIG_HOST=ensws01
export ENSTORE_CONFIG_PORT=7500
# write
cd /mnt/pic.es/data/enstore-ws/test
/opt/encp/encp /etc/fstab fstab
#read
/opt/encp/encp /tmp

## Slide 34: Observe file in the system
# check layers
cd /mnt/pic.es/data/enstore-ws/test
cat “.(use)(1)(fstab)
CDMS146016281400000
cat ".(use)(4)(fstab)"
G05501
0000_000000000_0000001
855
test
/mnt/pic.es/data/enstore-ws/test/fstab
0000B7E20C2EAC0343739C41C37F867A2FF9
CDMS146016281400000
moverws01:/dev/rmt/tps9d0n:1310163670
2109462862

## Slide 35: That is it Folks!