Alignment with Beam Halo
A. Parenti (DESY)
28/10/2008

---
Combined Alignment (1)
CMSSW 2_0_12
Configurations (alignment at detector level):
  - alignParams = {"PixelDets,111001,pixEnd", "BarrelDetsDS,111001", "BarrelDetsSS,101001", "TIDDets,111001,tecDS", "TIDDets,101001,tecSS", "TECDets,111001,tecDS", "TECDets,101001,tecSS"}
  - GlobalTag.globaltag = "1PB_V2_RECO::All"
Samples:
  - CSA08 Minimum Bias (1PB_V2_RECO): 1M events
  - CSA08 Cosmics (1PB_V2_RECO): 3M events
  - CSA08 Beam Halo (STARTUP_V2): ~60k events
    - STARTUP_V2: same misalignment scenario as 1PB_V2_RECO

---
Combined Alignment (2)
Strategy:
  - align with cosmics and minimum bias
  - as above + beam halo (5x weight)
  - compare geometries
cosmic + minimum bias sample
  - 4203871 tracks
  - 44244 parameters to determine
cosmic + minimum bias + beam halo
  - 4492606 tracks (5x 57747 beam halo tracks in it)
  - same number of parameters

---
Combined Alignment (3)
TEC. Comparison to ideal geometry (Subdet global displacements are subtracted):
Dr=90 mm
Dz=200mm
rDf=90mm
Misaligned
geometry:
Dr=90 mm
Dz=150mm
rDf=35mm
Aligned w/
MinBias+
Cosmics:

---
Combined Alignment (4)
TEC. Comparison to ideal geometry (Subdet global displacements are subtracted):
Dr=90 mm
Dz=200mm
rDf=90mm
Misaligned
geometry:
Dr=90 mm
Dz=160mm
rDf=60mm
Aligned w/
MinBias+
Cosmics+
BeamHalo:

---
Combined Alignment (5)
TID. Comparison to ideal geometry (Subdet global displacements are subtracted):
Dr=280 mm
Dz=460mm
rDf=450mm
Misaligned
geometry:
Dr=240 mm
Dz=45mm
rDf=30mm
Aligned w/
MinBias+
Cosmics:

---
Combined Alignment (6)
TID. Comparison to ideal geometry (Subdet global displacements are subtracted):
Dr=280 mm
Dz=460mm
rDf=450mm
Misaligned
geometry:
Dr=240 mm
Dz=85mm
rDf=40mm
Aligned w/
MinBias+
Cosmics+
BeamHalo:

---
Combined Alignment (7)
Minimum bias and cosmics allow to align endcaps
  - noticeable improvement, especially in TID
Beam halo tracks do not help:
  - Too many parameters and few beam halo tracks? Waiting for 21X production
  - Moreover there are few tracks connecting the two endcaps... (maybe due to the reconstruction)

---
Beam Halo only alignment (1)
CMSSW 2_0_12
Configuration file (alignment of endcap high-level structures only):
  - alignParams = {"PixelDets,000000,pixEnd", "BarrelDetsDS,000000", "BarrelDetsSS,000000", "TIDRings,111000","TECPetals,110000"}
  - GlobalTag.globaltag = "1PB_V2_RECO::All"
Samples:
  - CSA08 Beam Halo (STARTUP_V2): ~60k events
Parameters to align: 630

---
Beam Halo only alignment (2)
TEC. Comparison to ideal geometry (Subdet global displacements are subtracted):
Dr=90 mm
Dz=200mm
rDf=90mm
Misaligned
geometry:
Dr=190 mm
Dz=200mm
rDf=130mm
Aligned w/
BeamHalo:

---
Beam Halo only alignment (3)
TID. Comparison to ideal geometry (Subdet global displacements are subtracted):
Dr=280 mm
Dz=460mm
rDf=450mm
Misaligned
geometry:
Dr=190 mm
Dz=1.3mm
rDf=400mm
Aligned w/
BeamHalo:

---
Beam Halo only alignment (4)
Alignment done on high-level structures only... but plots show displacement of detectors wrt to the subdetectors:
  - Are they significant? Probably not
  - Plots should be made of subdetectors' displacements wrt whole tracker

---
Status and Plans
Use of beam halo events together with minimum bias and cosmics in a global alignment
  - minimum bias and cosmics improve detectors' alignment
  - only small changes adding beam halo too (maybe too few tracks?)
Second attempt: beam halo standalone alignment of high-level structures in end-caps: ongoing
That's all.
Thanks!