## Slide 1: New ideas for axion like particle dark matter search
F. Caspers, K. Zioutas, M. Betz
2012

## Slide 2: Tore Supra
From wikipedia:
Tore Supra is the only one of the largest tokamaks to have superconducting toroidal magnets, allowing the creation of a strong permanent toroidal magnetic field
… it allows to test critical parts of equipment such as plasma facing wall components or superconducting magnets that will be used in its successor, ITER.

## Slide 3: Tore Supra
The machine might be available for axion search as its successor ITER becomes operational
It is equipped with a big (V = 30 000 l) and strong magnet (B = 4.5 T)
Large active volume for relic axion  photon conversion
We use the Tore Supra chamber as a big microwave resonator

## Slide 4: Tore Supra
Outer plasma diameter : | 4.8 m
Inner plasma diameter: | 1.6 m
Plasma volume | 30.3 m3
Toroidal magnetic field at the plasma centre : | 4.5 T
Maximum magnetic field on the conductor : | 9.0 T
Average diameter of a magnet coil : | 2.60 m
Dimension of NbTi superconductor : | 2.8 x 5.6 mm²
Total magnetic energy : | 600 MJ
Plasma current : | 1.7 MA
Potential duration of the discharge : | 1000 s
Cooling power at 80 K : | 40 kW
Cooling power at 4.5 K : | 650 W
Cooling power at 1.75 K : | 300 W
Data and picture from: http://www-fusion-magnetique.cea.fr

## Slide 5: Tore Supra
Test signal
axions
The magnetic field converts axions to microwave photons,
which excite the TE011 mode
Photons
A test signal might be necessary to proof that the detector is working and to determine resonant frequency over time
The inner walls might have to be covered by copper sheets, to achieve higher Q factors and better EMI shielding
The microwave signal is coupled out by a small antenna and amplified. A commercial spectrum analyzer can be used to detect the axion signal

## Slide 6: Preliminary simulation results
Inner radius: 0.8 meter, outer radius: 2.4 meter
TE011 = H011 mode, f= 145.601 MHz
 Most sensitive to axions with ma = 6 ∙ 10-7 eV
Wall material | Conductivity | Unloaded Q - factor
Stainless steel | 9.8e+5 S/m | 19271
Copper | 5.8e+7 S/m | 148250
E – field of the TE011 mode in the Tore Supra cavity

## Slide 7: The relic axion overlap integral
E – field of TE011 mode (ECAV)
Static magnetic field of
superconducting magnets (B0)
To see if the TE011 mode is sensitive to relic axions, we must evaluate its geometric form factor C
Essentially: E-field must be parallel to the static magnetic field to couple to axions (dot product!)
This is the case for Tore Supra
P. Sikivie, Phys. Rev. D32, 2988 (1985), [Erratum-ibid.D36:974,1987].
C ≈ 0.39 (from numerical calculation)

## Slide 8: Expected sensitivity
With the rather conservative parameters on the left (QL = 1000), we could reach
gayy = 7∙10-16 GeV-1
in a 9 h measurement run

## Slide 9: Alternative magnets for haloscopes
O. Baker et al., Prospects for Searching Axion-like Particle Dark Matter with Dipole, Toroidal and Wiggler Magnets, Phys. Rev. D 85, 035018 (2012)
Dipole magnets
Wiggler magnets
Toroidal magnets
Pictures from: CERN, DESY, CERN

## Slide 10: Alternative magnets for haloscopes
Up to now all haloscope searches have used solenoid magnets to provide the magnetic field
However, at accelerator and advanced light source facilities a range of magnets are available, that have not yet been exploited for their use in searches for ALP DM (axion like particle dark matter)
In particular we have the typical dipoles used for the accelerator itself as well as toroidal magnets used in particle detectors
In addition we have the wiggler magnets used for creating synchrotron and free electron laser light
Can we use these magnets efficiently in haloscope searches for ALP DM?

## Slide 11: Dipole magnets
Accelerator dipoles offer strong fields (LHC: 9.5 T) in a long region (14 m), with the magnetic field oriented perpendicular to the long direction
A long and thin rectangular microwave cavity could be introduced in the magnet
In this configuration, TE – modes couple to axions (The E-field is parallel to the static magn. field)

## Slide 12: Dipole magnets
The TE101 – mode couples strongest to axions (Geometry factor C = 0.66)
In our example configuration it would be resonant at fres ≈ 5 GHz  ma ≈ 2.1 ∙ 10-5 eV (assuming w = 30 mm, h = 20 mm, L = 8 m)
E-field of the TE105 mode
in a rectangular cavity
But:
If the aspect ratio L/w becomes this large, the modes in the cavity converge towards a common resonant frequency
Two modes with similar resonant frequency will couple to each other and exchange energy. This energy is lost!

## Slide 13: Dipole magnets
Higher order modes limit the maximum length of one cavity
  Lmax = 1.5 m for Q = 1000
  Lmax = 6.7 m for Q = 20000
To solve this problem, we can:
  Use wiggler magnets (next slide)
  Use an array of several cavities with L < Lmax
Power is coupled out from each cavity and fed to an external power combiner (hybrid)
Our results predict that only a few cavities are needed to fill a typical magnet, making this approach technically feasible

## Slide 14: Wiggler magnets
We get maximum coupling to axions, if the TE10n mode is used, where n is the number of magnetic oscillations in the wiggler magnet
An advantage of the wiggler conguration is that the mode spacing grows with n. The problem of overlapping modes is therefore somewhat reduced
Maximum length of one cavity in a wiggler magnet with 1 magnetic oscillation over 30 cm:
  Lmax = 4.7 m for Q = 1000
  Lmax = 14.1 m for Q = 3000

## Slide 15: Dipole magnets: tuning
To sweep over a range of values for the axion mass (ma) tuning of the cavity is necessary
This can be achieved by placing movable dielectric rods in the cavity
The geometry depicted below provides 13 % adjustment range over ma while keeping the geometric factor approx. constant

## Slide 16: Toroidal magnets: Inspired by Atlas

## Slide 17: RF cavities in toroidal magnets
Currently used in particle physics detectors such as ATLAS
In certain regions, these magnets provide transverse (to the long side) magnetic fields similar to dipole magnets
But the corresponding bore sizes are significantly larger!
The large volumes provide a significant advantage in sensitivity
Either with single big cavities for low axion mass ma or with an array of smaller cavities for larger axion masses
RF - cavities
or arrays of
RF - cavities