## Slide 1: Multiple-Cavity Detector for Axion Search
12th Patras Workshop
2016. 06. 20~24, Jeju, South Korea
SungWoo YOUN
Young Scientist Fellow
Center for Axion and Precision Physics Research (CAPP)
Institute for Basic Science (IBS)

## Slide 2: Introduction
Multiple-cavity detector
  Increases experimental sensitivity for axion searches in higher frequency regions
  Requires signal combination in phase: phase-matching
Multiple small cavities
Single large cavity
Single small cavity
Higher
frequency
Larger
Volume
: Magnet bore
: Cavity

## Slide 3: Configurations
 | 1 | 2 | 3
Schematic |  |  | 
Characteristic | N complete readout chains | N amplifiers 1 combiner | 1 amplifier 1 combiner

## Slide 4: Configurations
 | 1 | 2 | 3
Schematic |  |  | 
Characteristic | N complete readout chains | N amplifiers 1 combiner | 1 amplifier 1 combiner
Sensitivity* (SNR) |  |  | 
SNRsngl = SNR of single cavity
NC
S
G, NA
* Correlated signal and uncorrelated noise ** N.F. comb = 0

## Slide 5: Configurations
 | 1 | 2 | 3
Schematic |  |  | 
Characteristic | N complete readout chains | N amplifiers 1 combiner | 1 amplifier 1 combiner
Sensitivity (SNR) |  |  | 
Pros. | Individual access | Higher sensitivity | Simpler design
Cons. | Lowest sensitivity N complete readout chains | N amplifiers | SNR3 < SNR2*
* In reality, N.F.comb ≠ 0
ex) G=12, N.F.amp=6, N.F.comb=0.5 => SNR3 is lower than SNR2 by 10%

## Slide 6: Configurations
 | 1 | 2 | 3
Schematic |  |  | 
Characteristic | N complete readout chains | N amplifiers 1 combiner | 1 amplifier 1 combiner
Sensitivity (SNR) |  |  | 
Pros. | Individual access | Higher sensitivity | Simpler design
Cons. | Lowest sensitivity N complete readout chains | N amplifiers | SNR3 < SNR2

## Slide 7: Multiple-Cavity Detector
Introduced in 1990 and exploited by ADMX
  KSVZ with 3.3639 < ma [μeV] < 3.3642 excluded with 90% C.L.
Phase-matching mechanism is challenging
  Failure reduces signal power and degrades SNR
    Broadens the bandwidth of power spectrum
    Decreases the cavity quality factor
5 year IBS Young Scientist program is devoted to develop the system at CAPP

## Slide 8: Phase Matching
Coherence of axion field and static magnetic field
  Axion signals are generated in phase
Resonance frequencies of individual cavities
  Cavities must be tuned at the same frequency
  Essential part (most challenging part) of the matching mechanism
Constructive signal combination
  Phase matching at power combiner in the time domain
  Identical cables with the same length
a

## Slide 9: Phase Matching
Phase matching ~ Frequency matching !
Resonance frequencies of individual cavities
  Cavities must be tuned at the same frequency
  Essential part (most challenging part) of the matching mechanism

## Slide 10: Design of a Multiple-Cavity System
Array of N identical cavities
  Same dimension and same tuning mechanism
N-way power combiner
  Before the first stage of amplification
Remaining RF components are identical with a single-cavity experiment
A quadruple-cavity detector
  For a magnet bore (D) of 10 cm
  Maximum cavity radius (R) of 1.7 cm
    Cavity wall thickness of 4 mm
    46% volume usage
  TM010 frequency: 6.75 GHz
D
R
Combiner
Amplifier
Magnet
S.A.
Cryostat

## Slide 11: Simulation Study (COMSOL)
Chart: Form factor
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
 | 0.40261 | 0.40396 | 0.40822 | 0.41614 | 0.42921 | 0.44997 | 0.48253 | 0.53197 | 0.59776 | 0.65856 | 0.68668
Chart: Quality factor
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
 | 23389 | 23259 | 22868 | 22216 | 21307 | 20160 | 18833 | 17490 | 16509 | 16436 | 17307
Chart: Resonant frequency
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
 | 5624000000 | 5635800000 | 5671400000 | 5732200000 | 5820400000 | 5938600000 | 6088800000 | 6268400000 | 6460400000 | 6623900000 | 6717200000
Δf ~1 GHz
δf/δθ ~ 5 MHz/deg
ΔQ ~ 30%
δQ/δθ ~ 0.15%/deg
Cu cavity
(R=1.7cm,L=10cm*)
Tuning system
(Dielectric rotational rod) (ε=10, r/R=0.1*)
* See poster by Junu Jeong

## Slide 12: Conversion Power and Scan Rate
A quadruple-cavity system
  4 cavities with R = 1.7 cm and L = 10.0 cm => V = 0.36 L
Conversion power
Scan rate

## Slide 13: Phase (Frequency) Matching
Source of frequency mismatch
  Machining tolerance in cavity fabrication
    50 μm => 25 MHz
Ideal frequency matching is not possible!
  Position resolution ≠ 0°: 0.1 m° => 0.5 kHz
Realistic approach: Frequency mismatch!
  Up to a certain level where a reduction in the (combined) power is not significant
  Frequency Matching Tolerance, FMT
f0
f
FMT
f0: leading frequency

## Slide 14: Phase (Frequency) Matching
Source of frequency mismatch
  Machining tolerance in cavity fabrication
    50 μm => 25 MHz
Ideal frequency matching is not possible!
  Position resolution ≠ 0°: 0.1 m° => 0.5 kHz
Realistic approach: Frequency mismatch!
  Up to a certain level where the (combined) power reduction is not significant
  Frequency Matching Tolerance, FMT
  Pcomb > 0.95 Pideal
f0
f
FMT
f0: leading frequency
Ideal
Combined

## Slide 15: Frequency Matching Tolerance – I
Pseudo-experiment study
  4-cavity detector, Qu = 105, f0 = 6 GHz
  Tolerances Under Test (TUT) = (0,) 10, 20 ,30, 60, 100, 200 kHz
  Combined power spectra
  1000 pseudo-experiments
TUT = 0 kHz
10 kHz
20 kHz
30 kHz
60 kHz
100 kHz
200 kHz
TUT = 0 kHz
TUT = 60 kHz
Power amplitude from each cavity is normalized to 1.
Averaged power spectra
Combined Power Spectra (60 kHz)

## Slide 16: Frequency Matching Tolerance – II
For 6.0 GHz axion signal, 4-cavity detector with Qu=105
  20 kHz is the FMT for the system
In general, FMT = 2 GHz / Qu
  For Qu=106, FMT = 2 kHz
  cf. position resolution of 0.1 m° => frequency resolution: 0.5 kHz
TUT (kHz) | Power Amp. | Qu | SNR | Scan Rate
0 | 1.00 | 1.00 | 1.00 | 1.00
10 | 0.99 | 0.99 | 0.99 | 0.96
20 | 0.96 | 0.95 | 0.94 | 0.85
30 | 0.93 | 0.91 | 0.88 | 0.71
60 | 0.78 | 0.73 | 0.67 | 0.31
100 | 0.60 | 0.55 | 0.45 | 0.11
Averaged power amplitude and width

## Slide 17: Tuning Mechanism – I
Basic principle – critical coupling
  Minimizing the reflection coefficient (Γ)
  Forming a circle passing through the center of the smith chart
For a single cavity
  Γ is minimized when
    System is critically coupled
For a multiple-cavity system
  Combined Γ is minimized when
    Frequency matching is successful
    Entire system is critically coupled

## Slide 18: Tuning Mechanism – II
Frequency matching & critical coupling
Consisting of three steps
  1) simultaneous operation of the tuning systems
    To shift search frequency
  2) finer operation of the individual tuning systems
    To achieve frequency matching
  3) global operation of the antennas
    To achieve critical coupling
    At the sacrifice of sensitivity loss of <0.5%*
…
Linear piezo
Rotational piezos
1)
3)
2)
* Machining tolerance of 50 μm and uncertainty on surface conductivity of 2%

## Slide 19: Experimental Demonstration
Double-cavity
  O.D.= 5.08 cm
  I.D. = 3.88 cm
  fTM010 = 5.92 GHz
  QL = 9,000 at RT
Tuning system
  Dielectric rods (95% alumina)
    fTM010 = 4.54 GHz at center
    QL = 2,500 at RT
  Two rotators
    Frequency tuning
  One linear positioner
    Global operation of two couplers
Couplers
Linear Positioner
Coupler
holder
Rotators

## Slide 20: Sequence of Demonstration
Assembly of a double-cavity system with a combiner
  Calibrate the system up to the two couplers
Critical coupling at slightly different resonant frequencies
  Measure the initial Q (and S11) values
Assembly of the full system
  See two reflection peaks and two circles
Operation a rotator
  For frequency matching
  Until the combined reflection coefficient is minimized
Operate the linear positioner
  For critical coupling
  Reflection peak becomes further deeper / Smith circle passes through the center
Compare the Q (S11) value with the initial ones

## Slide 21: Critical Coupling (Cavity I)
f010: 4.5353 GHz
S11: −46.4
Q : 2,530
Term.

## Slide 22: Critical Coupling (Cavity II)
f010: 4.5607 GHz
S11: −43.2
Q : 2,440
Term.

## Slide 23: Combining Two Cavities
Marker 1: 981 mU
Marker 2: 508 mU
S11 = −6 dB
I
II

## Slide 24: Frequency Matching – Rotator
f010: 4.5607 GHz
S11: −30.7
Q : 2,690

## Slide 25: Critical Coupling – Linear
f010: 4.5606 GHz
S11: −44.4
Q : 2,610

## Slide 26: Phase Matching – Movie

## Slide 27: Project Plan
Multiple stages
  Depending on cavity multiplicity (#) and cavity quality factor
  1st stage: double-cavity with Qu=104
  2nd stage: quadruple-cavity with Qu=104
  3rd stage: quadruple-cavity with Qu=106
  Final stage: septuplet-cavity with Qu=106
    R=1.3 cm, f(TM010)=~8 GHz (with a dielectric tuning rod)
# | Qu | 2015 |  | 2016 |  |  |  | 2017 |  |  |  |  |  | 2018 |  |  |  |  | 2019 |  |  | 
2 | 104 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | 104 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | 106 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 | 106 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design & Procurement
Construction & Test at RT
Commissioning at CR
Operation & Analysis

## Slide 28: Summary
Multiple-cavity detector
  Increases the sensitivity for axion search in higher frequency region
Basic design: signal combination preceding amplification
  Simpler setup with minimal sensitivity degradation
Realistic approach for phase (frequency) matching
  Frequency mismatch within FMT (Pcomb > 0.95 Pideal)
  FMT = 2 GHz / Qu for 6 GHz axion
Tuning mechanism
  To achieve frequency matching and critical coupling
Experimental demonstration
…
Linear piezo
Rotary piezos
1)
3)
2)

## Slide 29
Backups

## Slide 30: SNR – Configuration 1
Multiple chains
S : signal voltage
NC: cavity noise voltage
G : amplifier gain
NA : amplifier noise voltage

## Slide 31: SNR – Configuration 2
Amplification + combination
S : signal voltage
NC: cavity noise voltage
G : amplifier gain
NA : amplifier noise voltage
Noise from the combiner is assumed to be negligible.
Signal is correlated while noise is uncorrelated.
Voltage adds in sqrt.

## Slide 32: SNR – Configuration 3
Combination + amplification
S : signal voltage
NC: cavity noise voltage
G : amplifier gain
NA : amplifier noise voltage
Noise from the combiner is assumed to be negligible.
Signal is correlated while noise is uncorrelated.
Voltage adds in sqrt.

## Slide 33: Phase-locking (Time)
Source of phase mismatch at the combiner
  Different cable lengths between individual cavities and the combiner
NOTE: Ideal phase matching is difficult!
  Exactly same length of cables
  More realistic to keep the phases within a certain range
    Phase Matching Tolerance, PMT
    Acceptable as long as the reduction in combined power (or SNR) is not significant

## Slide 34: Phase-locking (Time)
Determining the PMT
  Consider a tolerance (tolerance under test, TUT)
  Assume that individual signals have phases (φi) within the tolerance, i.e. |φi − φ0 |< TUT when arriving at the combiner
  If the combined power is >95% of the ideal case, i.e. φi = φ0 or TUT=0, then take the TUT as the PMT
Pseudo-experiment study
  4-cavity detector, f0=6 GHz, Qu=105
  TUT = (0,) π/16, π/8, π/4, π/2, π/√2, π
  1000 pseudo-experiments
φ0
φ
TUT
φ0: leading frequency
Ideal
Combined

## Slide 35: Pseudo-experiment Study
Junu Jeong
Power amplitude from each cavity is normalized to 1.
TUT = 0 rad
π/16 rad
π/8 rad
π/4 rad
π/2 rad
π/√2 rad
π rad
TUT = 0 rad
TUT = π/8 rad
TUT = 0 rad
TUT = π/4 rad
Averaged power spectra
Combined Power Spectra (10 kHz)
Combined Power Spectra (60 kHz)

## Slide 36: Pseudo-experiment Study – Summary
For 6.0 GHz axion signal, 4-cavity detector with Qu=105
  π/8 rad is the PMT for this system
  This corresponds to Δl = ~3 mm (λ = 5 cm)
In general, Δl = 1/16*c/f
  For 10 GHz, Δl = ~2 mm
  Can be under good control
TUT (rad) | Power Amp. | Qu | SNR | Sensi-tivity
0 | 1.00 | 1.00 | 1.00 | 1.00
π/16 | 0.99 | 1.00 | 0.99 | 0.98
π/8 | 0.96 | 1.00 | 0.96 | 0.93
π/4 | 0.86 | 1.00 | 0.86 | 0.75
π/2 | 0.54 | 1.00 | 0.54 | 0.29
π | 0.25 | 1.00 | 0.25 | 0.06

## Slide 37: Isolating Termination Dissipation
Isolating terminations enable the dissipation of power due to various unbalances and possible input failures
Schematic representation of four 250 W amplifiers feeding a 4-way combiner
Power output and power dissipation associated with various input failure scenarios
At reson.
Non-reson.
1
1/2
1/2
1/2
1/4
0