## Slide 1: Configuration of the online calibration pipelines - throughput limiting factors
S. Hauf
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)

## Slide 2: Before monitoring starts - Interfacing to the calibration database
(optional) update calibration database with new data from dark images (offset, noise, subset of bad pixel parameters)  will be configured and available as an automated procedure, processing time of < 5 minutes expected.
(mandatory) load the calibration and correction constants pertinent to the current detector operating conditions  needs to be done only if settings are changed, and even then relatively quick: tens of seconds.

## Slide 3: Before correction starts – retrieving the right constant
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 1: T = 20°C ± 1 °C, V = 200V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 2: T = 25°C ± 1 °C, V = 200V ± 5V, E = 18keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set n: T = 21°C ± 1 °C, V = 195V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Cal. Measurement 1
Cal. Measurement 2
Cal. Measurement n
Updates CS1

## Slide 4: Calibration Database – Versioning and Detector-Condition-based Injection & Querying
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 1: T = 20°C ± 1 °C, V = 200V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 2: T = 25°C ± 1 °C, V = 200V ± 5V, E = 18keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set n: T = 21°C ± 1 °C, V = 195V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Observation with Det. X at Condition Y
required constants
Conditions

## Slide 5: Calibration Database – Versioning and Detector-Condition-based Injection & Querying
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 1: T = 20°C ± 1 °C, V = 200V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 2: T = 25°C ± 1 °C, V = 200V ± 5V, E = 18keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set n: T = 21°C ± 1 °C, V = 195V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Observation with Det. X at Condition Y
required constants
Conditions
Matching data
Matching data
Matching data

## Slide 6: Calibration Database – Versioning and Detector-Condition-based Injection & Querying
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 1: T = 20°C ± 1 °C, V = 200V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 2: T = 25°C ± 1 °C, V = 200V ± 5V, E = 18keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set n: T = 21°C ± 1 °C, V = 195V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Observation with Det. X at Condition Y
required constants
Conditions
Constants
Matching data
Matching data
Matching data

## Slide 7: Calibration Database – Versioning and Detector-Condition-based Injection & Querying
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 1: T = 20°C ± 1 °C, V = 200V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 2: T = 25°C ± 1 °C, V = 200V ± 5V, E = 18keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set n: T = 21°C ± 1 °C, V = 195V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Observation with Det. X at Condition Y
required constants
Conditions
Constants
Matching data
Conditions
Constants
Matching data
Matching data
Matching data

## Slide 8: Calibration Database – Version Management
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 1: T = 20°C ± 1 °C, V = 200V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set 2: T = 25°C ± 1 °C, V = 200V ± 5V, E = 18keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Quantum efficiency
Gain map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Offset map
Noise map
Gain map
Offset map
Noise map
Week 10
Week 11
Condition Set n: T = 21°C ± 1 °C, V = 195V ± 5V, E = 12keV ± 0.1keV,
p = log(10-3bar) ± 1log(bar) …
Observation with Det. X at Condition Y
required constants
Conditions
Constants
Matching data
Conditions
Constants
Matching data
Matching data
Matching data

## Slide 9: Online Calibration
Calibration of the data in the online monitoring stream often makes sense.
Possible limiting factors:
  I/O rate
  Processing rate
  Latency
Karabo-online views of scattering in a ferrous solution imaged by LPD

## Slide 10: I/O Limitations
Should especially for monitoring data (~1Hz update interval) not be an issue:
  1Mpixel * 512 Memory Cells * 4B(float) = 16Gbit/s
  Network connection: Infiniband@56Gbit/s
   Limitation rather on processing side?

## Slide 11: Possible components of correction pipelines
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.

## Slide 12: Possible components of correction pipelines
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.

## Slide 13: Possible components of correction pipelines
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.

## Slide 14: Possible components of correction pipelines
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.

## Slide 15: Possible components of correction pipelines
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.

## Slide 16: Possible components of correction pipelines
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.

## Slide 17: Possible components of correction pipelines
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.
40%
40%
7%
7%
7%
Experience shows that the two most expensive corrections are:
  Common mode: needs to calculate a per-row median, involves sorting  sorting network fastest implementation
  Split-events: need to scan a 25 pixel box for each pixel

## Slide 18: Possible components of correction pipelines – and importance on throughput
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.
40%
40%
7%
7%
7%

## Slide 19: Possible components of correction pipelines – and importance of throughput
pixel
row/column
image
granularity
Offset
sub.
CM
correct.
CTI correct.
Split
events
Gain correct.
Droop
correct.
40%
40%
7%
7%
7%
This is sufficient for 10Hz operation using all correction steps

## Slide 20: What about alignment?
For online displays, approximate accuracy should often be sufficient, e.g. accurate to the pixel size of the display.
  Use rendering routines of Karabo-GUI (underlying GuiQwt) to apply geometry information
  Negligible penalty if no geometry does not change often (updates in position)

## Slide 21: Conclusion
Quite confident the online calibration will not limit throughput but:
  How critical is latency? Longer correction pipelines will add roughly 100-500ms of per component
  Pipelines are configured to “drop on slowness” to allow PC-layer to prioritize persisting of data.
    The slowest pipeline step will limit the throughput

## Slide 22: Conclusion
    The slowest pipeline step will limit the throughput
  Do not do heavy processing in the GUI (widgets) as this will be limited to ~1Hz of update rate.
  If latency is not an issue consider elongating the pipeline, i.e. split processing into concurrent tasks an let the pipeline act as “cache”
  Keep in mind that we do not foresee persisting in the midst of the monitoring stream, once data is dropped due to slowness it will only be available offline.