## Slide 1: An Introduction into foreseen dataflows at the European XFEL (and common vocabulary)
S. Hauf
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)

## Slide 2: The Big Picture

## Slide 3: The Big Picture
Data products from the fast 2D detectors: raw and calibrated data

## Slide 4: The Big Picture
The hierarchical data format

## Slide 5: The Big Picture
The PC-Layer: where data hits the disks

## Slide 6: The Big Picture
The HDF5 format to be used at European XFEL

## Slide 7: The Big Picture
Retrieving and querying data as a user

## Slide 8: The Big Picture
Concurrent processing in Karabo

## Slide 9: The Big Picture
The XFEL calibration pipeline

## Slide 10: The Big Picture
At the end of the workshop we will have visited most components in this diagram
Notes: ----- Meeting Notes (02.02.16 16:57) -----
Add pictures of devices

## Slide 11: Common Vocabulary – Data products
Definitions as published in Kuster, Markus, et al. "Detectors and Calibration Concept for the European XFEL." Synchrotron radiation news 27.4 (2014): 35-38.
Raw data represents digitized detector signal, not altered by detector-specific corrections or calibrations; e.g., it is in the form of detector units such as analogue digital units (ADU). Vetoing, either by hard- or software triggers and zero-value suppression (e.g., by transferal to event lists), may have been performed and is irreversible. Raw data is the main archival data product at the European XFEL. It is not foreseen to be ex- ported outside the facility, and is not meant to be directly user-accessible.

## Slide 12: Common Vocabulary – Data products
Definitions as published in Kuster, Markus, et al. "Detectors and Calibration Concept for the European XFEL." Synchrotron radiation news 27.4 (2014): 35-38.
Calibrated data is generated from raw data by applying detector- specific corrections and transformation to physical units (calibration)— e.g., photons per pixel. Calibrated data is the standard data product with which users will be provided. It is not archived; instead, if a calibrated dataset is not accessible through the online-cache or user-space anymore it is requested, it will be reprocessed on the fly from the raw data repository using the appropriate calibration parameters provided by the calibration database.

## Slide 13: Common Vocabulary – Data products
Definitions as published in Kuster, Markus, et al. "Detectors and Calibration Concept for the European XFEL." Synchrotron radiation news 27.4 (2014): 35-38.
Calibrated data – distinctions
Calibration and correction constants are used to correct and calibrate raw data. Correction involves “removing” detector specific components to the signal. Calibration is the process of converting detector units to physical units, e.g. photons.
Calibration data production it the process of producing calibration and correction constants
Correction and calibration application is the process of correcting and calibrating raw data into calibrated data
Notes: ----- Meeting Notes (02.02.16 16:57) -----
constants -> parameters

## Slide 14: Common Vocabulary – Data products
Definitions as published in Kuster, Markus, et al. "Detectors and Calibration Concept for the European XFEL." Synchrotron radiation news 27.4 (2014): 35-38.
Alignment data is generated from dedicated alignment measurements, providing the position of each detector pixel and detector module in three-dimensional space. It is stored in the detector coordinate system (i.e., as pixel coordinates) and no additional interpolation or coordinate transformation will be applied. Alignment data is part of the standard data products with which users will be provided.

## Slide 15: Common Vocabulary – Data products
The previous definitions are mainly meant for (non-commercial) 2D-detector data (and strip detectors such as Gotthard).
Commercial cameras might already provide calibrated data as output
For digitizers etc. the notion of calibration will be much more application-specific, i.e. depending on use-case “raw” data might be provided.

## Slide 16: Common Vocabulary – Karabo Hash
In essence the Karabo-Hash is a associative data structure, which maps values to keys. Keys can be organized as hierarchical paths. Values have types preserved.
    C++ - equivalent: std::map<string, T>
    Python –equivalent : dict()
    Markup: XML  best conceptual match
Actually, more like boost::any
In more detail in the concurrency session

## Slide 17: Calibration and Correction Parameters of XFEL Detectors

## Slide 18: Why we plan on supplying calibrated data only
Arbitrary units
~109 correction and calibration constants, evaluated for the correct detector operating conditions.
~ Gigabytes of calibration constants needed
Raw
Corrected
Data courtesy of AGIPD consortium
AGIPD image of a pen-drive, corrected with PyDetLib
(offset, common-mode, relative gain, bad-pixel masking)

## Slide 19: Why we plan on supplying calibrated data only
~109 correction and calibration constants, evaluated for the correct detector operating conditions.
~ Gigabytes of calibration constants needed
Raw
Corrected
Example LPD: In terms of e.g. offset correction the LPD is 1.5 Gpixel detector: 1 Mpx x 512 memory cells x 3 Gains  “Offset map” will have approx. 3 GB in size

## Slide 20: Benchmarking calibration routines: pnCCD
Parameter | CAST | XFEL | Diff. (%)
Min (median) | 296.0 | 296.0 | 0
Max (median) | 1372.0 | 1372.0 | 0
Noise (median) | 5.3 | 5.2 | 1.8%
Peak pos (ADU) | 986.3 | 979.1 | 0.7%
Peak FWHM (eV) | 198.6 | 207.0 | 4.1%
ADU/eV | 0.17 | 0.17 | 0%
CAST pn-CCD
200x64 pixels
150 μm x 150 μm pixel size
300 μm sensor thickness
71.775 ms cycle time
Slightly better optimized event threshold
Different (not as good)
Implementation
– remedied
Comparison of existing, proven and validated CAST pipeline to XFEL implementation

## Slide 21: XFEL pipeline now exceeds performance of CAST pipeline
FWHM
173.1 ± 0.7 eV vs. 189.0 ± ?.? eV
at same efficiency

## Slide 22: Why we plan on supplying calibrated data only
Raw
Corrected
Facility-side calibration means:
Users neither have to provide large amounts of computing resources nor have to have in-depth expertise on detector physics to obtain state-of-the-art corrected and calibrated datasets for their experiments and can thus focus on their scientific analysis. Additionally, data aggregation of different experiments and instruments are simplified as calibration becomes user-independent.
~109 correction and calibration constants, evaluated for the correct detector operating conditions.
~ Gigabytes of calibration constants needed

## Slide 23: The Big Picture

## Slide 24: Why we plan on supplying calibrated data only – benefits for online monitoring
Pipelined correction routines can be used in offline and online processing
Full or partial correction of (subset of) data before passing it on to dedicated monitoring/quick analysis routines
Karabo-online views of scattering in a ferrous solution imaged by LPD

## Slide 25: The Big Picture

## Slide 26: Detector Alignment Data
Hierarchical concept for local detector alignment (not global instrument alignment)
Discussions with instruments yielded understanding that alignment of components, which may be moved on a per-run basis (i.e. quadrants), require input and support from instrument side (e.g. using powder samples)
XFEL photon system coordinate system (WP-73) is used
Alignment data will be shipped with calibrated data
WP-75 will provide transformation from pixel to Cartesian coordinates
Technical note exists with requirements from each instrument: https://bib-pubdb1.desy.de/record/222635
Absolute lab reference
Detector normal x,y,z
Detector reference origin
Panel reference origin
Module x,y,z
w.r.t. panel reference
WP 75
Instruments + WP 75

## Slide 27: Detector Alignment Data
For centralized processing (e.g. calibration) this means
  Data stays in pixel coordinates as long as possible  no interpolation, thus more accurate
  Alignment data is stored (and versioned) in a calibration database
  Alignment data is provided along with measurements, users use it as needed of request conversion of pixel data to aligned data set  point for discussing, see next slides
  Alignment data can be applied (to lesser accuracy) also in the online previews
LPD data with alignment information applied in online view

## Slide 28: Open questions
Calibrated data sets easily allow for zero-suppression by thresholding  lower data volumes.
  Should this be enabled by default?
  How configurable (for users) should it be?

## Slide 29: Open questions
If zero-suppression is used, sparse data can be converted to event lists, e.g. (x, y, z, pulse, intensity). X, Y, Z can be expressed in pixel or Cartesian coordinates
  Is there are need for a centralized service for this?
  Who decides how sparse data must be for this to make sense
  What happens if data is suddenly not “sparse” anymore

## Slide 30: Open questions
After alignment data application, how should data be output?
  Supersampled?
  Event-list type?
  Others?