## Slide 1: Data Processing Requirements of the SQS Instrument
XFEL Data Processing Workshop 2016
Thomas M. Baumann
03.02.2016

## Slide 2: The Small Quantum Systems (SQS) Instrument at European XFEL
Scientific Scope:
Soft X-ray beamline SASE3: 260 eV to 3000 eV photon energy,
Study of Atoms, small Molecules, Clusters and Biomolecules,
Nonlinear multi-photon processes,
Molecular dissociation dynamics,
Coincidences (Electron-Ion, Electron-Electron),
Imaging of Molecules and Nano particles.

## Slide 3: Overview of the Detectors at SQS
Six Electron Time-Of-Flight
Spectrometers (eTOF)
MCP detector
4.5 MHz readout
Coincidence with eTOF or VMI
Velocity Map Imaging Spectrometer (VMI)
MCP with Phosphor screen (10 Hz)
Alternative: Delay-line anode (4.5 MHz)
Coincidence with eTOF
Scattering Detectors
DSSC detector
FastCCD detector
Imaging MCP
Magnetic bottle spectrometer
MCP detector
XUV photon spectrometer
MCP with double delay line
Reaction Microscope (REMI) / COLTRIMS
2 MCP detectors with delay-line anodes
4.5 MHz readout
Electron – Ion Coincidences
Scienta detector
Imaging MCP detector

## Slide 4: Velocity Map Imaging Spectrometer (VMI)
MCP + Phosphor screen,
Photonic Science sCMOS camera:
  2048 x 2048 Pixel, 16 bit, 30 fps -> 10 Hz operation
May later be replaced by MCP + delay-line -> 4.5 MHz.
Target is ionized in interaction zone,
VMI optics project 3d velocity map on 2d detector plane,
Reconstruction of velocity map from images needed,
One common method: Inverse Abel-Transform:
hν = 280 eV, Ekin = 30, 32 eV
hv = 260 eV, Ekin = 10, 12 eV
hv = 270 eV, Ekin = 20, 22 eV
Target
FEL
Electrons
Parabolic electrode stack
MCP + Phosphor screen
Detector image
P04 (PetraIII): Ar 2p photoelectrons
B. Dick, Phys. Chem. Chem. Phys. 2014, 16, 570

## Slide 5: VMI Data Processing: Online analysis
Current development status
Karabo program for camera control and readout is available,
Online data processing devices are under development (thanks to Andrea Parenti!):
  Background subtraction
  Summing / averaging
  Region of interest definition
  Processing: e.g. sum, ratio,…
Implemented pipeline:
Next performance test during run at P04 in March.
Abel-Transform algorithm:
  Collaboration with Gregor Hartmann (DESY)
  Inversion of pre-processed data (sum of several runs)
  Parallel processing on GPU or multiple CPUs
  Python code (using pyopencl, pycuda, mpi4py)
camera
bkg.sub
master
slave
average
mask1
mask2
img.proc.1
img.proc.2
Single image Ar Auger @ P04

## Slide 6: Electron Time-of-Flight spectrometer (eTOF)
MCP detector
Mesh
Port aligner
Electrodes
Drift region
6 eTOF spectrometers
High resolution kinetic energy measurement on electrons produced in Target – FEL interaction.
MCP detectors.
Data acquisition on 4.5 MHz timescale,
Digitizer: SP device, 10 GS/s,
TOF resolution limited by digitizer resolution.
< 1 ns
Trigger
TOF < 220 ns
Online data processing (in electron counting mode):
Peak search / discrimination,
Calculation of time between trigger and signal,
Counting of pulses vs TOF (histogram),
Disregard of traces w/o signal (optional),
Coincidence plots,
Define and project regions of interest,
Display of histograms,
Storage of traces and histograms.
Current development status:
Karabo program for recording, displaying and storing digitizer traces is available.
Online data processing (in current mode):
Summing of traces.

## Slide 7: MCP Detector with Delay Line Anode
REMI and NQS:
Detection of electrons and ions after interaction with the FEL,
Full reconstruction of interaction dynamics from particle positions on the detector,
Two MCP detectors with delay line anodes,
Coincidence measurements,
Collaboration with Uni Frankfurt (R. Dörner) and RoentDek.
MCP stack with delay line anode:
Delay line anode in two or three directions (Hexanode),
Multi-hit capability,
Digitizer: SP Device, 2 GS/s,
Data acquisition on 4.5 MHz timescale.
RoentDek Detector
MPIK

## Slide 8: Delay Line Detector Data Processing
< 10 ns
Trigger (MCP)
Delay line several 10 ns
RoentDek Hexanode
Tv1
Tv2
Tw1
Tw2
Tu1
Tu2
Hexanode coordinates:
Cartesian coordinates:
Sorting algorithm:
Search for „good“ signal combinations.
Tolerance window e.g
Position uv similar to uw.
Position must be within MCP active area.
Position calculation performed by RoentDek software

## Slide 9: Summary
VMI requirements
  Karabo programs under development
  Next test run in March/April at P04
Digitizer requirements
  Karabo program for digitizer readout is available
  Implementation needed:
    pulse discrimination
    Trigger to Pulse time delay determination
    1D and 2D histogram creation
  Coincidence of several channels
  Possible test of eTOF spectrometer in March/April at P04