## Slide 1: ABCn’ introduction + work to be done 3 February 2016
J. J. John, Oxford

## Slide 2
Strip CMOS programme
3 years to develop a new strip sensor based on CMOS technology
Designing sensors with 2 foundries: Austrian Micro Systems (AMS) and TowerJazz (TJ)
Year 1 (done) – manufacture and characterise basic sensor elements
(CHESS-1)
Year 2 (now) – demonstrate large size sensor (CHESS-2) and ABCn’ readout solution
see Richard’s schedule slides later
Year 3 – demonstrate full-sized multi-sensor object
For more details, see introductory talk at first year review of Strip CMOS programme

## Slide 3
Readout overview
Programme | Sensor | Front end chip (sensor level) | Hybrid-level chip | Stave-level chip
Baseline, current | Planar strips Analogue outputs | ABC130 (ATLAS Binary Chip, 130nm) | HCC (Hybrid Controller Chip) | GBT on End of Stave Controller
Baseline, near future | Planar strips Analogue outputs | ABC130* Change to star architecture (+ more changes) | HCC* Change to star architecture (+ more changes) | GBT on End of Stave Controller
Strip CMOS | CHESS CMOS pixels arranged into strips Digital outputs | ABCn’ Digital readout chip based on ABC130* | HCC* No changes at this level, must be drop-in | GBT on End of Stave Controller No changes at this level

## Slide 4
Status of chips and specs
ABC130*: design in progress
current spec: version 0.9a
also see review of 15 Oct 2015
AMS-CHESS-2: design well advanced
see AMS-CHESS-2 design review
also see CMOS fortnightly updates
TJ-CHESS-2: design in progress
see TJ-CHESS-2 design review
also see CMOS fortnightly updates

## Slide 5
Detector pads: 256 input pads
Front End
x256
Evt_Buffer
CF
ReadOut
Block
Serial interface
L0_Buffer
Command Decoder
COM/L0/PR/LP
Top_Logic
Mask &Edge Det.
L0sync/BCsync
ABC* overview
-- F. Anghinolfi et. al, Specification for ABCstar ASIC, v09.a
analogue part
digital part

## Slide 6
ABC* digital part
-- General talk at ABC* specification review, 15 Oct 2015
Readout
Cluster
Finder
EvtBuffer
L0Buffer
(Pipeline)
Edge Det./
InpReg
CMD Decoder
Top Logic
DataOut
L0/CMD
PR/LR/L0sync/BCR
RCLK
BC
PadTERM
PadID<4:0>
RSTB
abcup

## Slide 7
Probable changes for ABCn’
-- General talk at ABC* specification review, 15 Oct 2015
Readout
Cluster
Finder
EvtBuffer
L0Buffer
(Pipeline)
Deserialiser
CMD Decoder
Top Logic
DataOut
L0/CMD
PR/LR/L0sync/BCR
RCLK
BC
PadTERM
PadID<4:0>
RSTB
abcup
SACI bridge
SPI bridge