## Slide 1: Two Dimensional SR-Interferometer at PETRA III
Artem Novokshonov
DESY, Tomsk Polytechnic University
DEELS 2016 Workshop DESY

## Slide 2: SR-Interferometer at PETRA
Mirror
Source point
SR
Slits
Lens
500 nm Bandpass Filter
Magnificating Lens
Polarizer
CCD Camera
14.2 m
Mirror
≈ 0.88 m
Schematic of the Interferometer

## Slide 3: SR-Interferometer at PETRA
Gero Kube, DESY / MDI
synchrotron light from
bending magnet NL 50
mirror boxes
visible light beampipe
Optical beamline (bunch length diagnostics)
30 m beam transport via relay optical system
Setup in optical hutch
Ü
alignment mirror
lens
double slit
magnification lens
Glan-Thomson polariser
bandpass filter & CCD
DEELS 2014 Workshop @ ESRF, 12.05.2014
vertical design emittance confirmed

## Slide 4: SR-Interferometer at PETRA
USR studies
confirmation of 3 GeV hor. emittance
Drawbacks
beamline with relay optics
→ additional uncertainties (lenses)
setup blocks Streak camera system
→ dismount interferometer for bunch
length measurement
space for only one interferometer
→ modify setup for measurement in
other transverse plane
beamline originally not designed for interferometric measurements
status 22.06.2016
status 06.05.2014

## Slide 5: SR-Interferometer at PETRA
Horizontal interferogram
Two dimensional interferogram
Vertical interferogram
First interferograms from the new one interferometer

## Slide 6: Virtual Lab Modelling
Virtual Lab Fusion (VL) – is an optical design software made by Light Trans company. Using VL one can simulate his own optical system with optical elements from the simplest (ideal lens, ideal mirrors, slits etc) up to structures made himself.
Advantages of VL for SR – interferometer modelling:
User can define any slits constructions
Parameter run can be performed
Disadvantages:
VL is not performed for synchrotron field calculations
Points to observe using VL:
Different kinds of slits (pinhole and rectangular)
Beam size determination mistake caused by shifting or rotating of slits

## Slide 7: Virtual Lab Modelling
At a first stage, VL results of interferometer modelling had to be compared with results of already existing code. For this case a Synchrotron Radiation Workshop (SRW) software was chosen.
Vertical comparison of VL results with results of SRW
Stages of the comparison:
Synchrotron radiation field was calculated by SRW
This field was propagated via double slit optical system in VL and SRW
Beam sizes were determined from both programs
 | VL results | SRW results | Real size
 | 170 μm | 169 μm | 169 μm
 | 10 μm | 9.4 μm | 9.75 μm
 | VL results | SRW results | Real size
 | 170 μm | 169 μm | 169 μm
 | 10 μm | 9.4 μm | 9.75 μm

## Slide 8: Virtual Lab Modelling
Two dimensional VL interferogram (rectangular slits)
Parameters of the slits:
Horizontal distance between slits – 6 mm
Vertical distance between slits – 11 mm
Half of horizontal slits width – 0.5 mm
Half of vertical slits width – 0.5 mm

## Slide 9: Virtual Lab Modelling
Two dimensional VL interferogram (pinholes)
Parameters of the slits:
Horizontal distance between pinholes– 5 mm
Vertical distance between pinholes– 11 mm
Radius of the pinhole – 1 mm

## Slide 10: Virtual Lab Modelling
Slits rotating. Horizontal size determination
α
Let us consider that our slits are rotated at some angle to the “not tilted” position. In this case there must be some mistake of beam size determination.
Non rotated interferogram
3 degree rotated interferogram

## Slide 11: Virtual Lab Modelling
Slits rotating. Vertical size determination
Not rotated vertical interferogram →
3 degree rotated
← interferogram

## Slide 12: Conclusion During this month the Interferometer will start to operate Using Virtual Lab we can calculate some mistakes and then to check it experimentally on the interferometer

## Slide 13: Thank you for your attention!