## Slide 1: HED commissioning and first experiment
HED group at XFEL:
Karen Appel, Nicole Biedermann*, Sebastian Göde, Zuzana Konopkova, Emma McBride**, Motoaki Nakatsutsumi, Andreas Schmidt***, Konstantin Sukharnikov, Ian Thorpe, and Ulf Zastrau
* DFG PhD student **PPE VW-fellow at SLAC ***also MID team
Commissioning Meeting
March 9, 2016
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: HED subset: Warm Dense Matter (WDM)
Etherm ~ EFermi
1..100 eV
rWDM ≈ rsolid
strong coupling
G ≥ 1
Ecoulomb ~ Etherm
Condensed Matter <> Warm Dense Matter <> Hot Dense Matter
High free-electron density: penetration only up to critical density
nc = w²e0m/e²
access to volumetric plasma parameters only by short wavelength radiation (w > wP)
Isochoric heating
static compression
shock/ramp
compression

## Slide 3: Key Milestones and Time Plan
Q4 2015
Q1 2016
Q2 2016
Q3 2016
Q4 2016
Q1 2017
Q2 2017
Q3 2017
Q4 2017
___ Hutch PRR
___ SASE 2 hutch construction start
___ Hutch constr. complete
___ Infrastructure PRR
___ Basic infrastructure done
___ all complete (inst. of sensitive comp.)
Installation of HED instrument components
First x-rays in SASE2
Commissioning with x-rays
Q4 2017
Q1 2018
Q2 2018
Q3 2018
Q4 2018
Q1 2019
Q2 2019
Q3 2019
Q4 2019
…
…
___ Early user experiments SDL, x-rays only
___ PP laser ready at HED IC1
___ PP laser ready in laser room
Commissioning of HIBEF lasers
___ full-scale user experiments

## Slide 4: Day-1 early experiments
quasi-static compression using the dynamic diamond-anvil cell (dDAC)
a) isochoric heating with intense x-ray pulses b) addition of pump-probe laser

## Slide 5: Day-1 early experiments
quasi-static compression using the dynamic diamond-anvil cell (dDAC)
a) isochoric heating with intense x-ray pulses b) addition of pump-probe laser

## Slide 6: Diamond anvil cell: schematic set-up
Sample detector distance: 300mm
Sample
X-ray transmission through a single diamond anvil
XFEL (E > 15 keV)
Modular X-ray detector
X-ray diffraction

## Slide 7: Dynamic diamond anvil cell: possible day 1
Pinhole?
Piezo
DAC
~300mm
50 ms
100 ms
5 ms
5 ms
Study of:
Pressure induced phase transitions
Dynamic compression
Strain rates of 10^2-10^4 1/s
Detector
Pressure change

## Slide 8: X-ray beam parameters
Based on Harald Sinns parameters:
What we need:
Photon energy: 15-25 keV critical
Pulse duration: any (max. photon number), 300fs is OK
Repetition rate: 100 kHz (limited by our day-1 detector)
Number of pulses: ≤ 60 (detector capacity)
Focus: 5-15 um (defocusing with CRL3 to avoid damage to the diamonds)
Seeding: benefit but not crucial
Monochromator: benefit but not crucial
Notes: Before you start editing the slides of your talk change to the Master Slide view:
Menu button “View” > Slide Master:
Edit the following items:
1. On the Title slide (second master slide)
a) Click to add title of your talk
b) Click to add subtitle (conference, location, name of the speaker, date)
2. On the Slide Master (first master slide)
a) The 1st row in the violet header: Delete the existent text and write the title of your talk into this text field b) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
Close Master View

## Slide 9: Detectors
Boundary conditions:
Pointing stability crucial  pinhole (B4C material?)
Absorption scan with diode to align the gasket hole
Fast area detectors for dDAC:
Vacuum: NO
Jungfrau: capability up to 1 MHz with max.16 images

## Slide 10: Day-1 early experiments
quasi-static compression using the dynamic diamond-anvil cell (dDAC)
a) isochoric heating with intense x-ray pulses b) addition of pump-probe laser

## Slide 11: Isochoric heating: Generating uniform Warm Dense Matter
NEEDS
 To generate WDM one needs femtosecond radiation sources of high brilliance (no hydro-dynamics).
optical short pulse laser radiation (l ~ 1 µm) :
high reflectivity at plasma (nc = w²e0m/e² ~ 1021 e-/cm³)
very hot electron distribution ~ keV, MeV
steep gradients in ne und T - highly ionized - strong E- und B-fields
POSSIBLE SOLUTIONS
(laser-generated) electron or ion pulses heat matter indirectly and isochorically
or: ultrashort X-ray pulses from Free-Electron-Lasers (FELs)
fs-pulses of high intensity
penetration into the volume, no reflection (nc > 1024 e-/cm³)
linear photo-absorption of bound electrons
defined ‘warm’ photo-electrons and Auger electrons with E < 100 eV
due to short wavelength very low ponderomotive force (F ~ Il²) at high intensity
heating is isochorical and homogeneous

## Slide 12: Interaction of intense x-rays with dense matter
X-ray heating
  X-ray energy is absorbed in the electronic system
    Photo-ionization
    Auger-processes
    Electron scattering
  Intense x-ray pulse will modify ionization & structure and will generate a two-temperature non-equilibrium state.
  Ion temperature will catch up at ps levels.
U. Zastrau, P. Sperling et al., PRL112, 105002 (2014)
Monte-Carlo simulation: Evolution of the electron distribution for different fluences of the 92eV XUV pulse (a) 0.2 J/cm², (b) 1.5 J/cm², and (c) 5 J/cm².
N. Medvedev, U. Zastrau et al., PRL 107, 165003 (2011)
FLASH Experiment: Increase of diffuse scattering due to electron-ion equilibration

## Slide 13: Study of: Isochoric X-ray heating; Electron coupling processes
Cu, Al,….
Stacked/layered targets
XFEL parameters:
Eph: 8-25 keV (tunable if possible)
Rep rate: 100 kHz
Bandwidth: 10-3 - 10-4
Pulse duration: 100-500 fs
Photon flux: > 2x1011 (>1 mJ)
Focus: 1 micron (variable using CRL)
XES (front)
XES (rear)
Inelastic Scattering
Measuring (Te, ne, Ti)
High Rep rate allows to measure
Plasmon scattering at >9keV
Monochromator to clean pulse spectrum
Transmission
(attenuation)

## Slide 14: X-ray pump-probe – fs dynamic response
Solid foils
Targets at initial density
HED x-ray beam split & delay line (SDL)
Wavefront splitting
Recombination
Dt
S. Roling, H. Zacharias, et al.,
SPIE conf 8504, 850407 (2012)
BMBF project 05K10PM2
University of Münster
Multi-layer mirrors --- Variable delay up to ~23 ps (5 keV), ~4 ps (15 keV), 2 ps (20 keV)
Measure ultrafast dynamic response (electron-electron, electron-ion equilibration)
with 2 subsequent fs x-ray pulses launched into sample

## Slide 15: Isochoric X-ray heating; Electron coupling dynamics; Equilibration times (e-e, e-ion)
Cu, Al,….
Stacked/layered targets
XFEL parameters:
Eph: 8-25 keV (tunable if possible)
Rep rate: 100 kHz
Bandwidth: 10-3 - 10-4
Pulse duration: 15 fs
Photon flux: > 2x1011 (>1 mJ)
Focus: 1 micron (variable using CRL)
XES (front)
XES (rear)
Inelastic Scattering
Measuring (Te, ne, Ti)
High Rep rate allows to measure
Plasmon scattering at >9keV
Transmission
(attenuation)

## Slide 16: Plasmons in isochorically heated Aluminum Free-electron temperature measurement
P. Sperling, ... U. Zastrau et al., PRL 115, 115001 (2015)
U. Zastrau et al.,
JINST 8
P10006 (2013)
U. Zastrau et al.,
RSI 85,
093106 (2014)
isochorically heated Al:
r = 2.8 g/cm³ , Z = 3
(weak) e-e collisions as treated in Born approximation are insufficient to explain data

## Slide 17: Day-1 early experiments
quasi-static compression using the dynamic diamond-anvil cell (dDAC)
a) isochoric heating with intense x-ray pulses b) addition of pump-probe laser

## Slide 18: Pump-probe laser parameters

## Slide 19: Isochoric X-ray heating; Electron coupling dynamics; Equilibration times (e-e, e-ion)
Cu, Al,….
Stacked/layered targets
XES (front)
XES (rear)
Transmission
(attenuation)
XFEL parameters:
Eph: 8-25 keV (tunable if possible)
Rep rate: 100 kHz
Bandwidth: 10-3 - 10-4
Pulse duration: 15-500 fs
Photon flux: > 2x1011 (>1 mJ)
Focus: 1 micron (variable using CRL)
Timing jitter: < 15 fs
Reflectivity/Polarimetry
Measurement (ne, Te)
PP Laser parameters:
Eph: 800 nm
Rep rate: 100 kHz
Pulse duration: 15 fs
Photon energy: < 1 mJ
Timing jitter: < 15 fs

## Slide 20: Isochoric optical heating; Shock-compression; Electron coupling dynamics; Phase transitions
Cu, Al,….
Stacked/layered targets
XES (front)
XES (rear)
XFEL parameters:
Eph: 5-12 keV (tunable if possible)
Rep rate: 10 Hz
Bandwidth: 10-3 - 10-4
Pulse duration: 15 fs
Photon flux: > 2x1011 (>1 mJ)
Focus: 1 micron
Timing jitter: < 15 fs
Inelastic Scattering
Measuring (Te, ne, Ti)
Diffraction
(phase transitions)
PP Laser parameters:
Eph: 800 nm
Rep rate: 10 Hz
Pulse duration: 15-800 fs
Photon energy: 1 -100 mJ
Timing jitter: < 15 fs
XANES

## Slide 21: Summary X-ray parameters day-1
dDAC experiments
Photon energy: 15-25 keV critical due to absorption
Pulse duration: any (300fs OK)
Pulse energy: maximum
Repetition rate: 100 kHz (limited by our day-1 detector)
Number of pulses: ≤ 60 (detector capacity)
Focus: 5-15 µm
Seeding/Mono: not crucial
Isochoric heating experiments
Photon energy: 5-25 keV (tunable if possible) 8-25 keV
Pulse energy: maximum > 2x1011 (>1 mJ)
Pulse duration: 15 fs , 100-500 fs
Repetition rate: 10 Hz , 100 kHz
Number of pulses: single
Focus: 1 µm
Seeding /Mono none 10-3 - 10-4
Timing jitter < 15 fs

## Slide 22
Thank you.

## Slide 23: X-ray beam transport (XTD6; HED branch)
Overview
Sequence and location of HED beam transport components