## Slide 1: Tutorial 3: Low Level RF Control Systems
Sven Pfeiffer (DESY)

## Slide 2: Tutorial 3: Low Level RF Control Systems
Sven Pfeiffer (DESY)
Outline:
Introduction/Motivation
System Description
System Modelling
Feedback Controller Design
Examples
This tutorial is not about middleware (control systems)
http://ecetutorials.com/control-systems/
www.aps.anl.gov/epics
http://www.tango-controls.org/
http://tesla.desy.de/doocs/index.html
http://www.visaut-solutions.de/
etc…..
 Talk: M. Killenberg (Control system independent software development)

## Slide 3: 1. Introduction/Motivation
LLRF and Feedback
  Examples: ERL and FEL
Basic LLRF components
Disturbances and Noise - Fast and Slow Distortions

## Slide 4: LLRF Controls and Feedbacks
“Bunch Compressor Properties”
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor
High power ~MW
Low power ~V
Typical RF stability values:
Bunch Length Compressors, S. Di Mitri, CAS 2016

## Slide 5: Example 1: Energy Recovery Linac (ERL)
©Rey.Hori/KEK
Injector LINAC
Main LINAC
Circumference ~ 90m
Marger
Beam Dump
9-cell SC cavity x 2
2-cell SC cavity x 3
QL = 1 107
NC Buncher
QL = 1.1105
Photocathode DC gun
Design parameters of the cERL
Compact ERL @ KEK [Nakamura2014, Miura2015]
Constructed as a test facility of a 3-GeV ERL future plan.
The commissioning has been started from 2013.
 Continuous wave mode (CW)
RF frequency= 1.3 GHz
QL = 5105

## Slide 6: Example 2: Energy Recovery Linac (ERL)
beam dump
6.5 MeV, 100 mA
= 650 kW
linac module
3 x 7 cell srf cavities
44 MeV
modified Cornell booster
3 x 2 cell srf cavities
4.5 MeV
srf-gun
1.4 cell srf cavities
1.5-2.3 MeV, single solenoid,
merger
dogleg
test and diagnostic line
(5mA@10MeV dump,
energy & slice diag.)
bERLinPro = Berlin Energy Recovery Linac Project
100 mA / low emittance technology demonstrator (covering key aspects of large scale ERL)
 | Basic Parameter
max. beam energy | 50 MeV
max. current | 100 mA (77 pC/bunch)
normalized emittance | 1 mm (0.5 mm)
bunch length (straight) | 2 ps or smaller (100 fs)
rep. rate | 1.3 GHz
losses | < 10-5
Courtesy: Andreas Jankowiak, Concept of Energy Recovery Linacs, CAS2016, Hamburg, 04.06.2016

## Slide 7: Example 2: Free-Electron Laser (FEL)
© DESY 2015

## Slide 8: Free-Electron-LASer in Hamburg (FLASH)
ACC3
R56=180mm
R56=43mm
FLASH 1
ACC1
3rd
ACC7
Laser
BC2
BC3
FLASH 2
315 m
ACC4
Gun
ACC2
ACC5
ACC6
  NRF gun (QL = 1.2⋅105)
Klystron with 5 MW input power
  SRF cavities (QL = 3⋅106)
Klystron with 5/10 MW input power
Operated at 10 Hz (100 ms)
Pulse length ~ 1ms
 1% duty cycle
Max. 1.2 GeV beam energy
Wavelength > 4.1 nm

## Slide 9: Example ERL and FEL Parameters
Compact ERL @ KEK
Photocathode DC gun
NRF Buncher
  QL = 1.1⋅105
SRF cavities
  QL = 4.8⋅105 ... 1.3⋅107
Driven by SSA, Klystron, (IOT)
  1 Amplifier per cavity
   single cavity regulation
FLASH @ DESY
NRF gun
  QL = 1.2⋅105
SRF cavities
  QL = 3.0⋅106
Driven by Klystron
  1 amplifier for RF gun
   single cavity regulation
  1 amplifier per 8/16 cavities
   multi-cavity regulation
Operated in Continuous Wave (CW)
High beam loading (10’s of mA)
  100mA @ bERLinPro
Operated in Short Pulse (SP)
Moderate beam loading (mA)
Goal of LLRF Controls and Feedback:
Stabilize certain properties/values to high performance
Being able to measure the quantities

## Slide 10: Basic LLRF Components in an RF field Feedback Loop
Plant: Series connection of components
Amplifier (Klystron, Solid State Amplifier (SSA), …)
Cavities (normal- or superconducting – NRF or SRF)
Pre-amplifier etc…
Sensor: Ability to measure signal to be controlled
Pick-ups, antenna, magnetic loop, …
Controller: Processing unit
Analog (resistor, capacitance, operational amplifier, logic blocks, …)
Digital (Microcontroller, DSP, FPGA,…)
Plant
Sensor
Controller
output
measurement
reference
error
input
newsline.linearcollider.org
LLRF'15, Shanghai, Nov 3-6, 2015 (T. Miura)

## Slide 11: (LL)RF Applications
Linear or circular machines
Normal-/superconducting RF systems
RF field frequency
  Typical in accelerators: MHz … tens of GHz
CW – Continuous Wave
Continuous RF field
    Duty factor 100%
Pulsed Mode
Certain amount of time is useable for beam acceleration
  LP – Long Pulse Mode
    DF 10% - 50%
  SP – Short Pulse Mode
    DF 1 %, e.g. 1ms on, 99ms off
Amplitude
Time
Amplitude
Time
Repetition rate
Pulse duration

## Slide 12: Disturbances and Noise - Fast and Slow Distortions
Pre-Amp,
Klystron,…
Controller
r(t)
e(t)
du(t)
dP(t)
n(t)
yr(t)
yi(t)
ui(t)
ur(t)
Delay
Cavity
Plant
dy(t)
Other:
Aging, switching in electronics (e.g. fans), ground motion and vibrations, faults in devices and components, thermal heating within macro-pulse, …
Electromagnetic interference (EMI)
Drifts
  Electronics
  Synchronization system
  Timing distribution
Disturbance to plant input - du(t)
DAC, vector modulator, temperature & humidity (PCB)
Disturbance to plant - dP(t)
Pre-amplifier, Klystron, HV modulator, cavity length (motor tuner or water regulation), Beam (beam loading and multi bunch effects)
Noise – n(t)
ADC distortions, noise, quantization noise, temperature & humidity (PCB)

## Slide 13: 2. System Description for RF Field Control Loop
Sensor (RF detection)
Actuator (RF manipulation)
Amplifier
Cavity
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor

## Slide 14: RF detection
Baseband sampling (RF  BB)
Down-conversion from RF  IF  BB
Sensor
Phasor diagram
Q
I
e.g.:
fRF = 1.3 GHz
fIF = 54 MHz
I/Q pair as amplitude and phase information w.r.t. MO signal
data processing
e.g. LLRF Controller
Details  see backup slides
Envelope of RF signal
LO split by hybrid
I/Q sampled by 2 ADCs
[Hoffmann.2008]
RF signal

## Slide 15: RF Field Control Loop
Sensor (RF detection)
Actuator (RF manipulation)
Amplifier
Cavity
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor

## Slide 16: RF field manipulation
Up conversion using vector modulator
  MO signal split to 0o and 90o
VM with bandwidth usually tens of MHz (>> cavity BW)
~
Actuator
Master Oscillator
Notes: Aout = Ain + dA = Ain*sqrt(I^2+Q^2)  dA = ….
Can be also from BB  IF  RF

## Slide 17: RF Field Control Loop
Sensor (RF detection)
Actuator (RF manipulation)
Amplifier
Cavity
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor

## Slide 18: Amplifier Example: Klystron
Non-linear behavior in amplitude (e.g. saturation at max. output) and phase
Linearization of static characteristic curve
Bandwidth usually tens of MHz (>> cavity BW)
Characterization
Linearization
Input
Output
Examples: See PhD Thesis M. Omet, KEK, 2014
http://www-lib.kek.jp/cgi-bin/kiss_prepri.v8?KN=201424001&OF=8.
Amplifier
Output amplitude and phase is function of input amplitude

## Slide 19: RF Field Control Loop
Sensor (RF detection)
Actuator (RF manipulation)
Amplifier
Cavity
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor

## Slide 20: Example: 9 Cell SRF Cavity
http://tt.desy.de/desy_technologies/accelerators_magnets_und_cryogenic_technologies/weld_free_cavity/index_eng.html
Modelled with 9 magnetically coupled resonators (RCL circuits)
Pi mode is used for acceleration (TM010 mode)
8pi/9 mode only 800kHz separated from operating frequency  may influence accelerating field stability
Mechanical model is neglected at this point, see example at the end
[Schilcher.1998]

## Slide 21: From RCL circuit to cavity characteristics
RCL circuit equations need to be mapped to measurable cavity parameters (bandwidth, shunt impedance, quality factor etc.)
Start with high frequency modelling
End with baseband model required in LLRF control scheme with down-conversion
http://tt.desy.de/desy_technologies/accelerators_magnets_und_cryogenic_technologies/weld_free_cavity/index_eng.html
Consider only 1 RCL circuit
(as simplification)

## Slide 22: From RCL to differential cavity equation
RCL circuit Cavity characteristics
Differential cavity equation with harmonic RF driving term
V

## Slide 23: Differential cavity equation
Solution for input signal
(RF source) is given as cavity properties with approximation for high Q cavities :
Tuning angle
Angle between driving current and cavity voltage
Cavity detuning
Steady state amplitude and phase of cavity signal with respect to the RF source
Half cavity bandwidth
Notes: QL(w0/w – w/w0) = QL ((w0^2 – w^2) / w*w0) = QL(w0-w)(w+w0)/w*w0 = QL(dw)2w/w^2 = 2*QL dw/w

## Slide 24: Cavity baseband model
The high (carrier) frequency cavity model is not of our interest for studying the cavity response under feedback operation; we are interested at the baseband model (envelope of RF signal)!
Separation of fast RF oscillations from the slowly changing amplitude and phases of the field vector
I… in-phase (real)
Q… quadrature (imaginary)
Phasor diagram
First order cavity differential equation for envelope, i.e. the cavity baseband equation:
As short hand notation with complex vector field:
Remove fast changing part!

## Slide 25: Step response

## Slide 26: Additional Passband Modes
Short outline, for details, see [Schilcher.1998] and [Vogel.2007]
n-th mode:
Cavity field is the sum of all passband contributions
For variation in the coupling and loaded quality factor see e.g. [Vogel.2007]

## Slide 27: Summary System Description
RF field detection
  Down-conversion to baseband (envelop of HF signal)
  Direct A/P sampling nowadays possible (high speed ADCs)
     May worsen SNR of ADC
  Preferred method depends on your application
RF field manipulation
  Up-conversion from baseband to HF
  Bandwidth in tens of MHz range
Amplifier (Klystron)
  Mostly non-linear input/output behavior  Linearization desired
  Bandwidth in tens of MHz range
Cavity (9-cell SRF cavity)
  Differential equation as baseband model
  Bandwidth (Hz … kHz), detuning and higher order modes

## Slide 28: System Overview – Example at FLASH
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor
High power ~MW
Low power ~V
Several RF stations
System description will differ (uncertainties, couplings etc.)
 System identification/modelling ideally with input u(t) and output y(t)
Y(s)
U(s)

## Slide 29: System Overview – Example at FLASH
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor
High power ~MV
Low power ~V
Several RF stations
System description will differ (uncertainties, couplings etc.)
 System identification/modelling ideally with input u(t) and output y(t)
U(s)
Y(s)
System model by identification for model based controller design (LLRF controller)
Actuator
Amplifier
Cavity
Sensor

## Slide 30: 3. System Modeling - General
System Input-Output Modeling
Laplace Transformation
Bode Diagram
Example: System Modeling using Matlab

## Slide 31: System I/O Representation
Time domain
Convolution of impulse response g(t) and input u(t)
Makes analysis very complicated
Frequency domain
Laplace transformation used in system analysis
Multiplication of impulse response G(s) and input U(s)
Makes system analysis easier
input u(t)
plant
g(t) ; G(s)
output y(t)
input U(s)
output Y(s)
Notes: [Hermann Schmickler CAS 2013 – Trondheim, Lecture “Multi-bunch Feedback Systems”]

## Slide 32: Transformation into Frequency Domain
Fourier transformation
  Defined for all t
Laplace transformation
  Defined for all t ≥ 0 (causal system)
Inverse Laplace transformation

## Slide 33: Example: Cavity Equation
Find transformation as table in www
http://electricalstudy.sarutech.com/images/laplace-transform-table1.gif
From time domain
To frequency domain

## Slide 34: Example: Cavity Equation
Matlab: >> step(G)

## Slide 35: Bode diagram
G(s)

## Slide 36: Serial, parallel and feedback connection of blocks
Serial connection
+
+
-
+
+
+
Negative FB loop
Parallel connection
Feedback

## Slide 37: System Modelling
 System identification using special input signals
Grey Box
Model
Fully based on physical description
e.g. cavity equation
Usage of defined input signal u(t)  observation of output signal y(t)
 G(s) = Y(s)/U(s)
Parameter estimation based on physical equation
 Find some free parameters
A system model is a simplified representation or abstraction of the reality.
Reality is generally too complex to copy exactly.
Much of the complexity is actually irrelevant in problem solving, e.g. controller design.
[Ljung.1999]
[Pfeiffer.2014]

## Slide 38: System Identification using Matlab
System Identification Toolbox for SISO systems
Bandwidth, G(s),
In/out + 1% noise

## Slide 39: 4. Feedback Controller Design
Ways to control
Control Objective
Stability
Gang of four
Types of control

## Slide 40: Ways to Control
plant
FF
input
Open loop
(simple)
output
Feed forward
+
feedback
Feedback
-
sensor
disturbance
disturbance
input
disturbance
plant
plant
Precise knowledge on I/O behavior;
No action on disturbances
Precise knowledge on I/O behavior;
Act by feedforward e.g. on disturbances
 No action on signal to be controlled
Feedback and regulate the signal to be controlled by acting on the input
New system with new properties !
See: connection of systems
reference
output

## Slide 41: Objective of a feedback control problem
Make the output y(t) behave in a desired way by manipulating the plant input u(t)
Regulator problem (output disturbance rejection with constant reference)
  Counteract the effect of a disturbance dY(t)
Servo problem (reference tracking without disturbance)
  Manipulate u(t) to keep the output y(t) close to the reference r(t)
Goal: in both cases the control error e(t) = r(t) - y(t) should be minimal
Additional: High robustness to plant/process variations
 e.g. certain phase margin ~60 deg (see next slides)
Pre-Amp,
Klystron,…
Controller
r(t)
e(t)
du(t)
n(t)
yr(t)
yi(t)
ui(t)
ur(t)
Delay
Cavity
Plant
dy(t)
Feedback Loop:
Delay
Delay

## Slide 42: Stability Criteria's (incomplete!)
A system is stable if for a given bounded input signal the output signal is bounded and finite (BIBO stable); if not, the system is called unstable
g(t)
Stable or unstable linear systems
  Open loop or closed loop
  Unstable open loop: Stabilize closed loop system behavior using feedback controller
Stability check in s-domain by e.g.:
  Pole location (all poles in left half plane)
  Bode diagram
  Nyquist plot
  H-infinity norm for MIMO systems
  Non-linear systems  harmonic balance
Stable if impulse response absolutely integrable and bounded
This system has n poles and m zeros, and if it is physically realizable we have n ≥ m.
Understanding Digital Signal Processing (2nd Edition)
Mar 25, 2004by Richard G. Lyons
Pole location
Impulse response

## Slide 43: Stability Criteria's (incomplete!)
A system is stable if for a given bounded input signal the output signal is bounded and finite (BIBO stable); if not, the system is called unstable
g(t)
Stable or unstable linear systems
  Open loop or closed loop
  Unstable open loop: Stabilize closed loop system behavior using feedback controller
Stability check in s-domain by e.g.:
  Pole location (all poles in left half plane)
  Bode diagram
  Nyquist plot
  H-infinity norm for MIMO systems
  Non-linear systems  harmonic balance
Bode diagram
Gain margin
(at -180 deg.)
Phase margin
(at 0 dB)
Nyquist plot
Short: Do not encircle -1!
 Check stability for “Gang of four”
Stable if impulse response absolutely integrable and bounded

## Slide 44: Gang of Four
S(f)
Waterbed effect
Oscillations at high frequencies
2005 - "Respect the Unstable," IEEE Control Systems Magazine, Vol. 23, No. 4, pp. 12-25, August 2003.

## Slide 45: Types of Feedback Control
C(s)
G(s)
r(t)
y(t)
e(t)
u(t)
Classical FB Control
Frequency domain analysis
 Bode Diagram, Nyquist Plot
Modern FB Control
Time domain analysis
State space representation
Linear-quadratic regulator (LQR) etc.
H-infinity optimization by shaping the sensitivity and complementary sensitivity function

## Slide 46: 5. Examples
RF field feedback loop
  SRF accelerating module
  Difference SRF and NRF regulation
  NRF accelerating module
Microphonics suppression
Disturbance rejection
Analog FB
schemes
Processing delay and system bandwidth
Digital FB schemes
Short Pulse (SP)
Continuous Wave (CW)
CW
SP
LP
USP
Mode of operation
Off

## Slide 47: 5. Examples
RF field feedback loop
  SRF accelerating module
  Difference SRF and NRF regulation
  NRF accelerating module
Microphonics suppression
Disturbance rejection
CW
SP
LP
USP
Analog FB
schemes
Mode of operation
Processing delay and system bandwidth
Off
Digital FB schemes
Short Pulse (SP)
Continuous Wave (CW)

## Slide 48: Example: RF field Control @ FLASH
Radio Frequency Field
Pulsed operation - 10 Hz
2ms pulse length
(Filling, Flattop and Decay)
800 Bunches @ 1MHz (FLASH),
2700 Bunches @ 4.5MHz (XFEL)
Control Strategies
Adaptation by Learning
Fast Controller (FPGA)
Beam Loading Compensation

## Slide 49: Example: RF field Control @ FLASH
Pulsed mode (10 Hz) @ 1% duty cycle
System Identification
Low frequency
High frequency
LLRF Controls
MIMO FB for intra-pulse FB
Iterative Learning Control for pulse to pulse FF adaptation
BLC
[C. Schmidt.2010]

## Slide 50: Example: RF field Control @ FLASH
Additional cavity passband modes limits FB gain if no suppression is done
Variation of time delay  feedback the mode with different phases
  E.g. pos. or neg. FB
Using only proportional FB (lower left)
Including notch mode (lower right)
unstable
unstable
stable
XFEL spec
Oscillations

## Slide 51: Example: RF field Control @ FLASH
Feedback controller design based on HIFOOd
Shaping filter
Objective:
S: Sensitivity
CS: Control sensitivity
T: Complementary sensitivity
S: Low frequency
(e.g. ref. tracking, system bandwidth)
T: High frequency
(e.g. measurement noise)
CS: Typically at high frequency
(e.g. limits the control effort)

## Slide 52: Example: RF field Control @ FLASH
Analytical FB controller: Static gain and notch
HIFOOd: Static gain, low pass and notch
  This further reduces measurement noise in feedback loop

## Slide 53: Example: RF field Control @ FLASH
Learning feedforward
Iterative learning control (ILC)
Norm-optimal ILC (compact form)
  In contrast to lifted representation
  [N. Amann, D. Owens, E. Rogers, 1996]
Closed loop state space model (A, B, C) to update drive signal from pulse to pulse
Learning from error each lap…
Courtesy: C. Schmidt

## Slide 54: 5. Examples
RF field feedback loop
  SRF accelerating module
  Difference SRF and NRF regulation
  NRF accelerating module
Microphonics suppression
Disturbance rejection

## Slide 55: RF field Control for SRF and NRF cavities.
Plant: SRF
Pulsed mode (~1 ms)
  Half Bandwidth ~ 200 Hz
Plant: NRF-SWS
Pulsed mode (~ 6 μs)
  Half Bandwidth ~ 200 kHz
x1000
Open loop
f [Hz]
A
1.3 GHz
Baseband
http://newsline.linearcollider.org/2012/03/29/advances-in-scrf-cavity-performance-in-the-technical-design-phase/tesla-type-cavity-2/
http://pitz.desy.de/news/2011/galerie/
TDS@PITZ

## Slide 56: RF field Control for SRF and NRF cavities.
Pre-Amp,
Klystron,…
Controller
r(t)
e(t)
du(t)
dy(t)
n(t)
yr(t)
yi(t)
ui(t)
ur(t)
Delay
Cavity
Plant
Open loop
Time delay changes only phase
GM = 40 dB
PM ≈ 60 deg.
KP = 100
GM ≈ 0 dB
KP < 1
0 deg.  +1 (e(t) = r(t) - y(t))
-180 deg.  -1 (e(t) = r(t) + y(t))
From neg. to positive feedback
Unstable closed loop operation
for open magnitude ≥ 1
Plant: SRF
Pulsed mode (~1 ms)
  Half Bandwidth ~ 200 Hz
  Delay ~ 2 μs
Plant: NRF-SWS
Pulsed mode (~ 6 μs)
  Half Bandwidth ~ 200 kHz
  Delay ~ 2 μs
x1000

## Slide 57: RF field Control for SRF and NRF cavities.
Quantization
noise
Pre-Amp,
Klystron,…
Controller
r(t)
e(t)
du(t)
dy(t)
n(t)
yr(t)
yi(t)
ui(t)
ur(t)
Delay
DAC, VM
Cavity
Plant
Open loop
GM = 6 dB
KP = 2
KP = 100
PM ≈ 60 deg.
Plant: SRF
Pulsed mode (~1 ms)
  Half Bandwidth ~ 200 Hz
  Delay ~ 2 μs
Plant: NRF-SWS
Pulsed mode (~ 6 μs)
  Half Bandwidth ~ 200 kHz
  Delay ~ 700 ns
x1000
~ x 1/3
Single cavity regulation scheme
using 2 instead of 4 MicroTCA.4 boards
Water cooling unit

## Slide 58: RF field Control for SRF and NRF cavities.
Water cooling unit
Quantization
noise
Pre-Amp,
Klystron,…
Controller
r(t)
e(t)
du(t)
dy(t)
n(t)
yr(t)
yi(t)
ui(t)
ur(t)
Delay
DAC, VM
Cavity
Plant
Open loop
GM = 6 dB
KP = 2
= 2
Error suppressed
by x3
KP = 100
Requirements for NRF cavity regulation
Small time delay
Small disturbances
Low noise of subsystems
= 100
Error suppressed
by 1+KP = 101
PM ≈ 60 deg.
Plant: SRF
Pulsed mode (~1 ms)
  Half Bandwidth ~ 200 Hz
  Delay ~ 2 μs
Plant: NRF-SWS
Pulsed mode (~ 6 μs)
  Half Bandwidth ~ 200 kHz
  Delay ~ 700 ns
x1000
~ x 1/3
Single cavity regulation scheme
using 2 instead of 4 MicroTCA.4 boards

## Slide 59: 5. Examples
RF field feedback loop
  SRF accelerating module
  Difference SRF and NRF regulation
  NRF accelerating module
Microphonics suppression
Disturbance rejection

## Slide 60: Feedback Control for an NRF cavity.
Cooling water regulation
LLRF controls
LLRF Controls
Water regulation
 Coupling between both FB loops
1% DF @ 10 Hz, 4.5 MW
  Long term error ± 1 bit@Resolution
  (16 bit ADC) of 0.02 K – 0.03 K
 14mK (rms) temperature stability
Required stability for d < 0.01 deg
without LLRF control:

## Slide 61: LLRF based temperature estimation
Optimal temperature is proportional to detuning
Unknown: Tuning angle
LLRF system resolution:
  5 mdeg @ 1MHz BW
Averaging over RF pulse (x10 - 25)
-21 kHz/K
Measurable!
12000 for FLASH
1.3GHz
Phase difference cavity probe and forward signal within the RF pulse

## Slide 62: Cascaded Control Scheme.
Idea: Usage of LLRF Signals
Delayed TIRIS (9s) and TIN (5s) information
  Transition from cavity body to sensor
  Low pass behavior of temp. sensor
FLASH RF GUN data
Temp. sensor (12 bit ADC)

## Slide 63: Cascaded Control Scheme – Result @ FLASH.
Blue: single pulse, Red: mean 100 pulses (10s@10Hz)
Disturbance rejection from water circuit
Use pulse length variation to heat/cool gun body within pre-defined limits
Factor > 3 improvement

## Slide 64: 5. Examples
RF field feedback loop
  SRF accelerating module
  Difference SRF and NRF regulation
  NRF accelerating module
Microphonics suppression
  Disturbance like water temperature variation for NRF cavities
Disturbance rejection

## Slide 65: Microphonics and its Suppression
From pulsed mode to CW: smaller cavity bandwidth (QL… 107)
Microphonics dominate system performance
Harmonic and stochastic microphonics
  Distribution along cavities or modules (phase advance)
  Mechanical response on the individual cavities
Measurement @ FLASH (QL… 3⋅106)
 RF field control is active
 Large variations in amplitude stability
… due to compacting machine @ XFEL injector (distance ~ 400m)

## Slide 66: Example: Microphonics Suppression
A. Neumann, Compensating Microphonics in SRF Cavities to Ensure
Beam Stability for Future Free-Electron-Lasers, PhD thesis, 2008
Low pass:
Total model:
Individual modes:

## Slide 67: Example: Microphonics Suppression
Feedback (LP + PI)
Adaptive Feedforward
Blue: open loop
Red: PI control
Black: FF+PI control

## Slide 68: Passive & Active Microphonics Reduction
Measurement at CMTB - DESY
Try to decouple cavities from external noise sources
Microphonics reduced using anti vibration mat for vacuum pump
Courtesy of: Jürgen Eschke
Courtesy of: Radoslaw Rybaniec
Time [s]
Detuning [Hz]
Time [s]
Red: active noise cancellation (ANC) off
Blue: ANC on
Black: Pump on
Blue: Pump off
Red: Pump on/isolated
Applied feedback
Courtesy of: Radoslaw Rybaniec
[Rybaniec.2016]
Poster:
K. Przygoda
Passive measurement

## Slide 69: 5. Examples
RF field feedback loop
Microphonics suppression
Disturbance rejection

## Slide 70: Example: Disturbance rejection @ cERL (KEK)
PI feedback loop (CW mode) and disturbance rejection loop
Estimate the disturbance d using plant inverse and filter Q(s)
   Disturbance Observer Based control (DOB)
Reference:
F. Qiu et al., Phys. Rev. ST Accel. Beams 18, 092801, 2015.
Beam loading as disturbance 1.6ms and 800 μA
Power-supply ripples rejection
This approach may also be helpful for microphonics reduction

## Slide 71: Outlook: Timing and Synchronization
Basic assumption for digital control: Clock is working exactly!
Reality: Clock is working up to some accuracy & precision ...
The clock is synchronized to the MO. The clock is connected to all digital LLRF components!
FPGA, ADC, DAC, etc.
Goal: Improve the clock (timing and synchronization system)
 Use feedback control to enhance the behavior
 By this you can keep the assumption of ideal clock!
Cavity
~
Actuator
LLRF Controller
(analog or digital)
Master Oscillator
Energy gain
Energy spread
Amplifier
Electron beam
Sensor
Poster:
M. Heuer
M. Titberidze

## Slide 72: Questions???
Thank you for your attention!
Contact: sven.pfeiffer@desy.de
Many thanks for the contributions and useful discussions to
J. Branlard, L. Butkowski, K. Flöttmann, M. Heuer, M. Hierholzer, M. Hoffmann, M. Killenberg, F. Ludwig, A. Nawaz, M. Omet, K. Przygoda, R. Rybaniec, C. Schmidt, H. Schlarb, F. Stephan, E. Vogel, A. Jankowiak, S. Di Mitri, A. Neumann, T. Schilcher, F. Qiu
and all these many people I have not mentioned here…

## Slide 73: Bibliography
[Nakamura.2014] "Nakamura, Norio and others", Present Status of the Compact ERL at KEK, IPAC 2014
[Miura.2015] “Performance of the cERL LLRF System” LLRF workshop, 2015
[Hoffmann.2008], DESY Thesis; http://www-library.desy.de/cgi-bin/showprep.pl?desy-thesis-08-028
[Omet.2014], http://www-lib.kek.jp/cgi-bin/kiss_prepri.v8?KN=201424001&OF=8, PhD Thesis, KEK, 2014
[Schmidt.2010], DESY Thesis; http://www-library.desy.de/cgi-bin/showprep.pl?desy-thesis-11-019
[Pfeiffer.2014], DESY Thesis, http://www-library.desy.de/cgi-bin/showprep.pl?desy-thesis-14-030
[Schilcher.1998], Vector sum control of pulsed accelerating fields in lorentz force detuned superconducting cavities, Ph.D. thesis, Hamburg University, 1998
[Vogel.2007], High gain proportional rf control stability at TESLA cavities. Physical Review Special Topics - Accelerators and Beams 10, 2007
[Ljung.1999], (1999), System Identification, Theory for the User, Prentice-Hall Inc. USA, 2nd edition, ISBN 0-13-656695-2.
[Skogestad.2005], Skogestad, S. and Postlethwaite, I. (2005), Multivariable feedback control: Analysis and design, Chichester: Wiley, 2 edition, ISBN 9780470011676
[Stein.2003] - "Respect the Unstable," IEEE Control Systems Magazine, Vol. 23, No. 4, pp. 12-25, August 2003.
[Rybaniec.2016], FPGA based RF and piezo controllers for SRF cavities in CW mode, 20th Real Time Conference, 2016, Padova, Italy
Pictures from DESY website; https://media.desy.de/DESYmediabank/?l=de&c=3976 and other sources in www

## Slide 74: Backup Slides

## Slide 75: 1. Introduction/Motivation
Brief history of feedback control (human designed)
Automatic feedback control systems have been known and used for more than 2000 years (300 B.C. by a Greek mechanican)
  Water clock – slow tickle of water into measuring container
  Ensure at constant flowing rate  Float regulator similar to todays flush toilet
  If water level in the supply tank not at correct level the float opens or closes the water supply  1st feedback to keep supply tank at constant level
Around 1681 Denis Papin’s invention of a safety valve for regulation of steam pressure
In the 17th century Cornelis Drebbel invented a purely mechanical temperature control system
1745 speed control was applied to a windmill by Edmund Lee
Nowadays control systems theory began in the latter half of the 19th century
  Started with stability criteria for a third order system based on the coefficients of the differential equation
[Nise, Norman S. 2004, Control Systems Engineering, 4th Edition, Wiley, USA.]
Notes: [http://controlrc.ifac-control.org/history/history-of-control#3BC]
270 B.C Water clock invented by a Greek mechanician named Ktesibios. ([3] p112)([4] p4) The water clock, invented by the Greek mechanism Ktesibios, is the earliest known control device to be constructed. The device worked by way of a slow trickle of water, flowing at a constant rate, into a measuring container, where an indicator in the measuring container would then tell the time as the water level rises. In order for the device to be successful the supply tank had to be at a constant level so the water would flow into the measuring container at a constant rate. To do this Ktesbios used a float regulator, similar to the device used in today’s flush toilet. When the water in the supply tank is at the right level, the float only allows enough water into the timekeeping tank for the system to operate correctly. If the water level in the supply tank falls below or rises above the desired level, the float opens or closes the water supply until the water level returns to the desired level. From this description you can deduce that the water clock uses feedback to keep the supply tank at a constant level, therefore making it also the first device to incorporate feedback.
[Nise, Norman S. 2004, Control Systems Engineering, 4th Edition, Wiley, USA.]

## Slide 76: Digital vs. Analog Control

## Slide 77: RF detection
Direct Amplitude and Phase Detection
  No down-conversion
  Analog or digital (up to 800MHz ADCs)
Baseband sampling (analog I/Q detector)
Digital I/Q sampling
IF Sampling (non-I/Q sampling)
2.-4. is based on mixing a reference signal (LO) with the RF signal  RF signal down-converted to an intermediate frequency and into base-band
e.g.:
fRF = 1.3 GHz
fIF = 54 MHz

## Slide 78: Baseband sampling
Analog I/Q detector (direct conversion from RF to BB)
Multiplication with LO
LO split by hybrid  phase difference of 90 deg
Problem:
I/Q imbalance and offsets
 Phase dependent amplitude measurement
2 ADCs necessary for digitalization
 Higher costs, more space, reduced reliability

## Slide 79: Digital I/Q sampling
Alternative to baseband sampling: only 1 ADC and switched LO (by 90 deg)
Output signal represents I, Q, -I, -Q
Field vector computed by 2 samples (I/Q value) and shifted by n ⋅ 90 deg (n…0,1,2,3)
Problems:
Nyquist frequency is fs/4
Rectangular output signal  high bandwidth needed (amplifier etc.)
Notes: 1 ADC instead of 2  cost efficient

## Slide 80: IF Sampling (non-I/Q sampling)
RF signal mixed down to an intermediate frequency (IF)
Lower sideband
Upper sideband
If LO and RF frequency equal  lower sideband at DC, upper sideband at 2 fRF
If phase is 0 deg between LO and RF  amplitude detector (in phase) I
If phase is 90 deg between LO and RF  phase detector (in quadrature) Q

## Slide 81: IF Sampling (non-I/Q sampling)
RF signal mixed down to an intermediate frequency (IF)
 sampled and mapped into base-band
Step-window for I/Q detection
I/Q pair as amplitude and phase information w.r.t. MO signal
Lower sideband
Upper sideband
Low pass filtered

## Slide 82: Differential cavity equation
Solution for input signal
(RF source) is given as cavity properties with approximation for high Q cavities :
Tuning angle
Angle between driving current and cavity voltage
for
As cavity properties with approximation for high Q cavities:
Cavity detuning
… Cavity resonance frequency
… Driving frequency
Phase and Amplitude of cavity signal with respect to the RF source
Notes: QL(w0/w – w/w0) = QL ((w0^2 – w^2) / w*w0) = QL(w0-w)(w+w0)/w*w0 = QL(dw)2w/w^2 = 2*QL dw/w

## Slide 83: Differential cavity equation
Resonance curve for amplitude and phase in steady state (no transients)
Half cavity bandwidth
With time constant
The high (carrier) frequency cavity model is not of our interest for studying the cavity response under feedback operation; we are interested at the baseband model (envelope of HF signal)!

## Slide 84: Differential cavity equation
Variation of cavity detuning
Black: RF source
Red: Cavity field
Steady state solution of cavity model (field) for sinusoidal input signal (RF source) with amplitude of one
Phasor diagram

## Slide 85: Example: SRF Cavity (vector-sum)
Grey box modelling - MIMO
Low frequency (index r)
High frequency (index c)

## Slide 86: RF field Control for an NRF cavity.
Cooling water regulation
  GOAL: Constant cooling, i.e. keep geometry and reflected signal constant
Cooling water regulation
LLRF controls
How: Variation of input water temperature TIN
Disturbance for LLRF regulation
How: Variation of input signal PIN
Disturbance for water circuit
RF-field control  LLRF control
  GOAL: Maintain constant acceleration field in amplitude and phase
Separation of both feedback loops is impossible for precision regulation

## Slide 87: Water regulation/RF gun cooling
Water from GUN
Water to GUN
Cold water and valve position to be controlled
Warm water, pump, heater, tank
With applied RF power in steady state
  nominal operation @ 4.5MW, 600us RF pulse
Mixing valves are controlled via PLC with PI control scheme
  Goal: Keep RF GUN (IRIS) temperature constant, e.g. on-resonance
  Long term error ± 1 bit@Resolution
  (16 bit ADC) of 0.02 K – 0.03 K
 14mK (rms) temperature stability
Required stability for d < 0.01 deg
without LLRF control:

## Slide 88: Example: RF GUN Frequency Control @ FLASH
Detuning:
Kf/T = 21 kHz/K
QL = 10.000
f0 = 1.3 GHz
Resolution ~ 0.1 mK
(Sub-mK)
[K]
Pk2pk ~ 0.1K
[deg.]
Pk2pk ~ 0.4o
Operated in pulsed mode
Pulse Width Modulation
to keep cavity on resonance
PWM off
RF gun temperature disturbance rejection
Normal conducting RF (NRF) cavity as heater @ FLASH
Factor > 3 improvement
[K]
Pk2pk ~ 0.03K
[deg.]
Pk2pk ~ 0.17o
PWM on
Extremely precise frequency control is essential for all NRF cavities due to limited FB gain caused by high bandwidth (e.g. QL = 10000  f1/2= 65kHz) and relatively large system delay (~1 μs)!
Same y-scaling for both panels