## Slide 1: Next steps and CHESS-2 data flow 5 May 2016 this version is the minutes – with notes and new slides added (the new slides are indicated with pink titles)
J. J. John, P. Caragiulo, H. Grabas

## Slide 2
Agenda
Review current work and discuss steps for next week
Walk through CHESS-2 data format
Discuss options for CHESS-2 data emulator

## Slide 3
Completed actions (since last week)
Jaya John: [done] send link to CHESS-2 review slides to Wojtek
Jaya John: [done] e-mail ABC130 emulator random hit code and document to everyone at USTC.
Wojtek: [done] set up invitations on GitLab for Weiguo, Prof. Song, Chenchen Wu and Tianbo Xu.

## Slide 4
Ongoing and new actions
Wojtek and Jaya John: [in progress] set up their Nexys Video with current ITSDAQ firmware and SCTDAQ software – on CentOS for UBC, Windows for Oxford. So far, CentOS is not the most friendly distribution to set up, requires some extra steps and installations. Currently resolving firewall issues.
Wojtek: [in progress] check the ABC130* code from Matt (ITSDAQ repo) in to GitLab. Could also check in the ABC130 command decoder, but could be later also.
Jaya John: add the SACI code to GitLab
Jaya John: prepare a mini-spec for CHESS-2 data emulator -- outline of spec discussed during this meeting
Jaya John: also ask CHESS-2 designers about timeframe for the CHESS-2 specification. Even a partial spec will be a great help for understanding.
After discussion: Hervé will work on documenting the parts which are most urgent for us. We agreed that the most important details for us now are the output interface and timing (after the serialiser).
The register and configuration details will not be needed initially. We will need them later on.
Hongbo and Weiguo: assist our colleagues at USTC to obtain CERN accounts, for gaining access to the ITSDAQ repository.
CERN accounts are in progress – need passports first. Weiguo has access to GitLab. Wojtek sent invitations also to everyone at USTC. Not working yet.
Will need to generate public SSH keys – for example with PuttyGen? Then we could use SSH to access the GitLab.
Wojtek: will test accessing via SSH and send instructions to all.

## Slide 5
CHESS-2 data format
Introduction to this key topic for the ABCN’:
How does CHESS-2 process and encode the hits received on the pixel array?
What is the format of data the ABCN’ will receive from CHESS-2?
These slides are based on Pietro Caragiulo’s CHESS-2 slides presented at ATLAS Upgrade Week, 18 April.

## Slide 6
CHESS-2 sensor overview
This is an overview of the CHESS-2 layout. There are 3 arrays of 128 strips each. The 3 arrays have independent data outputs. From a data out point of view, the arrays are identical and can be considered in isolation.
diagram: H. Grabas, UCSC
24.3 mm
When we get to configuring the arrays, then there are some small differences in how to configure the top 2 mirrored arrays, compared to the bottom (single) array.

## Slide 7
CHESS-2 Architecture
This is the block diagram for a single array (1 array out of the 3 in total)
diagram: P. Caragiulo, SLAC
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
Acquisition
Encoding
Configuration and Calibration
Read-out
Pixels are organised as:
128 strips, containing 32 pixels each
or 128 rows x 32 columns

## Slide 8
CHESS-2 Data Flow – 1/4
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
This is a high-level overview only of the data flow.
The following slides will go into details of the data format at each step.
After discussion: for the ABCN’, the key is to understand the format of the data out of the Serializer. The process by which this data is encoded is still useful to understand, though.
adapted from P. Caragiulo’s diagram

## Slide 9
CHESS-2 Data Flow – 2/4
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
2) strip encoding represents the hits occurring on each strip
adapted from P. Caragiulo’s diagram

## Slide 10
CHESS-2 Data Flow – 3/4
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
2) strip encoding represents the hits occurring on each strip
adapted from P. Caragiulo’s diagram
3) hit encoding reduces the data to the first 8 hits among the 128 rows and identifies which strips were hit

## Slide 11
CHESS-2 Data Flow – 4/4
adapted from P. Caragiulo’s diagram
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
2) strip encoding represents the hits occurring on each strip
4) the hit encoding is serialized, then transmitted off-chip using LVDS
3) hit encoding reduces the data to the first 8 hits among the 128 rows and identifies which strips were hit

## Slide 12
CHESS-2 Floor Plan (sensor layout) – 1/4
-- P. Caragiulo, SLAC
Pixels
2cm
4mm
Columns Selector
Rowss Selector
Pixels – Row, Column selectors

## Slide 13
CHESS-2 Floor Plan (sensor layout) – 2/4
-- P. Caragiulo, SLAC
Strip
Encoding
Strip Encoding

## Slide 14
CHESS-2 Floor Plan (sensor layout) – 3/4
-- P. Caragiulo, SLAC
8 Hits
Selection
and memories
8 Hit Encoding Logic & Memories

## Slide 15
CHESS-2 Floor Plan (sensor layout) – 4/4
-- P. Caragiulo, SLAC
Serializer & LVDS TX/RX
Serializer – LVDS TX/RX

## Slide 16
hit
Strip encoding
-- adapted from P. Caragiulo’s diagram
hit
32 columns = 32 pixels in each strip
128 rows = 128 strips
column 0
column 1
column 2
…column 31
column
address
(5 bits)
Multiple hit flag
no hits
no hits
1 hit in col 2
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
1 hit in col 31
* = 1st hit was in col 0, + there was at least 1 more hit in this row
see * below
interpretation:
Hit/no hit (internal signal)
msb
lsb
hit
hit
row 0
row 1
row 2
row 3
row 4
row 5
row 6
row 7
row 8
row 9
row 10
row 11
(etc)
column 3…
This first stage of encoding represents the state of each of the 128 strips (rows) as 7 bits in all:
The first hit in a strip appears as a 5-bit column address. First means the column with the lowest column address, or left-most column containing a hit.
This is followed by a 1-bit flag to indicate if there were any more hits within a strip.
There is also a 1-bit hit/no hit indicator – this is an internal signal to the next block.
An example with 4 hits in the array of pixels:
mean 0
mean 1

## Slide 17
Hit encoding
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
1
3
2
Output bus 8x13 bits
Memory
-- adapted from P. Caragiulo’s diagram
row 0
row 1
row 2
row 3
row 4
row 5
row 6
row 7
row 8
row 9
row 10
row 11
row 12
row 13
(etc.)
row 2 had 1 hit in col 2
= 1st write to memory
row 9 had 1 hit in col 31
= 2nd write to memory
row 10 had its 1st hit in col 0,
+ there was at least 1 more hit within row 10
= 3rd write to memory
interpretation:
Multiple hit flag
Hit/no hit (internal signal)
column address (5 bits)
strip (row) address (7 bits)
Multiple hit flag
column
address
(5 bits)
msb
lsb
msb
lsb
lsb
msb
These bits are ordered to match the Serializer’s memory . Note, the order was corrected with Pietro’s input, compared to the meeting of 5 May.
Multiple hit flag
column address (5 bits)
strip (row) address (7 bits)
The second stage of encoding sparsifies the strip data:
The strip-encoded data is checked for each of the 128 strips
The first 8 hits seen within the array, starting from row 0 at the top of the array, down to row 127 at the bottom, are encoded to output as 13 bits: multiple hit flag (1 bit) + column address (5 bits) + row address (7 bit)
mean 0
mean 1

## Slide 18
Storage and output of encoded hits - 1/3
CHESS-2 uses specialised circuitry to be able to record the first 8 hits to memory within the 25ns available (ATLAS bunch crossing period). More detail in these CHESS-2 slides.
What is important for the ABCN’ and CHESS-2 Data Emulator is understanding the memory which is the input to the Serializer block and the serialization.
The memory format is 8 bits x 13 bits/hit as shown below. There is also a 14th internal bit for each hit, Data Valid. This is effectively 14 rows x 8 columns. The memory operates as follows:
  During an initial reset phase, all 14 x 8 bits are cleared to zero, including the Data Valid bits.
  Then, as the first 8 hits are identified, for each of the 8 hit memories, Data Valid is set to 1 when the hit encoding circuit writes to that memory.
  Each row is served by an LVDS driver. The memory is emptied (clocked out) using a 320MHz clock.
Data Valid’s purpose is to distinguish between these two cases:
Internal Data
Valid bit
Data Valid is 0 => this hit memory does not contain a real hit. So this memory is empty and there were fewer than 8 hits for this cycle.
interpretation:
Data Valid is 1 => row 0 had 1 hit in column 0
column address (5 bits)
strip (row) address (7 bits)
Multiple hit flag
mean 0
mean 1

## Slide 19
Storage and output of encoded hits – 2/3
Continuing with the example of the 4 hits shown on earlier slides, the hits are written to memory and serialized as follows:
First write to memory
Second write to memory
Third write to memory
In this example, there are only 3 strips which are reporting hits, so the remaining 5 memory slots are not written and their Data Valid bits are 0.
Internal Data
Valid bit
column address (5 bits)
strip (row) address (7 bits)
Multiple hit flag
msb
lsb
lsb
msb
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Receiver
320 MHz clock
Serializer
Outs<0> = Sync/Data Valid
Outs<1> = Multiple hit flag
Outs<2> = Col<4>
Outs<3> = Col<3>
Outs<4> = Col<2>
Outs<5> = Col<1>
Outs<6> = Col<0>
Outs<7> = Row<0>
Outs<8> = Row<1>
Outs<9> = Row<2>
Outs<10> = Row<3>
Outs<11> = Row<4>
Outs<12> = Row<5>
Outs<13> = Row<6>
LVDS clock, 320 MHz
mean 0
mean 1

## Slide 20
these just summarise the values of the Outs<*> outputs
Multiple hit flag
3.125ns
Storage and output of encoded hits – 3/3
column address (5 bits)
strip (row) address (7 bits)
Internal Data Valid bit
msb
lsb
lsb
msb
Serializer memory contents:
Outs<0>
Outs<1>
Outs<2>
Outs<3>
Outs<4>
Outs<5>
Outs<6>
Outs<7>
Outs<8>
Outs<9>
Outs<10>
Outs<11>
Outs<12>
Outs<13>
Clock (320 MHz)
2
31
0
0
0
0
0
0
2
9
10
0
0
0
0
0
Col addr
Row addr
25ns – one complete readout cycle
Output waveforms:
first hit
second hit
third hit
fourth hit
fifth hit
sixth hit
seventh hit
eighth hit
mean 0
mean 1

## Slide 21
Discussion about CHESS-2 Data Emulator
We discussed two main approaches to generating random data in the CHESS-2 format:
Approach | Assessment
1. Generate random hits on a 128 x 32 array of bits, modelling the pixel array. Process the hits like CHESS-2, with strip encoding, then hit encoding, then serializing the data out. | This requires more FPGA resources and more development and verification time. Considering that CHESS-2 needed special asynchronous circuitry to process all hits within 25ns, it is unlikely that an FPGA implementation could be so quick. So there would be a multi-cycle pipeline. If we consider adding advanced features such as large cluster hits which span adjacent pixels: it would be easier to implement cluster hits with this approach.
2. Generate random hits on an 8x13 array of bits, representing the Serializer memory. Serialize this data out. | This is simpler to develop and uses less FPGA resources. For single-pixel hits, the outcome is the same as the first approach.

## Slide 22
Discussion about CHESS-2 Data Emulator
It’s best to reduce development time and use of FPGA resources.
We think it is fine to begin with single-pixel hits.
So we believe it’s best to pursue the second approach.