## Slide 1: MicroTCA systems at ESS
Simone Farina
Integrated Control System Division
www.europeanspallationsource.se
2016 December 07

## Slide 2: Outline
The European Spallation Source Facility;
Systems for beam control and instrumentation;
MicroTCA components selection;

## Slide 3: Facility Overview
The European Spallation Source is a Partnership of 17 European Nations committed to the goal of collectively building and operating the world's leading facility for research by use of neutrons
Facility located in Lund in southern Sweden and Data Management and Software Centre situated in Copenhagen
First protons delivered on a rotating tungsten target in 2019 and fully operational (22 instruments) in the second quarter of the 21st century
Around 35% of the construction budget is provided through In-Kind Contributions

## Slide 4: Accelerator Overview
Key Parameters:
Energy 2 GeV
Current 62,5 mA
Pulse Lenght 2,86 ms
Pulse Repetition Frequency 14 Hz
Average Power 5 MW

## Slide 5: Three layer strategy - control systems at ESS
ICS has adopted a three layer strategy for implementing the control system based on signal speed
  A custom made platform based on microTCA for applications with data acquisition exceeding 100 kHz
  The CPU will run EPICS and the FPGA will have a complete application development environment
  For slower signals, EtherCAT will be used as a real-time fieldbus with good price/performance ratio
  Synchronization and event information are key for applications where a full custom platform solution would be too costly
  Low speed signals are handled with commercially available PLC systems from Siemens
  This is a cost-effective solution that addresses ESS reliability and maintainability requirements
  The PLCs will be connected to EPICS for further integration into the control system
Signal speed
10 Hz
1 Hz
0.1 Hz
100 Hz
1 kHz
10 kHz
100 kHz
1 MHz
10 MHz
Digital controls platform
EtherCAT
Industrial automation (PLC)
A custom made microTCA board with a powerful FPGA. A FPGA framework constitutes the development environment. The CPU board runs EPICS
EtherCAT I/O modules that are connected to commercial or open-source EtherCAT master controllers which are in turn connected to the EPICS based control system
Slower signals are handled by industrial automation (PLC) for reliability and cost reasons. The standardized platform for ESS applications comes from Siemens

## Slide 6: Beam Instrumentation
18 Beam Current Monitor Systems
99 Beam Position Monitor Systems
1 Doppler Shift Measurement System
4 Emittance Meter Units
4 Farady Cup Systems
3 Insertable Beam Stops
4 Longitudinal Brunch Profile Monitor Systems
10 Non-invasive Profile Monitor Systems
14 Wire Scanner Systems
273 Beam Loss Monitor Systems
2 Target Imaging Systems
3 Aperture Monitor Systems
1 Grid System

## Slide 7: Beam Instrumentation
Signal speed
10 Hz
1 Hz
0.1 Hz
100 Hz
1 kHz
10 kHz
100 kHz
1 MHz
10 MHz
uTCA
EtherCAT
Industrial automation (PLC)
Three system architectures selected depending on performance and cost optimization:
PLC
  Industrial, process I/O
  Safety systems, high reliability
EtherCAT
  mid-range, beam synchronised I/O
  Used mainly as a fieldbus
MTCA
  High-speed front-end processing
  Digital Frontend Platform

## Slide 8: µTCA Infrastructure: crates
Plans to support two crate variants :
12 slots 9U for systems requiring more than 6 AMCs and/or more than 4 RTMs;
Constraints:
Cooling scheme: front to rear, defined by rack ventilation;
Triggers and Interlocks: signals conveyed to all AMCs, M-LVDS lines availability;
ISSUE: very few options for 3U crates with front to rear cooling
6 slots 3U to reduce the number of racks deployed.

## Slide 9: µTCA Infrastructure: MCH & PM
MicroTCA Carrier Hub :
N.A.T. selected, less interoperability issues found up to now.
Power Modules:
Many products under review:
Telkoor
Wiener
N.A.T.
Final choice made according to instrument requirements and space constraints.
More than one product might be selected.

## Slide 10: AMC boards: EVR
ESS Timing system based on Micro-Research Finland products:
clocks from/to TCLKA/TCLKB
24 differential lanes to RTM (no RTM designed yet)
driving/receiving differential triggers AMCRX/TX 17 through 20
front panel 4 x TTL outputs, 2 x TTL inputs (LEMO)
VHDCI front panel connector for IFB-300 interface box
Delay compensation and feedback
Segmented data buffer
Event masking in sequencer (event master/generator)

## Slide 11: AMC boards: LO & CLK
Local Oscillator (LO) and ADC Clock generation/distribution
ESS Bilbao LO generation (pizza-box solution)
Both solutions work for 352 MHz and 704 MHz
ISE – Polish Electronics Group Warsaw University – MicroTCA.4 AMC+RTM solution

## Slide 12: AMC boards: ICS supported
Beam Instrumentation will be built using 2 types of AMC boards provided by PSI through an in-kind collaboration:
AMC FMC (HPC) Carrier:
Support for 2 HPC FMC cards
Ultrascale FPGA family to cover also high demanding applications
Zone 3 assignment according to DESY recommendation for digital applications to promote standardization
AMC Digitizer board:
Similar digital architecture to FMC Carrier
Zone 3 assignment according to DESY Class A1 recommendation for analog applications
FMC slot LPC or HPC to interface to non-MTCA systems would be a nice feature

## Slide 13: FMC cards: ICS supported
ACQ420 (4 channel 16-bit 500 to 2000 ksps)
AD/DA Converter boards:
DAC 3113 (dual channel 16-bit/500 Msps DAC and 2 channels 16-bit/250 Msps ADC
FM-S14 (Quad-SFP/SFP+ up to 10Gbps)
FMC-4SFP+ (Quad/Dual-SFP/SFP+)
Additional FMC cards might be supported according to BI requirements
ADC 3112 (4 channels 12-bit/900(1000) Msps
or 2 channels 12-bit/1800(2000) Msps)
ADC 3110/3111 (8 channel 16-bit 250Msps)
High speed interface cards:
EtherCAT slave, in-kind project (Estonia)

## Slide 14: AMC boards: LLRF
Current firmware implementation based on Struck SIS8300-L2 but designed to allow easy porting to an In-Kind contributed digitizer
Timing board provides:
  Pulse coming
  Pulse start
  Pulse End
RTM board with piezo drivers currently under development by in-kind contributor (Poland)
Currently evaluating option to embed a CPU in the FPGA & ADC board
Phase reference
Timing
Interlock
LAN
Ethernet (port 0/1)
Control (PCIe)
Triggers (ports 17-20)
LO
Signals from:
PowerAmp
Cavity
PreAmp
VM

## Slide 15: AMC boards: BPM
Reuse as much as possible the LLRF hardware and firmware
Bandwidth
Custom RF front-end needed due to:
Input dynamic range
Two solutions under test (RTM)
External filters + Custom RTM (design by SLAC + ESS)
COTS RTM + custom external RF Front-End

## Slide 16: AMC boards: BPM
From BPM
From BPM
External BPF
352 MHz or 704 MHz
10 MHz bandwidth
...

## Slide 17: Summary
ESS will use MTCA platform as base for complex Beam Instrumentation and LLRF
In-Kind budget type pushes towards development of new components by partner nations companies
Many instruments already under test using COTS hardware
Vielen Dank für Ihre Aufmerksamkeit