## Slide 1
Andranik Tsakanian
Helmholtz-Zentrum Berlin, Albert-Einstein-Str. 15, 12489 Berlin
Annual Matter & Technology Meeting
31 Jan. - 2 Feb. 2017
GSI, Darmstadt, Germany
SRF Implementation in BESSY VSR for Picosecond X-ray Pulse Production

## Slide 2
Outline
Introduction to BESSY II storage ring
SRF Upgrade - BESSY VSR & Highlights
SRF Cavity Specific Designs
HOM Power Levels in SRF Module
Summary
2

## Slide 3
BESSY II Storage Ring
BESSY II is a 1.7 GeV synchrotron radiation source operating for 20 years in Berlin
Core wavelength in the range from Terahertz region to hard X rays
BESSY II Parameters | 
Lattice | DBA
Circumference | 240 m
Energy | 1.7 GeV
Current | 300 mA
RF Frequency | 500 MHz
RF Voltage | 1.5 MV
Bunch Length | 15 ps
Emmitance | 6 nm rad
2

## Slide 4: The Concept of BESSY VSR
  Low alfa operation only 12 days/year
  (all beamlines) ------- Low flux
  Femtoslicing is continuously operated ( only 1 beamline) -- Low flux
Limited pulse length in storage ring
Hardware (RF cavities)
At high current beam becomes unstable
  For ps pulses, flux is reduced by nearly 100
Machine optics
BESSY II @ present
Normal conducting cavity system
1
10
10−4
10−3
10−2
10−1
1
10
0.1
Bunch current (mA)
RMS bunch length (ps)
User optics
Low alpha optics
Bursting mode begins
4

## Slide 5: The Concept of BESSY VSR
  Low alfa operation only 12 days/year
  (all beamlines) ------- Low flux
  Femtoslicing is continuously operated ( only 1 beamline) -- Low flux
Limited pulse length in storage ring
Hardware (RF cavities)
At high current beam becomes unstable
  For ps pulses, flux is reduced by nearly 100
Machine optics
BESSY II @ present
Normal conducting cavity system
1
10
10−4
10−3
10−2
10−1
1
10
0.1
Bunch current (mA)
RMS bunch length (ps)
User optics
Low alpha optics
Bursting mode begins
4
  Can we design a system offering both possibilities simultaneously?

## Slide 6
1
10
10−4
10−3
10−2
10−1
1
10
0.1
Bunch current (mA)
RMS bunch length (ps)
Low alpha
User optics
Low alpha optics
Ith roughly proportional to V´rf σ2
80 × more voltage gradient
User optics
Supply short pulses down to 1.5 ps
  (100 × more bunch current )
Low α permits few 100 fs pulses
Configure BESSYVSR so 1.5 ps and 15 ps bunches can be supplied simultaneously for maximum flexibility and flux!
Limited pulse length in storage ring
Hardware (RF cavities)
At high current beam becomes unstable
  For ps pulses, flux is reduced by nearly 100
Machine optics
BESSY II @ present
Normal conducting cavity system
5
The Concept of BESSY VSR

## Slide 7
BESSY II, SC Upgrade – BESSY VSR
6
Voltage / MV
Present
Time [ ns ]
Voltage: 1.5 MV @ 0.5 GHz
15 ps bunch
G.Wüstefeld et al. „Simultaneous long and short electron bunches in the BESSY II storage ring“ , IPAC2011

## Slide 8
Voltage / MV
Time [ ns ]
BESSY II, SC Upgrade – BESSY VSR
SC Upgrade
6
Voltage / MV
Present
Time [ ns ]
Voltage: 1.5 MV @ 0.5 GHz
15 ps bunch
1.5 ps bunch
G.Wüstefeld et al. „Simultaneous long and short electron bunches in the BESSY II storage ring“ , IPAC2011

## Slide 9
Voltage / MV
Time [ ns ]
BESSY II, SC Upgrade – BESSY VSR
SC Upgrade
6
1.5GHz and 1.75GHz ---- RF beating
(modulate RF focusing)
Odd (voltage cancelation, 15 ps bunches)
Even (voltage addition, 1.1 ps)
G.Wüstefeld et al. „Simultaneous long and short electron bunches in the BESSY II storage ring“ , IPAC2011
Voltage / MV
Present
Time [ ns ]
Voltage: 1.5 MV @ 0.5 GHz
15 ps bunch
Voltage / MV
Time [ ns ]
BESSY VSR
Long Bunch
Short Bunch
1.5 ps bunch

## Slide 10
BESSY II, SC Upgrade – BESSY VSR
7
BESSY VSR Filling Patterns
Baseline
High concentration of long bunches populated with high current
(flux hungry users)
Few high current - short bunches
(slicing bunches …)

## Slide 11
BESSY II, SC Upgrade – BESSY VSR
7
BESSY VSR Filling Patterns
Baseline
Extended
High concentration of long bunches populated with high current
(flux hungry users)
Few high current - short bunches
(slicing bunches …)
More short bunches ( Extended )
High Population of long & short bunches at the same time

## Slide 12
Variable pulse length Storage Ring
BESSY II SC Upgrade – BESSY VSR
Simultaneous Store of long & short bunches
SC Upgrade
SRF SYSTEM: 2@1.5 GHz & 2@1.75 GHz
8

## Slide 13
Variable pulse length Storage Ring
BESSY II SC Upgrade – BESSY VSR
Simultaneous Store of long & short bunches
SC Upgrade
SRF SYSTEM: 2@1.5 GHz & 2@1.75 GHz
CHALLENGES
CW operation @ high field levels E=20MV/m
  Peak fields on surface (discharges, quenching)
High beam current (Ib=300mA),
Cavity HOMs must be highly damped (CBIs)
Exotic cavity design (damping end-groups)
Integrating in existing storage ring
Transparent Parking of SRF Module.
8

## Slide 14: BESSY VSR SRF Cavity Designs
FPC
5 x Waveguide dampers, HOM loads (warm)
Large beampipe radius – better HOM propagation
Waveguides are below cutoff for fundamental  can be moved close to the cavity for heavy damping.
Strong HOM damping concept
Tune fundamental mode: field flatness, R/Q …
Control cavity HOM spectrum (off-resonance condition) during the design.

## Slide 15
BESSY VSR SRF Cavity Designs
Lactive
Simulation Results – for both Cavity (TM010) |  |  | 
 | 1.5GHz | 1.75GHz | Design goal
Lactive | 0.5 m | 0.43 m | 
Frequency [GHz] | 1.4990 | 1.748887 | 3th & 3.5th harm. of 499.65 MHz
Qext | 4.997*107 | 4.266*107 | 
G [Ω] | 277.8 | 280.04 | 
Epk / Eacc | 2.313 | 2.407 | ≤ 2.4
Bpk / Eacc [mT / (MV/m)] | 4.96 | 5.023 | ≤ 5.3
R/Q0 [Ω] | 487.17.34 | 479.86 | ≥ 90 per cell
R/Q0 (Active) [Ω] | 531.83 | 524.07 | 
µff | 97.56% | 98.43 % | ≥ 95%
10

## Slide 16
Port Num. | Coherent Power [W] | 
 | 1.5 GHz | 1.75GHz
1-FPC | 27.11 | 22.88
2 | 120.18 | 174.14
3 | 120.03 | 174.52
4 | 100.86 | 127.86
5 | 102.15 | 128.00
6 | 103.28 | 140.42
7-BmP | 257.69 | 267.92
8-BmP | 305.88 | 248.55
Sum Coh. None-Coh. | 1137.19 1289.91 | 1284.28 1408.18
1.5GHz Design-FA
1.75GHz Design-A4
HOM Power of Single Cavity – VSR Baseline beam
Spectrally Weighted with “Baseline” pattern
Both cavities are not hitting any of beam resonances that are multiple of 250MHz (Coherent and none-coherent powers are at the same level).
Cornell‘s ERL cavities are designed to run at about 100-200W HOM Power.

## Slide 17
HOM Power of Single Cavity – VSR Baseline beam
HOM Spectrum in Fundamental Power Coupler

## Slide 18
Design of the 1.5 GHz BESSY VSR coupler
Coax coupler diameters: 49 mm x 20 mm.
Two ceramic windows to maintain vacuum.
Inner an outer coax bellows provide a tuning mechanism to allow for variable coupling with a Qext of 6x106 to 6x107
Rounded antenna tip
Magnitude plot of E-field at 1.5 GHz
S11 Plot
Magnitude of -46 dB at 1.498 GHz
Magnitude plot of E-field in coupler
Courtesy of Dr Emmy Sharples (HZB)
13
Notes: Un even field due to meshing of the cavity

## Slide 19
WG Tapered 60 x 88_91_95mm
TE10 - 6.25 GHz
Rbend=30mm
TE10 mode couples into different modes after bend: TE10, TE11, TM11…, depending on excitation frequency & the cutoff of each WG mode !
At high frequencies the TE10 is scattered from the bend into several modes, i.e. acts as mode mixer.
At optimized 30mm inner bending radius the reflection is minimal in broadband frequency sense.
Taper 91-95
Taper 88-91
Incident (TE10) Port,
60x88mm
60x95mm
Rbend=30mm
Reflection Broadband Behavior for TE10 Mode
Waveguide Bend Broadband Characteristics
Low reflection (broadband) from the WG bend is for bending radius = 30mm or bR ≥ 100mm.
Frequency [ GHz ]
Port modes -18

## Slide 20
Broadband RF Load Design
Load EM design is optimised for 1.5GHz system
(For most of the WG modes the reflection is bellow -15dB)
  Cooling system design
  Fabrication and Testing
1.75GHz system load design is foreseen.
HOM Load Requirements
Broadband – Multimode
Max. HOM Power 460W
15
TE10, 2.75GHz
TM12, 6.25GHz
Courtesy of J. Guo (JLAB)

## Slide 21
Setup 1: no Bellows
Setup 2: with Bellows
Wakefield Simulations
Long Range Wakes~ 20m
Spectral Weighting of all Port Signals with Beam Spectrum
Expected HOM Power Levels & Spectrum
Efficiency of HOM Damping
HOM Power Levels in SRF Module

## Slide 22
Setup 2: with Bellows
Setup 1: no Bellows
Wakefield Simulations
Long Range Wakes~ 20m
Spectral Weighting of all Port Signals with Beam Spectrum
Expected HOM Power Levels & Spectrum
Efficiency of HOM Damping
HOM Power Levels in SRF Module

## Slide 23
HOM Power Levels in SRF Module
HOM Power [ W ]
1.75 GHz Cavities
Beam pipes
18
1.5 GHz
1.5 GHz

## Slide 24
HOM Power [ W ]
1.75 GHz Cavities
Beam pipes
Bellows increases HOM power by ~28%
Corresponding spectrum is up to 5.5GHz
18
1.5 GHz
1.5 GHz
HOM Power Levels in SRF Module

## Slide 25: A COLD BEAD-PULL TEST-STAND FOR SRF CAVITIES
9-cell Tesla cavity mounted on the test-stand before the installation of the pillbox (a). Pill-box cavity mounted with the wire system inside the HobiCat cryomodule (Niobium 9-cell cavity hidden behind) (b).
Cold Test-Stand
[1] A. Vélez, A. Frahm, J. Knobloch, A. Neumann “Developments on a cold-bead-pull test stand for SRF cavities”. Proceedings of SRF2015, Whistler, BC, Canada. TUPB078.
[2] O. Kugeler, A. Neumann, W. Anders, and J. Knobloch, Review of Scientific Instruments 81, 074701 (2010).
Layout of the 9-cell Tesla cavity mounted within HoBiCaT test cryomodule [1,2].
Fundamental -mode
Courtesy of A. Velez (HZB)
1st Cold bead-pull test stand commisioned and in operation
Form factor of the bead extracted by means of a copper pillbox at 1.8 K
Experimental study of the effects created by cooldown process and tuner actuation on field profile
Sucessfully commisioned a 1.3GHz 9-cell Tesla cavity for the fundamental passband. Characteristic parameters such as R/Q can be experimentally determined.
Study of the field profile and R/Q for different HOM modes

## Slide 26
Challenges in Cavity Designs
( Off-Resonance with the Beam )
Strong HOM Waveguide Damping
HOM Power Levels & Spectrum in Single Cavities.
(Can be double by hitting single beam resonance)
Special HOM Load Design (Broadband, Multimode)
Power Ballance in Complete Modul.
  Summary

## Slide 27
Challenges in Cavity Designs
( Off-Resonance with the Beam )
Strong HOM Waveguide Damping
HOM Power Levels & Spectrum in Single Cavities.
(Can be double by hitting single beam resonance)
Special HOM Load Design (Broadband, Multimode)
Power Ballance in Complete Modul.
Study effects of undamped energy propagated throug the beam-pipes to the ring. Heating issues.
Concatenation studies . Cavity-cavity coupling, energy damping and impedances.
Sensitivity analyses on Cavity Deformations
(Fabrication Tolorances)
Thermal studies (waveguides, flanges...).
Engineering challanges & solutons.
  Summary

## Slide 28
Challenges in Cavity Designs
( Off-Resonance with the Beam )
Strong HOM Waveguide Damping
HOM Power Levels & Spectrum in Single Cavities.
(Can be double by hitting single beam resonance)
Special HOM Load Design (Broadband, Multimode)
Power Ballance in Complete Modul.
Study effects of undamped energy propagated throug the beam-pipes to the ring. Heating issues.
Concatenation studies . Cavity-cavity coupling, energy damping and impedances.
Sensitivity analyses on Cavity Deformations
(Fabrication Tolorances)
Thermal studies (waveguides, flanges...).
Engineering challanges & solutons.
And much more ongoing R&D.
  Summary

## Slide 29
Challenges in Cavity Designs
( Off-Resonance with the Beam )
Strong HOM Waveguide Damping
HOM Power Levels & Spectrum in Single Cavities.
(Can be double by hitting single beam resonance)
Special HOM Load Design (Broadband, Multimode)
Power Ballance in Complete Modul.
Study effects of undamped energy propagated throug the beam-pipes to the ring. Heating issues.
Concatenation studies . Cavity-cavity coupling, energy damping and impedances.
Sensitivity analyses on Cavity Deformations
(Fabrication Tolorances)
Thermal studies (waveguides, flanges...).
Engineering challanges & solutons.
And much more ongoing R&D.
  Summary
Thank You for Your Attention !
Let this Brilliant Light to be …

## Slide 30
Backup Slides

## Slide 31
Bunch Current [ mA ]
Bunch Train - Baseline
Bucket Number
∆f =250 MHz
Spectral weighting of port signal & Power per freq. bins (FFT)
FFT
- Simulated single bunch
Signal Spectral Weighting Technique

## Slide 32
WG Tapered 60 x 88_91_95mm
TE10 - 3.05 GHz
Rbend=50mm
Low reflection (broadband) from the WG bend is for bending radius = 30mm or bR ≥ 100mm.
Bending Radius Optimization for WG-Bend Low Reflection
Waveguide Bend Broadband Characteristics
Frequency [ GHz ]
Port modes -18

## Slide 33
BESSY VSR 1.5GHz SRF Cavity
HOM Spectrum in Waveguide Dampers

## Slide 34
Resonant Mode Extraction from Wake Potential
Kloss~2.266 KV/nC
Energy ~ 2.266µJ
Prony-Pisarenko Fit
Freq. [GHz] | Kloss [KV/nC] | Qloaded
1.5006 | 1.078 | 8.43e5
1.6561 | 0.069 | 60.2
2.4968 | 0.0025 | 63.02
2.7035 | 0.045 | 620.9
2.7613 | 0.61 | 82.3
3.0751 | 0.024 | 100.35
3.853 | 0.005 | 108.8
4.3024 | 0.729 | 3.15e3
4.3403 | 0.137 | 124.8
5.2508 | 0.025 | 173.96
5.9606 | 0.026 | 219
6.2534 | 0.0536 | 1.23e3
6.2958 | 0.0379 | 253.8
6.8204 | 0.0274 | 289.6
7.6459 | 0.0129 | 152
7.9392 | 0.0175 | 315.9
9.8534 | 0.0034 | 202.6
10.003 | 0.0131 | 400
Bunch Gauss 1nC, σ = 9mm, on axis
Simulated
Prony- Fit
s [m]
W// [ KV/nC ]
= /(2 Qloaded)
Modes with
Kloss / Kloss(1.5GHz) > 0.1%
Presented loss factors are corresponding to point charge.
Wake Potential – Long Range

## Slide 35
BESSY VSR Module
Setup 1: no Bellows
Setup 2: with Bellows